## Slide 1: Proposed detailed scope for potential RAN4 R18 items

## Slide 2: 4Tx for CPE/FWA/vehicle/industrial devices
Enable 4Tx on a single carrier for CPE/FWA/vehicle/industrial devices
  Investigate framework and architecture
  Example bands: n41, n77 and n78 (other bands to be introduced in the release independent way later from Rel-18)
    [FFS on FDD example band]
    [Note 1: the total number of example band should be limited to 3.]
    [Note 2: if FDD example band is added, study the REFSNES degradation due to 4Tx FDD operation in the example band]
    Note: FDD bands are not precluded to be introduced in the release independent way later from Rel-18.
  Specify the UE RF requirements to support 4Tx
    First priority: 4x4 UL MIMO
    Second priority: investigate and if necessary specify TXD requirement to support the same power class in UL MIMO and single antenna port
      [PA configuration assumption: 23dBm x 4, 26dBm x4]
    For UE power class (more clarification seems necessary particularly in combination with PA configuration, in terms of priority & the need to reduce the number of combinations)
      first priority: PC 1.5
      second priority: PC2 and PC3
      Note: PC1.5 is only applicable for TDD bands
  Specify the BS demodulation performance requirements to support UL 4-layer MIMO UE operation

## Slide 3: 8Rx for CPE/FWA/vehicle/industrial devices
Enable [6Rx and] 8Rx for CPE/FWA/vehicle/industrial devices
  Example bands: n41, n77 and n78 (other bands to be introduced in the release independent way later from Rel-18)
  Specify the UE RF requirements to support [6Rx and] 8Rx
  [Study the extension to 6/8 antenna SRS antenna switching]
  Specify RLM test cases with 8Rx
  Specify UE demodulation performance and CSI requirements to support [6Rx and] 8Rx
  Specify the requirements with 8 MIMO layers
  Note: FDD bands are not precluded to be introduced in the release independent way later from Rel-18.
  Note: whether or not to further consider 6Rx in this objective is to be further checked in RAN#99

## Slide 4: Lower MSD
Investigate the feasibility of and if necessary, specify lower MSD for inter-band CA/EN-DC/[DC] combinations (RAN4)
  [Example band combinations: CA_n1-n77, CA_n3-n41]
  Study how the MSD performance can be improved for example band combinations
    Study correlation of MSD improvement between different MSD resources (harmonics, IMD2/3/4/5, cross band isolation and harmonic mixing)
  [Study whether the generic approach can be applied based on UE indication of capability]
    During the study, based on the progress on the example band combinations, also check whether the generic approach can be applied based on UE indication of capability
    Aim to conclude the study phase by RAN#99

## Slide 5: UL 256QAM
Objective:
  Investigate and [if feasible], enablinge UL 256QAM for FR2 (RAN4)
    Study the gain, operating SNR, phase noise model and implementation aspects
    Specify the UE RF requirements
    Specify the BS demodulation performance
    Targeted power classes are PC1 and PC5 device types of UE are CPE/FWA [only].
Justification:
  The improved throughput and accompanying capacity increase achieved from UL 256QAM could be extremely useful for research and marketing purposes. Especially in some industry use case, e.g., the machine transmits the photograph with super high resolution to the cloud, which needs Gbps data rate. In such case, the need for 256QAM can be seen. And in such scenario thanks to lower path loss, the possibility to use 256QAM would be higher. However, the actual performance gain and implementation aspects need to be studied.
SI or WI (or WI with study phase) if approved:
  WI with study phase. To check the study phase output at RAN#99FFS option 1 or 2
    Option 1: Merged into FR2 RF enhancement WI with study phase
    Option 2: dedicated WI with study phase
Potential impact to other WG(s):
  No.

## Slide 6: Beam correspondence requirements for RRC_INACTIVE and initial access
Objective:
  [Study the need and how to specify beam correspondence requirements[/verification] for RRC_INACTIVE and initial access]
  Specify UE beam correspondence requirements for initial access and RRC_INACTIVE state, for the UE support SSB-based without UL beam sweeping [RAN4 RF]
  For RRC_INACTIVE at least [necessary] requirements for Random Access SDT and Configured Grant SDT
    It's not precluded for other transmission within RRC_INACTIVE state
    For initial access, [necessary] requirements verification of beam correspondence requirements based on msg1 spherical coverage (at least)
  Study the potential impact on testability aspects (i.e., test time).
Justification:
  UE beam correspondence functionality for RRCCONNECTED, RRCINACTIVE and initial access in IDLE is specified in the RAN1 and RAN2 specifications already in Release 15 but no FR2 UE beam correspondence requirements have been defined for RRCINACTIVE and initial access in IDLE yet. The current UE beam correspondence requirements are only defined for RRCCONNECTED. Without UE beam correspondence requirements for RRC_INACTIVE and initial access it is not possible to ensure good UE RACH and msg1 performance and UL coverage in FR2 deployments due to varying UE performances.
  Rel-15 RRCINACTIVE and Rel-17 small data transmission (SDT) have a large potential in UE power efficiency, latency and signalling overhead reduction. RRCINACTIVE allows for reduced latency and UE power saving, while SDT further enhances this for small data sessions. Considering that UE power savings are especially important for successful FR2 operations and good end-user experience, it would be important that the networks could efficiently utilize RRCINACTIVE and Small Data Transmissions for FR2 as well. Without well performing UE beam correspondence support wide usage of RRCINACTIVE and Small Data Transmission may not be feasible in practical FR2 deployments.
  To enable efficient use of RRCINACTIVE and Small Data Transmission in FR2 deployments to save UE power with reasonable latencies we see it important to develop FR2 UE beam correspondence requirements for RRCINACTIVE in Rel-18.
SI or WI (or WI with study phase) if approved:
  WI with study phase To check the study phase output at RAN#99FFS
  Merged into UE RF FR2 enhancement WI including other objectives
Potential impact to other WG(s):
  No impact to RAN1 and RAN2. Additional test cases may be defined for the RAN5 test specifications.

## Slide 7: Requirement for FR2 multi-Rx chain DL reception
Objective: (more refinement is necessary)
  Introduce necessary requirement(s) for enhanced FR2 UEs with DL reception simultaneously with different QCL TypeD RSs on single component carrier with up to 4DL MIMO
    Enhanced RF requirements:
      Specify RF requirements, mainly spherical coverage requirements, for devices with simultaneous reception with different QCL TypeD RSs
      [Note that the current requirement of 50%-ile spherical coverage is kept intact]
    Enhanced RRM requirements
      Specify RRM requirements for enhanced FR2 UEs with simultaneous DL reception with different QCL TypeD RSs on a single component carrier. At least following points can be candidates:
      Delay/timing/interpretation/scheduling restriction
    UE demodulation requirements:
      Specify UE demodulation and CSI performance requirements for enhanced FR2 UEs with simultaneous DL reception with different QCL TypeD RSs on a single component carrier
    Notes:
      For the dual-TCI case, focus on handheld UEs supporting “simultaneousReceptionDiffTypeD-r16” UE capability, and for the 2- or 4-layer downlink MIMO reception, focus on UEs supporting the basic mTRP CSI reporting capability (FG 23-7-1 of NR FeMIMO).
        stage 1: 2 layers downlink MIMO
        stage 2: 4 layers downlink MIMO
      FFS staged approach for 2 and 4 MIMO layers should be needed.
Justification:
  The existing Rel-15 NR FR2 minimum UE requirements are defined with an assumption that UE is equipped with a single antenna panel and capable to perform DL reception using a single RX beam/chain reception. Furthermore, the UE performance requirements are limited for DL MIMO rank 1 and 2. In FR2, 4-layer MIMO reception requires beam reception from at least two directions. Although this is supported by the MIMO features since Rel-15, no performance requirements have yet been specified. This is important for high-rate MIMO in FR2, as well as for FR2 HST scenarios.
  During Rel-16 and Rel-17, the support of NR FR2 CA with IBM (Independent Beam Management) and CBM (Common Beam Management) with simultaneous DL reception on different component carriers from the co-located and non-col-located TRPs was defined. The IBM concept implies a UE is capable of DL simultaneous reception on different UE panels/chains using separate beams on different component carriers and requires improved UE baseband and RF capabilities (multiple baseband chains and support of multiple antenna panels).
  Several enhancements to enable efficient and robust DL multi-TRP/panel operation were introduced in the Rel-16 NR eMIMO WI. For instance, DL transmission schemes with simultaneous and non-simultaneous multi-beam reception from multiple TRPs/panels were introduced. The simultaneous reception may require support of simultaneous multi-panel operation with several independent RX beams/chains at the UE side. As part of this item, a new FR2 UE capability for simultaneous multi-beam reception was introduced (simultaneousReceptionDiffTypeD-r16). However, no RF, RRM or performance requirements were defined in Rel-16 and Rel-17 for FR2 UEs with simultaneousReceptionDiffTypeD-r16 capability.
  Enhanced NR FR2 UEs with multi-beam simultaneous reception and multiple RX chains can provide a meaningful performance improvement in FR2 improving both demodulation performance (4-layer DL MIMO), RRM performance and improve RF spherical coverage. This work item aims to introduce the requirements for UEs capable of multi-beam/chain simultaneous DL reception on a single component carrier to achieve improved RF, RRM and UE demodulation performance.
  Different implementation scenarios could be considered at the UE. Single-TCI reception on different beams has been supported since Rel-15 via the Type I codebook, requiring coherent reception at the UE from at least two directions, which could be achieved with either a single panel or multiple coherent panels. Alternatively, dual TCI operation can work with or without the assumption of coherence at the UE, and can be combined with the Rel-17 mTRP framework even if the base station is actually deployed as a single TRP. Dual TCI operation is therefore the most flexible assumption allowing a variety of actual implementations.
  This WI therefore provides the requirements for both single and dual TCI assumptions to specify requirements for reception of 4-layer downlink MIMO with simultaneous reception at the UE from two different directions.
SI or WI (or WI with study phase) if approved:
  [Dedicated WI]
Potential impact to other WG(s):
  No
NOTE:
  Further discuss merging the core part and test methods into single WI.
  FFS “Rx antenna model supporting 4 DL MIMO layers with dual TCI” should be included in Enhanced RF requirements in the objective.

## Slide 8: RRM Enhancements
Core part objectives
FR2 RRM requirements delay reduction enhancements
  FR2 SCell activation delay reduction
    Identify cases where FR2-1 SCell activation delay can be reduced (e.g., unknown target cell cases, etc.), and specify reduced delay requirements for such cases [RAN4]
    Specify if needed, enhancement and/or signalling enhancement for the UE to meet the enhanced delay requirements [RAN4, RAN1, RAN2]
    Note: the technical solutions can be extended to FR1 and/or FR2-2, when applicable
  Note: RAN1/RAN2 work can be triggered by RAN4 LS only
Extension of requirements for existing features to new scenarios
  Define RRM requirements for FR1-FR1 NR-DC scenarios [RAN4]
    RRM requirements include the number of serving carriers, PSCell addition/release delay requirement, PSCell change and conditional PSCell change delay, scheduling availability, and CSSF. Other Rel-15 requirements are not precluded and are subject to WI stage discussion

## Slide 9: Measurement Gap Enhancements
Core part objectives
Enhancements of pre-configured MGs, multiple concurrent MGs and NCSG
  Define RRM requirements for UEs configured with a combination of pre-configured MGs, and/or multiple concurrent MGs and/or NCSG [RAN4]
    Prioritize at least joint requirements for UE configured with
      Case 1: Pre-configured MGs and multiple concurrent MGs (i.e., concurrent MGs where at least one of the gaps is a pre-configured gap)
      Case 2: NCSG and multiple concurrent MGs (i.e., concurrent MGs where at least one of the gaps is NCSG)
    Note: Prioritization among other possible combinations of pre-configured MG, concurrent MG and NCSG can be discussed in WI phase
Define RRM requirements for measurement without gaps for the following cases
  NR SSB-based inter-frequency and intra-frequency measurements without gaps for UEs reporting NeedForGapsInfoNR IE [RAN4]
    Study whether the additional interruption is allowed when UE reporting ‘NeedForGapsInfoNR'. Further define the interruption length, occasion and ratio, if the interruption is allowed
    Define related requirements, such as CSSF, measurement period, scheduling restriction etc.
  Inter-RAT measurements without gaps [RAN4]
    Inter-RAT NR measurements
    [Inter-RAT LTE measurement]

## Slide 10: Advanced receiver to cancel inter-user interference for MU-MIMO
Detailed Objective:
  Evaluate and specify advanced receiver to cancel inter-user interference for MU-MIMO
    Phase I: Study the performance gain, reference receiver assumption, testability, required signalling overhead, as well as impact on other WGs
      Further discuss reference receiver assumption with below candidates
        E-MMSE-IRC
        R-ML
      Target scenario: Focus on slot based transmission
    Phase II (if any pending on the conclusion for phase I):
      Specify PDSCH demodulation requirements under MU-MIMO scenario with advanced receiver
        Note: Performance requirements shall be specified under single reference receiver assumption
Note: To check the status of the study in RAN#100.
Note: The study on this objective assumes that the network scheduler has full flexibility to pair co-channel UEs. (this note no need to be included into WID objective).
Status: Stable enough, this objective can be included into WI

## Slide 11: ATP
Detailed Objectives:
  Specify absolute physical layer throughput requirements with link adaption
    Note: Rel-17 RAN4 study outcome is a starting point for this objective
Status: Objective stable enough, FFS for how handle this objective with two options
  Option 1: Included this objective into RAN4 performance evolution WI (majority’s preference)
  Option 2: Included into RAN5-led WI with RAN4 responsible objective
Moderator suggests to follow the majority, include this objective into Rel-18 RAN4 WI

## Slide 12: FR2-1 OTA testing for UEs with multi-panel reception and 4DL layer
Justification:
  In RAN1 Rel-17 WI on further enhancements on MIMO for NR (Acronym: NR_FeMIMO), the objective is to extend the specification to support several aspects on NR MIMO including multi-panel UEs which also has RAN4 impact. With RAN4 considering an objective to define requirements for UEs with multi-panel reception and up to 4DL layers for FR2-1, the FR2 test methodologies for RF, RRM, and demodulation need to be enhanced to support the verification of these new requirements, together with a preliminary assessment of the related uncertainties.
Detailed objective:
  Define a test methodology for RF/RRM/Demodulation requirements testing for devices that can receive/transmit simultaneously from multiple AoAs
    The multiple AoA test setup should enable testing of up to 2 DL Layers with dual polarization for each angle
    For RRM, the target should be 4 angles with 2 angles used simultaneously
  Define a test methodology for up to 4 DL MIMO layer demodulation testing
  Smartphone form factor should be the first priority, other UE types should also be discussed as 2nd priority
  Develop the related preliminary uncertainty assessments for the test methodologies
  Rel-15 and Rel-17 FR2 test methods should be used as the baseline. As such, the conclusions and agreements in TR 38.810 and TR 38.884 should be taken into account.
  The tests shall take the test system reuse, test system complexity and test time into account to keep the whole test costs within a reasonable level.
SI/WI: Include as part of dedicated Rel-18 FR2 OTA testing enhancements SI
Potential Impact to Other WGs: None
Status: Moderator recommends to include this topic/area into Rel-18 SI for approval at RAN#95e

## Slide 13: EMC enhancement
Justification and Detailed Objectives:
  Justification and Detailed Objectives will use the justification and scope in the draft WID in RP-211825 as a baseline with the corrections identified in the initial round and suggested updates to E-UTRA UEs and the timeline identified during the intermediate round
  Additional item added to Phase 1 objectives as follows in brackets to allow for further discussion at RAN#95e.
    [4. Study the possibility to draft a single EMC specification for network nodes (BS, Repeaters, IAB, etc.; all RATs) to replace multiple legacy EMC specs.]
SI/WI: Dedicated WI
Potential Impact to Other WGs: None
Status:
  Justification and Detailed Objectives stable with exception of proposed study below
  Needs minimal discussion at RAN#95e concerning a proposal to add a study of the possibility to draft a single EMC specification for network nodes
  Moderator recommends to include this topic/area as Rel-18 WI for approval at RAN#95e

## Slide 14: Simplification of band combination specification
Recommended Objectives: (New SID: Simplification of band combination specification)
  Investigate and simplify the working procedure for approving documents for TS and TR to improve the efficiency to specify band combinations and the quality of specifications
    Improve the efficiency considering
      RAN4 reduces the redundant and unnecessary work for big CRs, draft CRs and/or TPs, if any
      The following rules will be investigated and defined if necessary
        Investigate whether the workflow can be improved under the condition that quality can be guaranteed.
        Develop rules or guidelines covering the process of not for block approval.
      Develop the necessary tools to reduce RAN4’s workloads if feasible
    Improve the quality considering
      RAN4 improves the procedures for cross-checking to avoid conflict between big CR/CRs across basket WIs and other WIs
    RAN4 captures the agreements about the rules and guidelines including but not being limited to the outcome of the above sub-bullets in the corresponding TR
  Investigate the feasibility and optimize the specification structure and reduce the test burden
    Study the methodology to simplify the test efforts for a UE supporting multiple features, e.g., NR-CA, EN-DC on the same band combination
      Study of similarity and dependency of RF requirements for different features on the same band combination
    Study the methodology to simplify RF requirement specifications for
      MSD requirements in 38.101-1 and 38.101-3, e.g., reducing the test configurations with different bandwidth combinations
      For Delta_TIB and Delta_RIB requirements, investigate and define the framework of the general principle or requirements with band-combination specific exceptions
      For Delta_TC,c, investigate whether it can be removed in low boundary formula for Pcmax
  NOTE 1: The requirements applicable to UE won’t be increased.
  NOTE 2: The work should be applied to all the power classes
Other tentative agreement:
  The consolidation/re-alignment for Rel-18 basket WI will be discussed before the Rel-18 basket WIs are approved.

## Slide 15: Enhancement for 700/800/900MHz band combinations
Recommended Objectives: (New SID: Enhancement for 700/800/900MHz band combinations)
  Investigate the feasibility and solutions to enable simultaneous transmission on two UL bands and simultaneous reception on two or three bands for the band combination of 700, 800 and 900MHz spectrum for smart phone form factor
    The following band combinations will be considered. And the technical discussion on three band combination will start after the completion of feasibility study of all the fallback band combinations.
      CA_n8-n20-n28 with uplink configurations of CA_n8-n20, CA_n8-n28, CA_n20-n28, and the fallback modes
      [CA_n5-n8-n28 with uplink configurations of CA_n5-n8, CA_n5-n28, CA_n8-n28, and the fall back modes]
      [CA_n5-n8 with uplink configurations of CA_n5-n8, and the fallback modes]
      CA_n20-n67 with uplink on band n20
    The following aspects need be studied
      UE architecture including n-plexing, PA
      Study feasibility of low band wideband antenna
      Performance due to impacts including inter-modulation products
      Method to manage the inter-modulation product impacts
    Power class 3 (PC3) is considered in this study
  Identify necessary RAN4 requirements including Tx and Rx RF requirements
Issues which need further discussions in the objectives
  Should CA_n5-n8-n28 with uplink configurations and CA_n5-n8 be included as the example band combinations given that the downlink of band n5 overlaps with uplink of band n8?
Additional tentative agreement:
  A nine months duration for the SI, with a potential follow-up WI to be discussed depending on the outcome of the SI. should be agreed followed by a Rel-18 WI, if the outcome of the study demonstrates the feasibility.

## Slide 16: BS RF requirement evolution
Recommended Objectives: (New WID: NR BS RF requirement evolution for NR)
  mmWave multi-band BS
    Example bands: 26+28GHz, 28+39GHz, 26+40GHz, 28+40GHz
      Target at studying and defining the generic requirements
    Phase I: Study phase (12 months)
      Investigate the feasibility and performance of wideband RF and antenna architectures covering multiple FR2 bands
      Investigate if FR1 multi-band methods are re-usable for FR2, and (if so) agree on the appropriate inter-RF BW gaps
      Investigate if FR1 exceptions are acceptable for FR2
      Investigate whether a generic solution for all combinations within FR2-1 is possible and/or a solution for all or a part of the 24-29GHz frequency range in which n257/n258/n261 overlap should be targeted
      Study the definition of FR2 multi-band BS
    Phase II: normative work depending on the conclusion of phase I
      Core part:
        Specify the definition of multi-band for FR2, if needed
        Specify RF core requirements for FR2 multi-band BS, if deemed feasible
          Define RF core requirements to include FR2 multi-band BS
            Dependent on the study phase outcome, this may be all or part of FR2 bands
          Define EMC requirements
      Perf part:
        Specify the BS conformance test requirements, if needed
      NOTE 1: The requirements for mmWave multi-band BS are to be defined for the synchronized operating bands.
      NOTE 2: No change is needed for 37 series specification since FR2 is not included in MSR AAS BS specifications.
    A potential follow-up WI is to be discussed depending on the outcome of the SI

## Slide 17: ATG
Recommended Objectives: (New WID: Air-to-ground network for NR)
  Specify features to core specifications of RF requirements for coexistence between ATG and IMT terrestrial network [RAN4]
    Scenario: [To further clarify the scenario & the assumptions]
      BS on the ground, and the CPE type of UE mounted in the aircraft
      A direct radio link between BS on the ground and CPE type of UE mounted in the aircraft
    Core part: Specify core requirements for coexistence between ATG and IMT terrestrial network [RAN4]
      Example bands include n1, n78 and n79.
      Perform FR1 co-existence evaluation for ATG network (e.g. ACLR, ACS)
      Identify key characteristics where it is necessary to differentiate ATG ground-based BS and UEs from conventional ground based BS and UEs
        Aim to reuse existing requirements for BS and UE where possible, e.g.,
          Reuse TN BS requirements for ATG BS
      Specify RF requirements for ATG UE/BS
        Considering the results of co-existence simulations in terms of impact on emissions and RX requirements, cell sizes and link budgets, technology capabilities, likely BS and UE architectures and other relevant aspects.
        Taking into account identified differences between ATG and fully ground based systems
        Consider BS type 1-C/1-H/1-O and specify the requirements
        Consider conductive requirements for UE
      Specify RRM core requirements for ATG UE
        Taking into account identified differences between ATG and fully ground based systems
        Considering the different nature of ATG UEs and their view of the network, increased cell sizes and other relevant aspects
      Specify new UE/BS type(s) for ATG network if necessary
    Perf part: Identify and specify RRM/demodulation performance requirements for ATG. [RAN4]
      Identify key performance requirements where it is necessary to differentiate ATG BS and UEs from conventional ground based BS and ground-based UEs
        Aim to reuse existing requirements for BS and UE where possible, e.g.,
          Reuse TN BS requirements for ATG BS
      Specify test procedures for ATG BS conformance testing
      RRM performance requirements and test cases for ATG UE. [RAN4]
      Demodulation performance requirements for ATG UE/BS. [RAN4]

## Slide 18: Support of intra-band non-collocated EN-DC/NR-CA deployment
Recommended Objectives: (New WID: Support of intra-band non-collocated EN-DC/NR-CA deployment)
  Phase I:
    Study the feasibility to support non-co-located scenario for FR1 intra-band non-contiguous EN-DC/NR-CA
      Investigate the tolerable power imbalance between carriers
      Investigate the required arrival time difference between CCs
      Evaluate the UE performance under the power imbalance and arrival time difference
        Discuss and decide reference UE architecture considering the UE capability of interBandMRDC-WithOverlapDL-Bands-r16
      [Study the feasibility for support of 4Rx chains with up to 4-layer MIMO
        Study if the 4Rx chains with supporting up to 4-layer per CC can be supported for the intra-band non-contiguous non-collocated scenario
        If not, study if the Rx chain number supported per CC is allowed to be reduced from 4 to 2.]
      Work is limited to CA/EN-DC for EN-DC/NR-CA for bands 42, n77/n78
  Phase II:
    Phase II work will get started after the feasibility in phase I is confirmed
    Core part:
      Specify the power imbalance
      Specify MRTD and MTTD requirements in non-collocated deployment
      Discuss and decide if the different requirements will be specified based on UE capability of interBandMRDC-WIthOverlapDL-Bands-r16.
    Perf part:
      Specify PDSCH demodulation requirements for non-collocated scenarios for intra-band non-contiguous EN-DC and NR-CA
        Define PDSCH demodulation performance requirement based on the applicable MRTD and power imbalance values.
        Power imbalance between the carriers is limited
    NOTE: Power imbalance may be specified as the condition in the demodulation performance requirements
Issue which needs further discussions in the objectives:
  The objective in [ ] for the feasibility study for support of 4Rx chains with up to 4-layer MIMO.

## Slide 19: FR2 HST enhancement
Recommended Objectives: (New WID: Enhanced NR support for high speed train scenario in frequency range 2 (FR2))
  Core part:
    Only train roof-mounted high power devices with target applicable carrier frequency up to 30GHz are considered in this WI
    Specify the RF requirements for intra-band carrier aggregation (CA) scenario, and investigate and specify the RRM requirements for intra-band carrier aggregation (CA) scenario
    Specify the requirement for simultaneous multi-panel operation for train roof-mounted FR2 high power devices [RAN4]:
      Maximum 2 active panels supporting the multi-panel simultaneous reception.
      NOTE: Focus on FR2 HST specific requirements, and avoid the overlap with the scope of FR2 multi-Rx DL reception
    [Study the feasibility, and if feasible enable supporting HST velocity of up to a maximum of 500km/h, with carrier frequency up to 30GHz]
    Study on reference tunnel deployment scenario for FR2 HST and specify the channel model and corresponding core requirements if any
    FFS other core requirements considering the following potential objectives for the corresponding scenarios below
      Specify the requirements to support the scenario with mixed near-to-track (i.e., Scenario-A with Ds = 700m and Dmin = 10m) and far-from-track (i.e., Scenario-B with Ds = 700m and Dmin = 150m) RRH deployment
      Specify the new uplink timing adjustment mechanism for FR2 HST scenario with large propagation delays from different TRPs to UE
  Perf part:
    Specify the RRM test cases, and investigate and if needed specify the demodulation performance requirements for intra-band carrier aggregation (CA) HST scenario.
    Specify the necessary demodulation performance requirements for simultaneous multi-panel reception.
      NOTE: Focus on FR2 HST specific requirements, and avoid the overlap with the scope of FR2 multi-Rx DL reception
    Specify the other necessary RRM and demodulation performance requirements depending on the outcome of core part.