## Slide 1: Outline of left issues of [95e-31-R17-RedCap-WI]
Source: Moderator(RAN1 VC, CMCC)
RP-220891
3GPP TSG RAN#95-e
17th – 23rd, March 2022
Agenda Item: 9.5.1.7

## Slide 2: Possible Agreement 3(Background of left Issues – left Issue 2)
Left Issue 2 – UE feature
Features | Index | Feature group | Components | Type (the ‘type’ definition from UE features should be based on the granularity of 1) Per UE or 2) Per Band or 3) Per BC or 4) Per FS or 5) Per FSPC)
28. NR_redcap | 28-1 | RedCap UE | 1. Maximum FR1 RedCap UE bandwidth is 20 MHz. 2. Maximum FR2 RedCap UE bandwidth is 100 MHz. 3. Early indication of RedCap UE in Msg.1 for 4-step RACH 4. Separate initial UL BWP for RedCap UEs - It includes the configuration(s) needed for RedCap UE to perform random access - Enabling/disabling of frequency hopping for common PUCCH resources 5. Separate initial DL BWP for RedCap UEs - It includes CSS/CORESET for random access - FFS: For separate initial DL BWP used for paging, CD-SSB is included - For separate initial DL BWP only used for RACH, SSB may or may not be included FFS whether to add any other basic features for RedCap UE | [Per UE]
28. NR_redcap | 28-3 | Half-duplex FDD operation type A for RedCap UE | 1. Half-duplex FDD operation (instead of full-duplex FDD operation) type A for RedCap UE | [Per band]

## Slide 3: Possible Agreement 3
FG 28-1 is reported per UE, and FG 28-3 is reported per band
For discussion reference: Justification for reporting FG 28-1 “Per band”
In FR1 below 2.5 GHz, there are FDD and TDD bandswith CBW no more than 20 MHz and requiring a R15/16 eMBB UE to have a minimum of 2 RX branches
On these bands, a “high-end” Rel-17 RedCap device supporting the envelope of radio and upper layer capabilities (2 RX, FD-FDD, 256 QAM, and etc.) will behave the same way as a Rel-15/16 eMBB UE, without using capabilities not intended for RedCap UE
  Such high- end p RedCap UEs can access the legacy cells supporting R15/16 eMBB UE without requesting NW to upgrade its HW/SW
Benefits of “Per Band” Reporting for FG 28-1
  Improve deployment flexibility of Rel-15/16/17 NR UE
  Reduce cost/latency to roll-out Rel-17 RedCap UE
  Better co-existence with legacy NR UEs without causing market fragmentation
  Simplify IODT testing and avoid negative interaction with UE testing on NTN and unlicensed spectrum
  No need for xDD and FR differentiation
  Compliant with WID requirements and previous agreements in Plenary/WGs
  “Per band” reporting will NOT violate the restrictions on R17 p RedCap UE, including CA, DC, wider CBW, more than 2 Rx branches, and etc.
The mandatory restrictions imposed on p RedCap UEs will prevent a non-RedCap UE (supporting CA/DC/wider CBW/more than 2 Rx branches/advanced upper layer functionalities) to declare itself as “RedCap UE”

## Slide 4: Possible Agreement 5 (Background of left Issues – left Issue 5)
Left Issue 5 - CR for operating bands
  RP-220462, company CR to TS 38.101-1, proposes to implement a new operating band section for Redcap UE
Initial round discussion
  Questions “Approve the CR in RP-220462? Yes/No”
  In the 13 companies attending the discussion, 7 companies think this CR is not needed, 4 companies support this CR, 1 company is fine with the CR, but note that it is premature to approve the CR, 1 one company think it redundant but helpful, additionally, two of the proponent companies think this CR should not be discussed anymore if it is not approved in RAN#95.
Second round discussion
  Question “It is not pursued to approve the CR in RP-220462.”
  It is observed that some companies think it necessary for RedCap UE, some companies think otherwise, and some other companies think it is fine to without this band list even they prefer, at least from moderator's observation, approving this CR is not the only way to support RedCap, just try to confirm or deny the observation/understanding in the final round
Final round discussion
  Question “Can RedCap UE be supported without approving CR in RP-220462？”
  7 of the 9 companies confirm that RedCap UE can be supported without approving this CR, 1 company comments that this CR can be helpful for improving clarity, but without the CR, the specification is not broken, 1 company strong prefer approving this CR from standard effort and specification implementation. In addition, some companies prefer to continue to discuss it in RAN4, while some companies comment it does not make more sense to repeat this discussion and it should be concluded in this meeting

## Slide 5: Possible Agreement 5
It is not pursued to approve the CR in RP-220462 in Rel-17.

## Slide 6: Offline Agreement 2
Confirm all the tasks of RAN4 except "Agree RedCap operating band list in FR1 and add the operating band clause" in RP-220292
  Whether to keep "Agree RedCap operating band list in FR1 and add the operating band clause" in the final exception sheet is decided by the outcome of Issue 5.
The performance part Rel-17 RedCap WI target completion date is extended to 6 months after the core part target completion date, and is allocated the relevant meetings of the TU allocation requested in the SR (see Table in RP-220135, excerpted as below).
 | RAN4#103 | RAN#96 | RAN4#104 | RAN#97 | RAN4#104bis | RAN4#105 | RAN#98
R4RD | 0.75 | Jun. 2022 | 1 | Sept. 2022 | 0.75 | 0.5 | Dec. 2022

## Slide 7: Wrap up
Note RP-220964, final SR
  Reflecting conclusions/agreements achieved in [95e-31-R17-RedCap-WI]
Approve RP-220965, exception sheet
  Including RAN4 tasks only, reflecting conclusions/agreements achieved in [95e-31-R17-RedCap-WI]
Approve RP-220966, update of WID
  Reflecting conclusions/agreements achieved in [95e-31-R17-RedCap-WI]