## Slide 1: 3GPP TSG RAN Meeting #76 West Palm Beach, Florida, June 5-8, 2017 Agenda item: 10.1.1 Document for: Discussion
Considerations on evolution of NB-IoT/eMTC
RP-171045

## Slide 2: IoT : Roadmap in 3GPP
Rel-13 eMTC
1.4 MHz bandwidth
One deployment scenario: in-band
Max data rate(FD-FDD):
~800 kbps/~1 Mbps
Coverage enhancement: 155.7dB
Rel-14 eMTC
Up to 5 MHz bandwidth BL UE
Large TBS support
Max data rate(FD-FDD):
      ~1 Mbps/~3 MHz for 1.4 MHz
      ~4 Mbps/ ~7 MHz for 5 MHz
Positioning : OTDOA
Multicast support
VoLTE enhancement
Rel-13 NB-IoT
180 kHz bandwidth
Three deployment scenarios: In-band, guard-band, standalone
Max data rate(anchor, inband):
~22.6 kbps/ ~58.3 kbps
Coverage enhancement: 164 dB
Rel-14 NB-IoT
Positioning : OTDOA
Multicast support
Non-Anchor PRB support
New power class
Max data rate((anchor, inband):
~65.1 kbps/~142.5 kbps
Rel-13
Low complexity
Low power
Enhanced coverage
Rel-14
Use-case extension

## Slide 3: Characteristics of Current IoT applications
NB-IoT and eMTC can be used for different market segments:
    eMTC is suitable for applications with medium and high throughput, mobility and low latency requirements
    NB-IoT is suitable for applications with large scale coverage, low device cost and high system capacity requirements
eMTC
NB-IoT
155dB
164dB
~10 years
~10 years
Half duplex<375Kbps
Full duplex<1Mbp
<70Kbps
<350km/h
<30km/h
~$10/module
100k@5MHz
50k@200KHz
<$5/module
<700ms
10S
Uplink data rate
Coverage
UE battery life
Mobility
Latency
Device cost
Capacity
Voice
Support
Use cases | Data volume | Mobility | Latency requirements | Voice needed | Suitable Tech.
Smart meters | low | No | low | No | NB-IoT
Smart parking | low | No | low | No | NB-IoT
Wearable devices | low | high | high | Yes | eMTC
Tele matics | Medium | high | high | Yes | eMTC
N/A

## Slide 4: Further IoT evolution in Rel-15
eMTC
  General enhancement: Power consumption ,latency, system acquisition time, load control
  Spectrum efficiency enhancement
  Support of higher UE velocity
NB-IoT
  General enhancement: Power consumption ,latency, system acquisition time, load control
  New use cases support: TDD , small cell ,stand-alone operation mode support
  Measurement accuracy enhancement
Observation:
Convergence the enhanced features in some use cases and deployment scenarios

## Slide 5: Evolution of NB-IoT/eMTC
It’s natural to consider independent evolution for NB-IoT/eMTC in future releases
  For eMTC, the desired improvements may be for more flexibly resource utilization to support more variable IoT applications.
  For NB-IoT, the desired improvements may be still focus on lower power consumption/device cost and super large coverage.
  Some suitable technologies still can be used in both NB-IoT and eMTC
    Such features may be transparent to higher layer in order to avoid switching between different modes
    E.g., wake-up-signal (WUS)
  Differentiation between NB-IoT and eMTC should be kept since they target different deployment scenarios

## Slide 6: Evolution of NB-IoT/eMTC to mMTC
It’s important to consider of final evolution for NB-IoT/eMTC to mMTC in future releases
  Features specific for IoT deployment scenario and IoT application should be prioritized
    E.g. Positioning improvement , power consumption reduction
  Features benefits both technologies should be introduced together to simplify standardization work
    At the same time, there is no need to duplicate everything aspects of individual technology without justification of specifically targeted scenario
    Detailed design should still be optimized current frame of each technology and deployment scenario.

## Slide 7: Evolution of NB-IoT/eMTC to mMTC
  Further study is required
    KPI targets that can satisfy diverse IoT application requirement
  KPIs currently considered:
  The target for coverage, i.e. MaxCL in uplink and downlink between device and Base Station site (antenna connector(s)) for a data rate of 160bps, should be 164dB
  The target for UE battery life for mMTC : beyond 10 years, 15 years is desirable
  The target for connection density : at least 1 000 000 device/km2 in urban environment
  The target for latency : at most 10 seconds latency requirement for uplink exception report

## Slide 8: Proposals
In Rel-15, enhancement should focus on be enhancement of specific aspects of individual technology
  Support of both eMTC and NB-IoT mode and switching between two air interface should be based UE implementation.
    No specification optimization for dual mode operation in Rel-15
For any future release, enhancement shall consider convergence to the final evolution path
  General enhancement should be adopted for both technologies with minor variations
  Differentiations targeting specific use case of each technology should be kept

## Slide 9: Thank you