## Slide 1: Supporting 2Tx UE and Single UL Transmission in NR
RAN#77, SAPPORO, SEPTEMBER 11-14 2017
AI 9.2.1
AT&T

## Slide 2: Motivation
Dual connectivity between LTE and NR is a key feature used by the Option 3X NSA architecture. This requires separate UL transmission on the MCG and SCG to deliver the UCI independently to each one of them.
    UL PUCCH on SCG and MCG delivers the HARQ ACK/NACK, CSI measurements
    UL PUSCH on SCG and MCG allows for the UL bearer to be split.
In some band combinations such as NR on 3.5GHz and LTE on 2GHz there is potential issue of supporting simultaneous UL on both bands due to inter-mod between these two bands.
    Even for these band combinations the problem only happens when the transmit power in both or one of these bands is high. When the transmit power in both of these bands is low then the problem is mitigated significantly and it is possible to sustain simultaneous UL transmission on both the bands
This contribution highlights potential techniques and their pros and cons for addressing this issue.

## Slide 3: Option 1: Single RF Chain with Dual Baseband
UE is equipped with only 1 Tx chain.
In order to transmit UL PUCCH on both F1 and F2 the RF chain toggles between the two frequencies.
Peak Data Rate Impact:
    NR allows for HARQ ACK/NACK bundling therefore ACK/NACK from all the 8 HARQ processes can be bundled over the 4 PUCCH slots in UL. No NR peak data rate impact
    LTE does not allow for HARQ ACK/NACK bundling (FDD), therefore ACK/NACK all the 8 HARQ processes CANNOT be bundled over 4 PUCCH slots in UL and ONLY 4 HARQ processes are usable. Peak data rate on LTE reduced by 50%.
Timing Advance Impact:
    Since the Tx chain toggles between the two frequencies the UL transmission on the two frequencies (LTE and NR) cannot have different timing advance since that would require overlapped transmission on two frequencies which is NOT possible with a single Tx chain. This could be a potential issue in a deployment where LTE and NR are delivered by two different layers (e.g. LTE on macro and NR on pico) where the system may require different timing advance on the two frequencies
TA1
TA2

## Slide 4: Option 2: Dual RF Chain with Dual Baseband
TA1
TA2
UE is equipped with only 2 Tx chain.
In scenarios where there is MSD degradation due to IMD issues the network can schedule the UL transmission on LTE and NR by TDM. This can be handled in implementation
In scenarios where there is NO MSD degradation such as no IMD or both Tx chains operating at low power the network can schedule the UL transmission on LTE and NR simultaneously.
No Peak Data Rate Impact:
No Timing Advance Impact:
    Since both the Tx chains operate independently it is possible to have independent timing advanced on the UL transmission on the two frequencies (LTE and NR) cannot have different timing advance since overlapped transmission on two frequencies is possible. This implies that this solution can support ALL deployment scenarios including where LTE and NR are delivered by two different layers (e.g. LTE on macro and NR on pico)

## Slide 5: Proposal
Based on these observations we make the following proposals:
Proposal 1: Make 2 UL Tx as the baseline for dual connectivity between LTE and NR
Proposal 2: Define RRC Signaling to allow the network the configure the device to transmit on 1 UL frequency at a time.
      The UE still uses two UL Tx but is allowed to transmit on only 1 frequency at a time.
      RRC Signaling is required to allow the UE to know that it is expected to transmit on 1 frequency at any given instance and therefore determine the conflict resolution in the event of a scheduling collision on both the frequencies.