## Slide 1: Motivation for Multi Hop Relay for IoT & MTC for utilities use cases for LTE (New WID proposal: RP-171882)
3GPP TSG RAN Meeting #77
Sapporo, Japan, September 11 - 14, 2017
Agenda item: 10.1.2
RP-171900
Veolia

## Slide 2: Background
When deploying IoT metering solutions, utilities (gas, water, electricity…) are faced with the critical issue of Network ”black spots”.
  Some meters are very deep indoor and their coverage could not be assured by the network provider.
  Devices in this case are at the edge of a cell and are likely not to be able to reach the eNB in a single hop.
  They will need to increase drastically their battery consumption by emitting at full power.
In some city, it could represent more than 5 % of the UEs deployed.
In already existing deployed LPWA technologies (Non-3GPP), repeaters are successfully used to cope with this issue.
It is therefore paramount for 3GPP to address this issue as well as part of the Release 15 scope to reinforce NB-IoT (and LTE-M) position among LPWA protocols.
A solution is to define multi-hop relay nodes able to become relays for other devices and to act as small cell for the UE at the edge and as an UE for the eNB.

## Slide 3: Justification/Key benefits
Better power consumptions profiles for devices on the edge of the cell / black spots (increased throughput and/or power consumption reduction).
Less infrastructure cost (instead of increasing coverage).
Facilitate deployment (deployment done in conjunction with the customer deployment).
Reserved to particular use cases/closed user groups (utilities - for security and activation by provisioning).
Functionality of relaying of other customer’s UEs member of the user group will be essential.
Functionality for new UE Relay to advertise its capability and its “power consumption profile” (directly or through the network) and for the UE to detect and use appropriate UE relay will be beneficial.
The multi-hop relay is an edge networking enabler.
With Multi-Hop relay approach, some of the UEs deployed by the utilities and end user customers are helping to increase the operator coverage while providing a complete solution for the utilities.

## Slide 4: Objectives of the new WID
To create new WID to address this topic: RP-171882
WG impacted: RAN 2, RAN 1, RAN 4, RAN3
Main objectives:
  Evaluate the appropriate solution to assume Multi-hop relay considering ProSe D2D (results of SI “Further Enhancements to LTE Device to Device, UE to Network Relays for IoT and Wearables”) or other mean such as introducing L3 relay node having RRC layer and lower, acting as a small cell to the next hop and a UE to the previous hop, and has no support of S1 and X2 interfaces.
  Evaluate security aspects including
    UE/Relay identification
    Support for closed subscriber group (CSG) functionality (for utilities only)
  Support of functionality for Relay nodes and eNB to differentiate between a normal UE and a relay mode.
  Support of functionality for new UE Relay to advertise its capability and its “coverage” (directly or through the network - to be defined) and for the UE to detect and use appropriate UE relay (still with minimal impacts on power consumption).