## Slide 1: Way forward on LTE UDC
Acer, ASTRI, AsusTek, Broadcom, CATT, CATR, China Mobile, China Unicom, CHTTL, CoolPad, HTC, Huawei, HiSilicon, H3C, III, Intel, ITRI, MediaTek, Potevio, Qihoo 360, Samsung, SK Telecom, Spreadtrum, Verizon, Xiaomi
3GPP TSG RAN#77 11-14 September 2017 Sapporo, Japan | TDoc RP-172033 Agenda Item 10.1.2 Revision of RP-171922

## Slide 2: Background and Status [1/3]
RAN#76
  The TR was approved but the SI is extended until September. RAN agreed that additional information on the APDC solution is to be provided to RAN2 by 2017-06-26. At the next RAN2 meeting, we will analyse this additional information and update the TR via CRs. RAN#77 will make a decision between DEFLATE based solution and APDC solution (unless RAN2 is able to make a quick and easy decision). 1 TU is allocated for this activity in RAN2#99. (See SR in RP-171464)

## Slide 3: Background and Status [2/3]
RAN2#99
  RAN2  99#14: [R2-1709921] CR36.754 simulation results of APDC
    No objection received by the deadline
    Results from (R2-1708296, R2-1708383, R2-1708572, R2-1709041, R2-1708360) for 8KB and 16KB buffer sizes
    Indicates APDC compression efficiency being function of compression buffer size
    Clarify the buffer size issue of APDC (32KB buffer not supported)
    Update conclusion section based on the results.
  R2-1708357 Clean-up of the TR 36.754 (agreed)
  R2-1709742 Update of Description and Evaluation Results for DEFLATE (agreed)
“Both solutions based on DEFLATE and APDC are candidates for a UL data compression solution. However RAN2 recommends only one solution to be selected for specification in a potential Work Item (WI).”
RAN#77 decision on a single algorithm 

## Slide 4: Background and Status [3/3]
 |  |  | DEFLATE Static Huffman 1byte UDC header |  | APDC 26Jun |  | RoHC Available
Input |  |  | 8KB | 32KB | 8KB | 16KB | 
#1 | FTP- Client (CMCC) |  | 49.96% | 49.96% | 54.34% | 54.34% | 73.3%
#2 | FTP- Server (CMCC) |  | 44.61% | 44.61% | 50.34% | 50.34% | 59.7%
#3 | Online video (CMCC) |  | 62.98% | 62.99% | 61.00% | 61.04% | 5.4%
#4 | Long period video (CMCC) |  | 71.26% | 73.75% | 76.67% | 78.13% | 5.1%
#5 | SIP UE1(CMCC) |  | 86.50% | 87.95% | 83.91% | 85.18% | 4.4%
#6 | SIP UE2 (CMCC) |  | 83.79% | 84.87% | 80.62% | 81.78% | 21.7%
#7 | SIP UE3 (CMCC) |  | 86.85% | 88.25% | 84.20% | 85.67% | 23.1%
#8 | Web surfing (CMCC) |  | 65.20% | 70.03% | 64.24% | 66.87% | 45.1%
#9 | Video data (MediaTek) |  | 59.08% | 57.92% | 73.47% | 73.9% | 80.7%
#10 | Long duration FTP (MediaTek) |  | 62.01% | 58.56% | 75.34% | 75.30% | 83.4%
#11 | Multiple IP flows (Qualcomm) |  | 71.63% | 73.79% | 73.35% | 74.68% | N/A
 |  |  |  |  | NOTE: 32KB not supported |  | 

## Slide 5: Summary
Performance(1) | Complexity | Readiness | IODT | 3GPP compliance
DEFLATE = APDC | DEFLATE = APDC | DEFLATE > APDC | DEFLATE > APDC | DEFLATE = APDC
TR36.754: Solution based on DEFLATE and solution based on APDC have shown significant and similar compression efficiency. DEFLATE efficiency better with SIP than APDC – VoLTE capacity gains expected DEFLATE and RoHC outperform APDC | DEFLATE can be used in low-end platforms No advantage with APDC | DEFLATE ready: RFC1951(2) in public domain DEFLATE is widely used in the two most popular mobile platforms today APDC is not specified | DEFLATE known (RFC1951) and widely used today DEFLATE IODT will be expedited | Network upgrade required (RRC, PDCP) regardless whether DEFLATE or APDC is used
NOTE 1: compression efficiency |  | NOTE 2: published in May 1996 |  | 

## Slide 6: Way forward on LTE UDC
RAN#77 to adopt the DEFLATE-based solution as the only new compression algorithm for LTE UDC
Corresponding WI in RP-172023

## Slide 7: Appendix – TR36.754 results
 |  | DEFLATE Static Huffman 1byte UDC hdr. |  | DEFLATE Adap. Huffman no 1byte UDC hdr |  | DEFLATE Adap. Huffman 1byte UDC hdr |  | APDC 26Jun |  | RoHC
Input |  | 8KB | 32KB | 8KB | 32KB | 8KB | 32KB | 8KB | 16KB | 
#1 | FTP- Client (CMCC) | 49.96% | 49.96% | 51.69% | 51.69% | 49.96% | 49.96% | 54.34% | 54.34% | 73.3%
#2 | FTP- Server (CMCC) | 44.61% | 44.61% | 46.02% | 46.02% | 44.61% | 44.61% | 50.34% | 50.34% | 59.7%
#3 | Online video (CMCC) | 62.98% | 62.99% | 65.56% | 65.55% | 64.93% | 64.92% | 61.00% | 61.04% | 5.4%
#4 | Long period video (CMCC) | 71.26% | 73.75% | 73.37% | 75.47% | 71.93% | 73.97% | 76.67% | 78.13% | 5.1%
#5 | SIP UE1(CMCC) | 86.50% | 87.95% | 86.99% | 88.25% | 86.87% | 88.13% | 83.91% | 85.18% | 4.4%
#6 | SIP UE2 (CMCC) | 83.79% | 84.87% | 84.94% | 85.34% | 84.83% | 85.23% | 80.62% | 81.78% | 21.7%
#7 | SIP UE3 (CMCC) | 86.85% | 88.25% | 87.31% | 88.62% | 87.20% | 88.52% | 84.20% | 85.67% | 23.1%
#8 | Web surfing (CMCC) | 65.20% | 70.03% | 66.99% | 71.04% | 66.22% | 70.28% | 64.24% | 66.87% | 45.1%
#9 | Video data (MediaTek) | 59.08% | 57.92% | 61.26% | 59.92% | 59.41% | 58.07% | 73.47% | 73.9% | 80.7%
#10 | Long duration FTP (MediaTek) | 62.01% | 58.56% | 63.91% | 60.46% | 62.01% | 58.56% | 75.34% | 75.30% | 83.4%
#11 | Multiple IP flows (Qualcomm) | 71.63% | 73.79% | 73.03% | 74.87% | 72.08% | 73.92% | 73.35% | 74.68% | N/A
 |  |  |  |  |  |  |  | NOTE: 32KB not supported |  |