## Slide 1: Signalling for Single/Dual UL Tx (current status)
RAN2 Chairman (Intel)

## Slide 2: UE capability signalling
  Define in RAN4 specs for which band combinations and channel allocations within that band combination the UE is allowed to indicate that it does not support 2 simultaneous UL tx (this is not implying the granularity of the signalling)
Signalling to be defined to support the 'red text' from RAN4 part of the single tx discussion (i.e. as in RP-172064):
  UE capability indicates that the UE does not support 2 simultaneous UL transmission for [the RAN4 specified channel allocations in] a given band combination. If the UE indicates that it does not support 2 simultaneous UL transmission then network must respect this capability when configuring/scheduling the UE.

## Slide 3: Dynamic signalling mechanism
UE request indicating a preference for single UL transmission can be transmitted. UE can trigger request based on current configuration, current radio conditions, etc. The network can decide whether or not to respect the request when configuring/scheduling the UE (network decision can change based on, for example, current radio conditions, etc) [This has similarities to current IDC mechanism].
  FFS Whether UE need to be explicitly informed of the network's decision.