## Slide 1: Discussion contribution to RAN of NR V2X
NTT DOCOMO
3GPP TSG-RAN #78 RP-172463
Lisbon, Portugal, Dec. 18-21, 2017
Agenda Item: 9.1.1

## Slide 2: Background
Similar to LTE V2X, challenges are different between PC5 and Uu to support NR V2X
  For PC5, large specification impact and compatibility among different releases are major challenges
    For broadcast services supporting legacy UEs, UE has no choice but to transmit with legacy compatible mechanisms
  For Uu, specification impact dedicated for V2X services is not clear and can be small. But feasibility study is necessary.
In NR V2X, not only below 10 GHz, but also above 10 GHz including 63-64 GHz are considered as target spectrum for PC5 operation

## Slide 3: Questions for PC5
(Q1) What is Intended services for each spectrum and RAT? e.g.,
  Below 10 GHz, LTE V2X  V2X use cases (basic safety)
  Below 10 GHz, NR V2X  eV2X use cases
  Above 10 GHz, NR V2X  eV2X use cases
(Q2) Can V2X and eV2X use cases co-exist in the same carrier? Or, should it be different carrier (adjacent carrier in the same band or different band)
  It is related to objective on co-existence
(Q3) Are there any necessity of a spin-off WI in Rel-16?
  Market demand to have a spin-off WI for below 10 GHz in Rel-16?
  Can a WI in single release complete specification of PC5 below and above 10 GHz?
Baseline considerations
We should avoid market fragmentation (between LTE V2X and NR V2X, within NR V2X releases)
Continuous V2X evolution may or may not introduce compatibility issue.
Considering longer product cycle, NR V2X should not targeting to replace existing V2X technologies.

## Slide 4: Questions for Uu
(Q1) What is V2X specific Uu enhancement?
  If V2X specific Uu enhancement is not clear, feasibility study based on Rel-15 NR Uu will be necessary
(Q2) Are there any necessity of enhancement on LTE Uu? e.g.,
  For network control of NR PC5
  For NSA operation between LTE Uu and NR Uu

## Slide 5: V2X Specification Schedule for below 10 GHz
 | Rel-16 | Rel-17
Alt. 1 |  | 
Alt. 2 |  | 
Alt. 3 |  | 
Alt. 4 |  | 
Alt. 5 |  | 
Alt. 6 |  | 
WI (PC5)
WI (Uu)
SI (PC5 + Uu)
WI (PC5)
WI (Uu)
WI (PC5)
WI (PC5)
SI (PC5)
WI (PC5)
SI (PC5 + Uu)
WI (PC5 + Uu)
SI (PC5 + Uu)
SI (PC5)
WI (PC5)
WI (Uu)
SI (PC5+Uu)
WI (Uu)
SI (PC5 + Uu)
WI (PC5 + Uu)

## Slide 6: V2X Specification Schedule for above 10 GHz
 | Rel-16 | Rel-17
Alt. 1 |  | 
Alt. 2 |  | 
Alt. 3 |  | 
Alt. 4 |  | 
Alt. 5 |  | 
Alt. 6 |  | 
SI (PC5 + Uu)
WI (Uu+PC5)
SI (PC5 + Uu)
SI (PC5 + Uu)
WI (Uu)
SI (PC5 + Uu)
SI (PC5 + Uu)
WI (PC5 + Uu)
SI (PC5 + Uu)