## Slide 1
Views on UE NR features
www.huawei.com
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18-21, 2017
Agenda Item: 9.2.1
Huawei, HiSilicon
RP-172481
Notes: 讲解：
我希望向大家汇报三方面的情况。
行业趋势与华为战略
2013年经营业绩
未来（行业有希望，运营商选择我们，员工热情奋斗）

## Slide 2
There has been ongoing discussion about UE feature list on Rel-15 NR in RAN1,RAN2 and RAN4 [1]-[3].The number of UE features listed tend to grow very large. RAN guidance can be helpful to avoid unnecessary UE feature segmentation
Our views on some important features are also presented
          [1] R1-1720788, RAN1 UE feature list on Rel-15 NR, NTT DOCOMO
          [2] R2-1714226, Offline discussion output on L2/3 capabilities, Intel
          [3] R4-1714257. LS reply on MIMO layers UE capabilities MIMO capability, RAN4
Introduction

## Slide 3
Avoidance of unnecessary segmentation of UE features
In the offline discussion in RAN1#91, 91 items were proposed to be added on top of 90 items submitted before RAN1#91 in [1].
Since each segmented feature item can theoretically be set to optional and not all UEs would implement it, unnecessary segmentation of features would potentially bring problems to the following aspects,
  potential degradation of system performance in the real deployment
  unclear message to the feature planning in the deployment and to product planning that leads to diverged implementation of features, which would hurt the ecosystem
Proposal: RAN to provide guidance to Rel-15 feature list discussion that the granularity of features should be kept reasonably big to avoid unnecessary segmentation

## Slide 4: Overview of RAN1-led NR features
0. Waveform, modulation, subcarrier spacings, and CP
  Pi/2- BPSK optional [0-5]
  60kHz[0-10] and ECP[0-11] mandatory
1. Initial access and mobility
  CSI-RS based RRM/RLM/BM mandatory [1-6,1-7,1-8]
2. MIMO/RS
  4 layer PDSCH reception at the UE as mandatory[2-2]
  PRB bundling with size 2/4 [2-3]
  DMRS configurations with up to 12 orthogonal ports[2-3]
    Support both configurations type 1 and type 2
  2 layer PUSCH transmission at the UE as mandatory[2-5]
  CSI-RS based beam management as mandatory[2-8]
  DL Codebook: Type-I up to 16 ports and A subset of Type II feedback schemes can be mandatory[2-12/13]
  PTRS as mandatory at least for high frequency[2-15/16]
  CSI-RS for fine time and frequency tracking (TRS) as mandatory[2-17]
  SRS antenna switching and carrier-based switching as mandatory[2-18]
3. Scheduling and HARQ
  PDCCH monitoring[3-4] and Blind Decoding[ 3-6], UE Processing Time[3-26], Soft Buffer Size[3-25]
  Grant-free type I mandatory [3-31, 3-32]
  A-CSI on short PUCCH mandatory[3-19]
  TDD and Group-common PDCCH [3-41,3-42]
4. CA/DC, BWP, SUL
  BWP adaptation mandatory[4-2]
  SUL [4-9]
5. Channel coding mandatory [5-1]
6. UL TPC[6-1]
  *The feature numbers are according to R1-1720788, RAN1 UE feature list on Rel-15 NR

## Slide 5: WF, modulation, SCS and CP

## Slide 6: Optional: pi/2 BPSK [0-5]
Pi/2 BPSK w./w.o FDSS
  The output power boosting resulting from pi/2 BPSK w./w.o FDSS highly depends on the UE max. power limit, PA characteristics and RF requirement
    In LTE, RAN1 #48 concluded that none of pi/2 BPSK or FDSS (frequency domain spectrum shaping) are supported in LTE UL, considering the following response from RAN4
      It is possible to achieve the nominal maximum output power with LTE PA for QPSK without FDSS assuming a low number of resource blocks
      it is not feasible to increase the UE output power beyond the maximum nominal output power due to the regulatory requirements and co-existence issues.
    In NR, the evaluation results show that pi/2 BPSK w./w.o FDSS can bring potential benefit for below 6GHz HPUE (26dBm max. output power) and above 6GHz UE, while it highly depends on the PA characteristics and RF requirements on ACLR and EVM. Therefore, pi/2 BPSK support is up to UE implementation
  Pi/2 BPSK will increase testing complexity if mandatory
  Pi/2 BPSK w./w.o FDSS should be optional as UE capability

## Slide 7: Mandatory: 60kHz [0-10]
Benefits of 60KHz
For URLLC
  60kHz numerology can allow for relaxed
  hardware processing to meet 0.5ms URLLC
  latency than 30 kHz numerology
  60kHz can provide better performance (2-3dB) than 30kHz with the same mini-slot length
For eMBB
  Better (3-5dB) link performance for high speed scenario
  Better (12-16%) user throughput gain for low to medium traffic load
  60kHz agreed as mandatory for mm-wave, it is straight forward to support 60kHz for those UE which support mm-wave
URLLC coexistence with eMBB
  In a carrier, URLLC traffic can be flexibly scheduled in 60kHz BW part
    60kHz numerology provides more flexible scheduling opportunity for URLLC
    60kHz BW part does not contain SSB, hence, resource allocation is less constrained
  Regular/Large eMBB traffic can be scheduled in 30kHz or 15kHz BW part with slot-level TTI
  For dynamic resource sharing, eMBB traffic can be opportunistically scheduled in 60kHz BW part

## Slide 8: Mandatory: 60kHz ECP [0-9]
  Use cases for ECP
    Multiplexing of eMBB and URLLC deployed below 6GHz
    Transmission of URLLC with 60 kHz subcarrier spacing
    High speed scenario for 30 kHz and 60 kHz (including SFN and Non-SFN)
  60kHz ECP can provide larger gain in SFN and Non-SFN high speed scenarios
All UE need to support 60kHz ECP for long delay spread scenarios
Non-SFN TDL-A
Non-SFN TDL-B
SFN TDL-A

## Slide 9: IAM: CSI-RS based RRM/RLM/BM mandatory

## Slide 10: Mandatory: CSI-RS based RRM/RLM/BM [1-6,1-7,1-8]
Application Scenarios
  Efficient for NR deployment supporting TRPs in SFN (specifically of SS/PBCH blocks) operation
    CSI-RS for mobility from the target cell can be configured in the handover command (and the associated dedicated PRACH preambles). Target cell can establish the right TRP(s) based on the CSI-RS association with RACH preamble.
  Secondary Carrier could be without SS Blocks (e.g. non-contiguous intracell CA). For efficient HO or carrier activation/deactivation, CSI-RS needs to be configured in these Scells.
Benefit of CSI-RS for RRM and RLM:
  Allow networks to configure SS Blocks burst set periodicity up to 160ms for power efficient network operations.
  Per UE, CSI-RS can be configured in wider bandwidth and on a per need basis providing improved RSRP and RSRQ accuracy.
  Provide an accurate RLM i.e. CSI-RS can be sent in narrower beam compared to SS-RS for RLM. This improves the hypothetical PDCCH BLER in addition to shorter monitoring time for UE due to shorter CSI-RS periodicities.
NR Cell 1
NR Cell 2
UE movement
CSI-RS based mobility
After hand-over, network can immediately establish UE-specific TRP(s) for data communication
CSI-RS can be configured in wider bandwidth “as needed”, providing improved RSRP accuracy.

## Slide 11: MIMO/RS

## Slide 12: Overview of MIMO/RS
4 layer PDSCH reception at the UE as mandatory[2-2]
PRB bundling with size 2/4 [2-3]
DMRS configurations with up to 12 orthogonal ports [2-3]
  Support both configurations type 1 and type 2
2 layer PUSCH transmission at the UE as mandatory[2-5]
CSI-RS based beam management as mandatory[2-8]
DL Codebook: Type-I up to 16 ports and a subset of Type II feedback schemes can be mandatory [2-12/13]
PTRS as mandatory at least for high frequency[2-15/16]
CSI-RS for fine time and frequency tracking (TRS) as mandatory[2-17]
SRS antenna switching and carrier-based switching as mandatory [2-18]

## Slide 13: Mandatory: DMRS configuration type 2 [2-3]
 | DMRS configuration Type 1 | DMRS configuration type 2
Main Features | Max 8 orthogonal ports for MU Max 4/8 ports for DL SU Comb 2 + 2 CS + (TD-OCC) | Max 12 orthogonal ports for MU Max 6/8 ports for DL SU 2-FD-OCC across adjacent REs + (TD-OCC)
Throughput | Lower throughput performance Smaller number of ports [More quasi-orthogonal layers] | Higher throughput performance Larger number of ports [Fewer quasi-orthogonal layers] 15%~20% mean UPT gain for 4Rx UE and 17%~29% mean UPT gain for 8Rx UE
Estimation Performance | Poor performance due to de-spreading loss: Unsuitable for large subcarrier spacing scenarios Unsuitable for frequency-selective scenarios | Robust performance with higher de-spreading gain: Benefit to large subcarrier spacing scenarios Benefit to frequency-selective scenarios ~1dB SINR gain @60KHz SCS or 1000ns delay spread
Reception Complexity | Higher channel estimation complexity Limits PRB bundling size | Lower channel estimation complexity Can support larger bundling size
All UE need to support DMRS configuration type 2 in terms of performance and reception complexity.
Notes: 4/8 or 6/8 are for configured with 1 (or 2) symbols with DMRS

## Slide 14
Mandatory: Type 2 Codebook [2-12/13]
Table 2. Overhead comparison of Type I and Type II |  |  |  |  |  |  | 
Payload size for 4 ports |  |  |  |  |  |  | 
 | Type I |  |  |  | Type II (L=2,W+S,8PSK) |  | 
 | WB-reporting | SB-reporting (10 subbands) |  |  | WB-reporting | SB-reporting (10 subbands) | 
Rank 1 | 5 | 23(L=1)/42(L=4) |  |  | 24 | 135 | 
Rank 2 | 6 | 15(L=1)/34(L=4) |  |  | 44 | 266 | 
Payload size for 8 ports (wideband) |  |  |  |  |  |  | 
 | Type I |  | Type II (L=2, W+S,8PSK) |  | Type II (L=3, W+S,8PSK) |  | Type II (L=4, W+S,8PSK)
Rank 1 | 8 |  | 27 |  | 39 |  | 49
Rank 2 | 9 |  | 47 |  | 72 |  | 94
Payload size for 8 ports (10 subbands) |  |  |  |  |  |  | 
 | Type I |  |  | Type II (L=2, W+S,8PSK) | Type II (L=3, W+S,8PSK) |  | Type II (L=4, W+S,8PSK)
Rank 1 | 26(L=1)/45(L=4) |  |  | 138 | 184 |  | 268
Rank 2 | 18(L=1)/37(L=4) |  |  | 269 | 362 |  | 532
Table 1. Performance comparison of type II over type I |  | 
 | Cell average gain | Cell edge gain
4T2R | ~18% | ~27%
32T2R | ~35% | ~49%
UE complexity comparison (8T2R, N1=N2=2, O1=O2=4, Rank1 feedback)
Taking 10 subbands as an example
  The total number of complex multiplication with Type I and Type II: 8120 and 2031
  Compared with Type I, the complexity at UE side for Type II is 25%
At least a subset of type II NP codebook should be as mandatory for UE capability.

## Slide 15: Mandatory: SRS antennas switching [2-18]
  Support higher rank DL transmission
  With 4 Rx at UE side, support up to 4 layers DL transmission.
  In the TDD case, enable 4 antenna SRS switching (1T4T or 2T4T) for obtaining the full rank channel.
About 23% mean UPT gain can be observed over 2Tx switching for 2T4R/UE
About 26% mean UPT gain can be observed over 1Tx switching for 1T4R/UE

## Slide 16: Scheduling and HARQ

## Slide 17: PDCCH monitoring periodicity [3-4] and Blind Decoding [3-6]
3-4: Minimum PDCCH monitoring occasion for a CORESET should be defined for different SCS, i.e,
  2OSs for 15kHz SCS
  4OSs for 30kHz SCS
  7 OSs for 60kHz SCS
  14 OSs for 120kHz SCS
3-6: Scale the BD (blind decoding) capability with up to 8CC is acceptable.
Number of BD in different SCS
  Same total BD per slot for slot and non-slot monitoring
  Higher SCS can have smaller number of BD
No. of PDCCH BDs per slot | SCS |  |  | 
 | 15kHz | 30kHz | 60kHz | 120kHz
PDCCH monitoring periodicity of 14 or more symbols | 44 | 22 | 11 | 6
PDCCH monitoring periodicity of less than 14 symbols | 44 | 22 | 11 | 6

## Slide 18: HARQ Processing Time [3-26]
The maximum number of HARQ process should be 16, for DL and UL respectively.
UE report the capability of N1 and N2 in different scenarios
  Slot-based scheduling in the non-CA case with single numerology for PDCCH, PDSCH, and PUSCH
  The HARQ time for non-slot-based scheduling can’t simply take the slot-based scheduling as the baseline.
  The values of N1 are determined using the DL numerology for mixed numerologies scheduling.
  The values of N2 are determined using the UL numerology for mixed numerologies scheduling.
  For CA, we can assume the same capability apply to each CC for up to 4 CC
Configuration | HARQ Timing Parameter | Units | 15 KHz SCS | 30 KHz SCS
Front-loaded DMRS only | N1 | Symbols | 3 | 5
Front-loaded + additional DMRS | N1 | Symbols | 12 | 12
Frequency-first RE-mapping | N2 | Symbols | 4 | 6
(Capability #2)
15 KHz SCS | 30 KHz SCS
[2.5-4] | [2.5-6]
[12] | [12]
[2.5-6] | [2.5-6]
Status of RAN1 discussion

## Slide 19: UE Soft Buffer Size [3-25]
UE capacity depends on instant peak data rate and sustainable data rate.
  instant peak data rate depends on baseband processing capability
  sustainable data rate depends on UE soft buffer size, in addition to baseband processing capability
Proposal: report soft buffer size as UE capability.
Proposal: in LTE-NR DC, semi-static soft buffer sharing between LTE and NR is supported
Define two types of LTE-NR DC UEs
  Type 1:with limited LTE-NR interworking capability
  Type 2:with tight LTE-NR interworking capability
Report the following UE soft buffer size as UE capability:
  Buffer size for LTE operation
  Buffer size for NR operation
  Total buffer size for LTE-NR DC operation.

## Slide 20
Mandatory: GF Type 1 and repetitions [3-31, 3-32]
GF Type | Type Definition | Target Scenarios | Benefits
Type 1 | Resource (re)configuration is only based on RRC signaling and no L1 signaling is needed | low-latency and high-reliability services with sporadic and non-periodic packet arrivals, e.g., URLLC service Can also support services with periodic packet arrivals, e.g., VoIP Massive small packet transmissions with low cost and low signaling overhead in e.g., mMTC and eMBB scenarios | [Latency] Simple resource (re-)configuration suitable for unknown traffic pattern (event driven and sporadic) and ultra low latency feature [Reliability] Simple resource (re-)configuration with Less L1 signaling overhead and reliability issue, especially for ultra high reliability cases [Service diversity] Simple resource configuration to support multiple configurations for different types of services with various latency and reliability requirements simultaneously in case the number of serving cells is limited [Energy saving] Simple resource configuration to avoid unnecessarily frequent DCI monitoring to save energy consumption for the massive MTC devices with latency budget [Efficiency] Allow contention to support higher resource utilization
Type 2 | Resource (re)configuration is based on both RRC signaling and L1 signaling, where L1 signaling is used for resource activation/deactivation/modification | Moderate-to-low- latency and reliability services Most likely for the case with known traffic patterns, e.g., periodic packets such as VoIP | [Efficiency] Allow contention to support higher resource utilization [Flexible control] More flexible and dynamic for resource update when accurate CSI knowledge is available
LTE SPS | Semi-statically configured resource with DCI activation/deactivation | Periodic traffic such as VoIP | [Flexible control] More flexible and dynamic for resource update when accurate CSI knowledge is available
Proposal: 3-14 (DL SPS) is optional (not widely used in LTE). GF Type 1 is mandatory
Proposal: K repetition should be mandatory for GF (no need for a UE feature separate than GF). If split number of repetitions into different UE features, then support at least k=4
4 Repetitions
3 Repetitions
2 Repetitions
1 Repetition
Performance improvement by HARQ combining
Latency reduction of GF-repetition over GB-Rx

## Slide 21: Mandatory: A-CSI on short PUCCH [3-19]
Motivation 1: provide fast CQI feedback, such as Y=0
  Support CSI feedback in the same slot as DL grant
  Provide in-time CSI feedback to enable fast link adaption for DL scheduling
  Good for services like URLLC service requiring low latency
Motivation 2: suitable for beam reporting
  Only require lightweight CRI/RSRP feedback of around 10 bits for beam management
    Beam management procedures are mainly based on aperiodically triggered beam sweeps
Motivation 3: beneficial for DL heavy case
  Overhead for A-CSI on short PUCCH is smaller than A-CSI on PUSCH
  Uplink portions of slots may not be long enough for long PUCCH and long PUSCH
  Can configure more short UL portions for low latency (HARQ, CSI)

## Slide 22: TDD: Operation modes for NR [3-41/42]
During offline discussion, it was proposed that NR supports the following operation modes:
  Semi-static SFI configuration without dynamic SFI
  Dynamic SFI without semi-static SFI configuration
  Semi-static SFI configuration with dynamic SFI
  No semi-static SFI configuration and no dynamic SFI
    All transmission direction via DCI and/or configured periodic DL/UL signals
Proposal: Operation mode 4 (i.e. no semi-static SFI configuration and no dynamic SFI) should NOT be assumed as a typical network operation (or supported as optional)
  Note: Both semi-static operation (operation mode 1) and dynamic operation (operation mode 2/3) are beneficial for NR thus should be supported in NR

## Slide 23: CA/DC, BWP, SUL

## Slide 24
Mandatory: BWP adaptation [4-2]
Scenarios
Scenario#1 (agreed): Supporting reduced UE BW capability
Scenario#2 (agreed): Supporting reduced UE energy consumption by mean of bandwidth adaptation
Scenario#3 (agreed): Supporting FDM of different numerologies
Scenario#4: not support as a wideband carrier, support it as non-contiguous intra-band carrier aggregation
  Merits of BWP adaptation
    Scenario#2 : UE power saving ( 20-90% power saving depend on the ratio of wider BWP and narrow BWP)
      Adjust the RF bandwidth to reduce the energy consumption.
        Small bandwidth for PDCCH monitoring and low data rate transmission
        Large bandwidth for PDSCH with large traffic
    Scenario#3: Dynamic resource sharing
      Enable resource sharing for different BWP with different numerology
        eMBB UE can share the resource with URLLC BWP
        Low latency eMBB traffic can share its resource to large latency eMBB traffic

## Slide 25: SUL and UL sharing
Feature x-0: 7.5kHz shift for SUL bands in which UL sharing is possible, if the UE supports the SUL bands
  At least the already agreed, mandatory d 6 SUL bands n80 – n85 are SUL bands in which UL sharing is possible
  Additional SUL bands shall be identified as soon as possible
  Prefer “mandatory” for all LTE re-farmed bands
Feature x-1: A UE supporting a SUL band combination is mandatory to support the following (with Feature x-0 as a pre-requisite if the SUL band is possible for UL sharing)
  RACH, PUSCH, PUCCH, SRS operations on SUL and non-SUL of the same cell
  Same and different numerologies between DL/non-SUL and SUL of the same cell
  DCI based PUSCH scheduling on SUL and non-SUL of the same cell
Feature x-2: Switching time between LTE UL and NR UL on the same UL
  UE shall report one of “~0us” and “<20us”
  Per UE capability, i.e. same capability applies to all EN-DC band combinations supported by the UE, in which NR SUL overlaps with LTE UL
Feature x-3: Switching time between NR SUL and NR non-SUL of the same cell
  No agreed switching time so far
  Per SUL band combination capability and may not need UE capability signaling, i.e. all UEs supporting the same SUL band combination shall support the same switching time between NR SUL and NR non-SUL

## Slide 26
Copyright©2015 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Thank you !