## Slide 1: Motivation for new SI: Study on Flexible and Full Duplex for NR
LG Electronics and China Telecom
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18 - 21, 2017
RP-172501

## Slide 2
Introduction
Trends in NR
  Support duplexing flexibility with and without cross-link interference mitigation schemes
  Explosive Increase in Demand for Data Traffic
    Traffic volume/burst and DL/UL traffic asymmetry
  Ultra Low Latency required
  Support Various Usage Scenarios by a single cell: eMBB, URLLC, mMTC
Enabling Technologies
  Advanced cross-link interference mitigation schemes such as IC receivers
  Dynamic and flexibility of frequency resource utilization
    Support flexible DL/UL resource allocation with FDM manner
    - e.g., multiplexing between eMBB DL and URLLC UL with FDM manner
    - e.g., multiplexing between mMTC UL and eMBB/URLLC DL with FDM manner
  Full duplex functionality
    Support simultaneous DL/UL resource allocation for spectral efficiency enhancement and latency reduction
NR requires further enhanced solution with high spectral efficiency and low latency

## Slide 3
Motivation
In Rel-14 NR SI, performance benefits of duplexing flexibility are observed in various deployment scenarios
Observations for indoor hotspot scenario:
  Evaluations show that duplexing flexibility with cross-link interference mitigation schemes and on a 4GHz and 30GHz provides better UPT compared to static UL/DL resource partition and duplexing flexibility without cross-link interference mitigation schemes
  Evaluations show that duplexing flexibility without cross-link interference mitigation schemes on a 4GHz and 30GHz provides better UPT compared to static UL/DL resource partition at least for some cases
  The evaluated cross-link interference mitigation schemes include sensing based methods, advanced receivers (e.g. MMSE-IRC, EMMSE-IRC), coordinated scheduling/beamforming, power control, link adaptation, hybrid dynamic/static UL/DL resource assignment.
Observations for urban macro scenario:
  Evaluations show that duplexing flexibility with cross-link interference mitigation schemes on a 4GHz unpaired spectrum and on a 2GHz paired spectrum provides better average UPT compared to static UL/DL resource partition and duplexing flexibility without cross-link interference mitigation schemes.
  The evaluated cross-link interference mitigation schemes include advanced receivers (e.g. MMSEIRC, EMMSE-IRC, packet exchange for interference cancellation), coordinated scheduling/beamforming, power control, link adaptation.
  Evaluations show that duplexing flexibility on a 2GHz paired spectrum with SRS on the DL part without dynamic DL/UL resource allocation provides better cell average/edge throughput compared to no SRS on the DL part of the spectrum.

## Slide 4
Motivation
As service requirement with asymmetric UL and DL traffic increases, and the ratio between UL and DL traffic changes over the time, the static paired spectrum for UL and DL is not efficient to support dynamic asymmetric traffic.
Duplexing flexibility in both paired and unpaired spectrum are essential.
Service type | UL/DL ratio -average
Online video | 1:37
Software download | 1:22
Web browsing | 1:9
Social Netwok Service | 4:1
Email | 1:4
P2P video sharing | 3:1

## Slide 5
Motivation
Limitation in TDM between DL/UL
  TDM between DL and UL leads higher latency in both DL and UL due to time partitioning between DL and UL
  Symmetric DL/UL partitioning to address URLLC may not be effective from spectral efficiency perspective particularly when traffic patterns are either DL heavy or UL heavy
Further enhancements in spectral efficiency
  By allowing full duplex at one spectrum, enhanced spectral efficiency can be achieved (ideally by 2x)

## Slide 6
Flexible duplex for paired spectrum
Flexible bands for paired spectrum
  Flexible bands can be allocated to DL or UL according to DL/UL traffic ratio.
DL
UL
Symmetric DL/UL
spectrum allocation
f1
f2
f3
f4
DL
UL
Asymmetric DL/UL
spectrum allocation
f1
f2
f4
f3
f4
Flexible band

## Slide 7
Flexible Duplex for NR
Flexible Duplex with FDM manner
  Handling Mixed Usage Scenarios
    - e.g., multiplexing between eMBB DL and URLLC UL with FDM manner
    - e.g., multiplexing between mMTC UL and eMBB/URLLC DL with FDM manner
  Sub-band wise DL/UL adaptation required
  Occurrence of DL’s OOB power in UL reception at gNB
  Occurrence of inter-cell cross-link Interference between gNBs and UEs
Potential gains from flexible duplex with FDM manner
  DL or UL resource availability at any time  possibly reduce latency for URLLC applications
  Multiplexing becomes easy for different usage scenarios
<Example of flexible duplex with FDM manner>
gNB
eMBB UE #1
URLLC UE #2
DL
Guard Band
UL

## Slide 8
Full Duplex for NR
<Example of full duplex operation at gNB>
Full Duplex gNB
UE #1
UE #2
Full Duplex at gNB
  Efficient adaptation for time variant DL/UL data traffic
    Spectral efficiency enhancement via fully utilized frequency resources
    Overall latency reduction via always on UL transmission opportunity
    Easier multiplexing among different usage scenarios with different DL/UL traffic patterns
  gNB with Full Duplex capability required
  Occurrence of self-Interference at gNB
  Occurrence of inter-cell cross-link interference between gNBs
  Occurrence inter/intra-cell cross-link interference among UEs
Potential gains from full duplex
  Expected spectral efficiency enhancement
Self-interference
UE-to-UE cross-link Interference
DL
Full Duplex (DL+UL)
UL
* N X M, where N, M are the number of transmit and receive antennas, respectively.

## Slide 9
Objectives
  To study enhanced mechanisms for providing better duplexing flexibility in unpaired and paired spectrum.
    Development scenarios and use cases of Rel-15 NR SI/WI are the starting point for the discussions.
    It is assumed that downlink and uplink resources in a band can be multiplexed in TDM manner.
  To study mechanisms and benefits for providing full duplex operations in unpaired and paired spectrum.
    Full duplex operation includes simultaneous DL/UL transmission on the same resource and/or DL/UL multiplexed in a FDM manner
    Objectives include deployment scenario/use cases and study on interference mitigation/cancellation/coordination techniques.

## Slide 10: Thank You