## Slide 1: Channel estimation enhancement for high speed vehicles using pre-DFT RS
CEWiT, IITH, IITM, Tejas Networks, Reliance Jio, Vivo
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18 - 21, 2017
R4-172637

## Slide 2: Background
RAN1 has defined PT-RS feature that uses pre-DFT RS for DFT-S-OFDM modulation.
While PT-RS are intended for phase tracking in mmwave systems, the RS can be used for other purposes such as channel/Doppler tracking of high velocity/speed UEs.
IMT2020 demands higher UE speeds up to 500 Kmph.
In the Dec version of rel-15 specification, additional RS are defined to allow channel tracking in high speed UEs.
  Yet, at high carrier frequencies, and high vehicular speeds Doppler effects cause channel variation within a OFDM symbol that cannot be tracked for existing DFT-S-OFDM PUSCH slot formats.
Since, Pre-DFT RS insertion along with data is already supported by PT-RS, this feature can be used for channel tracking of high speed Ues (such as Ues located in high speed trains) in coverage limited scenarios
  However, channel tracking requires a higher RS density than phase tracking.
To this end in RAN1-90bis the following has been agreed:
R1-1719073 WF on pre-DFT RS IITH, Mitsubishi, Deutsche Telekom, AT&T, IITM, CEWiT, Tejas Networks, Reliance Jio Also supported by Qualcomm, IDC, National Instruments, KDDI, Softbank
  Conclusion
  Companies are encouraged to study if chunk based pre-DFT RS K>4 can be supported for enhanced channel estimation of DFT-S-OFDM PUSCH in future NR MIMO related study/work items
  FFS: values of K and other details (K is the number of samples in a chunk)
Considering the above conclusion, we propose to introduce a SI followed by WI that defines an increased pre-DFT RS density for channel tracking purposes.

## Slide 3: Simulation Results

## Slide 4: Summary of Link Simulations with High Doppler
Figure 1 QPSK, Comparison of LTE-rel 15 and pre-DFT Reference Signal (RF) (denoted as legend IIT proposal)
Assumptions: Single tap Rayleigh fading with Doppler 1Rx, 1Rx, 3.5 GHz, 15 Khz subcarrier spacing, 28.57% RS overhead in both cases, Rel-15 uses 4 dedicated RS in 14 OFDM symbols. Pre-DFT RS is inserted in every OFDM symbol without dedicated RS. High speed trains typically
Assumptions: AWGN, receiver is unaware of Tx shaping type , Practical (MMSE); adaptive (coarsely optimized) frequency smoothing BW
Observations:
Under same RS overhead, Pre-DFT RS insertion in every OFDM symbol without dedicated RS tracks the channel in High Doppler
Figure 2 16 QAM, Comparison of LTE-rel 15 and pre-DFT Reference Signal (denoted as legend IIT proposal)

## Slide 5: Proposal
The detailed objectives are as follows.
  Evaluate pre-DFT RS for both data and control channels at high UE speeds
  Based on the outcomes of the study phase consider specification of the required pre-DFT RS density for DFT-S-OFDM waveforms for FR1 and FR2.
    Consider UE speeds up to 500 Kmph for FR1