## Slide 1: Motivation for study on 6 GHz LTE LAA/eLAA and NR-U (New SID proposal: RP-172510)
3GPP TSG RAN Meeting #78
Lisbon, Portugal, Dec. 18 - 21, 2017
Agenda item: 10.1.5
RP-172554
Ericsson

## Slide 2: Background
Both CEPT and FCC are examining the possibilities of making available additional spectrum in 6 GHz band:
  CEPT aims at introducing low power wireless access systems (including Radio LAN (RLAN)) in the band 5.925-6.425 GHz under a non-protected basis and ensuring certainty of continued operation, development and protection of existing services (Fixed Services (FS) and Fixed Satellite Services (FSS))
  FCC issued a Notice of Inquiry focusing on exploring potential opportunities (for both unlicensed and licensed services) in 5.925-6.425 GHz and 6.425-7.125 GHz
ETSI is developing the TR 103 524 on Wireless Access Systems including RLANs in the band 5.925-6.725 GHz
Different incumbents in different regions:
  In Europe:
    5.925-6.700 GHz band is allocated to FS, FSS earth to space and, on a secondary basis to Earth Exploration Satellite (passive);
    6.700-7.025 GHz band is allocated to FS, FSS (earth to space, space to earth) and, on a secondary basis to Earth Exploration Satellite (passive).
  In US:
    5.925-6.425 GHz band is currently allocated for non-federal use for FSS and FS on a primary basis;
    6.425-7.125 GHz band is allocated exclusively for non-federal use on a primary basis for FS at 6.525-7.125 GHz, Mobile Service at 6.425-6.525 GHz and 6.875-7.125 GHz, and FSS at 6.425-6.700 GHz and 7.025-7.075 GHz for uplink and at 6.700-7.025 GHz for both uplink and downlink.

## Slide 3: Justification/Key benefits
Avoid that 3GPP LTE and NR technologies, expected among others in the 6 GHz spectrum, arrive late (after other technologies)
Following the regulatory framework since the beginning help accelerates definition of RF requirements
Share coexistence studies with other regulatory bodies and contribute to solutions for mitigating the interference to the victim services
Start studying unlicensed 3GPP technologies in the first segment of 6 GHz spectrum begins harmonization process of the band in different regions
  In Europe 5.925-6.425 GHz is considered for wireless access system, including RLANs
  In US potential use of 5.925-6.425 GHz band for unlicensed operations is under investigation

## Slide 4: Objectives of the new SID
WG impacted: RAN 4, RAN 1, RAN 2
Main objectives:
  Investigate coexistence aspects, regulatory framework in different regions, and band arrangement to have band harmonization in 6GHz [RAN4] with focus on the band 5.925-6.425 GHz for support of
    LTE LAA/eLAA operations
    NR-U operations
  Study channel access procedures to enable effective and fair coexistence among different technologies operating in 5.925-6.425 GHz [RAN1, RAN2] (to be started in a second phase)