## Slide 1: Enabling high power UEs using pi/2 BPSK with spectrum shaping feature for sub 6 GHz LMLC deployments
CEWiT, IITH, IITM, Tejas Networks, Reliance Jio
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18 - 21, 2017
R4-172637

## Slide 2: Background
RAN1 has defined the pi2 BPSK modulation for DFT-S-OFDM for PUSCH and long PUCCH carrying more than 2 UCI bits. The spectrum shaping function is not specified in the standard but RAN4 defines EVM equalizer spectrum flatness requirements for the spectrum shaping filter so that UE implementation allows vendor specific spectrum shaping filtering. In RAN4#85 meeting, the following has been agreed for FR2:
The spectrum shaping filter and associated requirements are applicable only to FR2
  UE shall be allowed to employ spectral shaping for pi/2 BPSK
  We propose the following X1, X2 and Y values, as defined in R4-1711569, for spectrum flatness requirement so as to not preclude any of the proposed filters
    X1 = [6]dB, X2 = [20] dB, Y = [-15] dB
    X3 such that X2 = X1 + X3
    Impact on network performance should be studied
PA Output Power for FR2: Qualcomm and IITH have shown that the PA can be driven with BPSK at a higher power level than with QPSK while meeting the requirements
  The waveform defined by BW = 100MHz, SCS=60KHz, DFT-S-OFDM QPSK, 128RB0 is the reference waveform with 0dB MPR and is used for the power class definition
  MPR requirements for waveforms that operate at higher output power than the reference waveform can be defined with a negative value
  The Pcmax requirement includes an additional term to account for negative MPR in both Pcmax_L and Pcmax_H terms
An agreement could not be reached on the spectrum shaping filter usage to FR1.

## Slide 3: Motivation for introducing spectrum shaping for FR1
3GPP IMT2020 submission to ITU-R WP 5D should mandatorily meet Low Mobility Large Cell (LMLC) requirement that is introduced by the Indian administration
LMLC is targeted for rural sub 6 GHz deployments with large cell radius. Deployments are expected in both TDD and FDD bands.
Typical inter-site distances are or the order of 5 Km.
In order to meet the coverage demands of large cells, we propose to use low PAPR pi/2 BPSK DFT-S-OFDM waveform with spectrum shaping for both data and control channels.
This waveform allows up to 3.0 dB higher UE power compared to reference QPSK waveform.
We propose to enable a 26 dB UE power class using a negative MPR. Higher power UEs other than 26dBm can also be introduced using negative MPR value.
The massive MIMO receiver processing gain coupled with the higher UE power is essential for meeting the coverage
Note: Apart from LMLC use case, many vendors and operators expressed interest in supporting pi/2 BPSK with spectrum shaping for FR1 for urban deployments

## Slide 4: Summary of link results for pi/2 BPSK with spectrum shaping for FR1

## Slide 5: Summary of Huawei Contributions
Figure 1 Dependence on #PRB of the detection loss of transparent RRC-1.0 (1+D) FDSS relative to no shaping. Contribution: R4-1710213
Assumptions: AWGN, receiver is unaware of Tx shaping type , Practical (MMSE); adaptive (coarsely optimized) frequency smoothing BW
Figure 1 BLER versus SNR (Link-level Simulation), Fading, Code rate 1/6, Contribution: R1-1705060
Assumptions: AWGN, receiver is unaware of Tx shaping type , Practical (MMSE); adaptive (coarsely optimized) frequency smoothing BW
Assumptions: Fading channel, Transparent filter, LMMSE channel estimation. MMSE equalization
Observations:
<0.6 dB loss in performance (worst case)
3 dB gain in PAPR

## Slide 6: Summary of Qualcomm Contribution
Figure 1 EVM as a function of the Antenna port power, Contribution number: R4-1713626
Observations:
PA Sat power was 30.2 dBm in the test conditions
Can increase the PA power to saturation level with minimal degradation in EVM

## Slide 7: IITH Results (AWGN) R4-1714191, Further Link Results for p/2 BPSK DFT-S-OFDM Waveform with Spectrum Shaping and MMSE Receiver
Assumptions: AWGN,Transparent filter, MMSE, Rate 1/6 convolution code, ZC pilots, Polynomial PA model, PA output power 25.6 dBm, Saturation power 26 dBm, M=Number of allocated subcarriers
Observations: Loss due to filtering is at most 0.6 dB using MMSE
M=24
M=120

## Slide 8: IITH Additional Link Results (Fading) R4-1714191 Further Link Results for p/2 BPSK DFT-S-OFDM Waveform with Spectrum Shaping and MMSE Receiver
Assumptions: TDL-C fading model, Transparent filter, MMSE, Rate 1/6 convolution code, ZC pilots, Polynomial PA model, PA output power 25.6 dBm, Saturation power 26 dBm
Figure 1: TDL-C 300ns, M=24
Observations: Loss due to filtering is at most 0.6 dB using MMSE for low delay spread and 1.2 dB using MMSE for very-high delay spread
Figure 2: TDL-C 1000ns, M=120

## Slide 9: Summary of Nokia Contribution
Parameter | No SS | 1+D | 50% truncated RRC, r=0.25 | 25% truncated RRC, r=0.25
PA out [dBm] (without loss) | 27.7 | 28.9 | 27.8 | 28.1
IBO [dB] | 2.4 | 0.1 | 2.3 | 1.8
LTE 30 kHz OOBEM margin [dB] | 4.8 | 3.8 | 4.9 | 4.0
LTE 1 MHz OOBEM margin [dB] | 0.2 | 0.1 | 0.3 | 0.0
EUTRA ACLR [dB] | 27.8 | 29.6 | 28.4 | 28.6
LTE IBEM [dB] | 1.8 | 0.3 | 1.9 | 1.0
Tx EVM [%] (complex plane) | 6.1 | 9.8 | 6.1 | 5.7
Link performance with and without spectral shaping in AWGN channel. Contribution: R4-1712476
Assumptions: AWGN, receiver is unaware of Tx shaping type, MMSE. 1/3 Rate.
Observations:
1+D has BLER of 1
  Conflicts woth Huawei and IITH data
PA gain of 1 dB
  Higher gains were achived by IITH and QC

## Slide 10: Summary of Ericsson Contribution
Assumptions: AWGN, receiver is unaware of TX shaping type , MMSE. 2/3 Rate. Three tap [y 1 y] filter used for spectrum shaping.
Contribution: R4-1712527
Filter | PSD flatness | MPR gain (dB) |  |  | Link loss (dB) |  | 
 |  | 3 RB | 18 RB | 100 RB | 3 RB | 18 RB | 100 RB
[0 1 0] | ± 0 dB | - | - | - | - | - | -
[0.05 1 0.05] | ± 1 dB | 0.1 | 0.2 | 0.3 | 0.1 | <0.1 | <0.1
[0.1 1 0.1] | ± 2 dB | 0.3 | 0.4 | 0.5 | 0.3 | 0.2 | 0.2
[0.15 1 0.15] | ± 3 dB | 0.5 | 0.5 | 0.8 | 0.5 | 0.3 | 0.3
[0.2 1 0.2] | ± 4 dB | 0.6 | 0.6 | 1.1 | 1 | 0.7 | 0.7
[0.3 1 0.3] | ± 5 dB | 0.6 | 0.7 | 1.6 | >2.5 | 1.7 | 1.7
Observations:
Spectral shaping has an impact on the BS receiver performance for high coding rate used (2/3)
  As per pi/2 BPSK is being considered for low MCS (last two entries of the table). Typical operational range -10 to 0 dB and code rates are around 1/6
  Rate=2/3 is the operational range for QPSK

## Slide 11: Values of X1, X2 and Y by Proponents
Company | X1 (dB) | X3 (dB) | X2 (dB) | Y (dB)
Qualcomm | 6 | 14 | 20 | --
Huawei | [6-8] | 12 | [18-20] | [-15 ... -25]
IITH | 5 | 15 | 20 | -15
Nokia | 4.5 | 4.5 | 10 | -15
Ericsson | 4/6 | 0 | 4/6 | --

## Slide 12: Summary
PA Output Power: Qualcomm and IITH have shown that the PA can be driven with BPSK at a higher power level than with QPSK while meeting the requirements
  Intel [R4-1712330] proposed:
    The waveform defined by BW = 100MHz, SCS=60KHz, DFT-S-OFDM QPSK, 128RB0 is the reference waveform with 0dB MPR and is used for the power class definition
    MPR requirements for waveforms that operate at higher output power than the reference waveform can be defined with a negative value
BLER AWGN:
  Huawei and IITH has shown <0.6 dB loss in performance due to filtering for narrow allocations and <0.1 dB for wider RB allocations using MMSE filter.
BLER Fading (IITH, Huawei results)
    Loss due to filtering is at most 0.6 dB using MMSE for low delay spread and 1.2 dB using MMSE for very-high delay spread.
  Low delay spread cases eg. in Narrow band allocations and LOS channels (like mmwave and Rural), detection losses are very low

## Slide 13: Proposal
The spectrum shaping filter and associated requirements are applicable to FR1
  UE shall be allowed to employ spectral shaping for pi/2 BPSK
  We propose the following X1, X2 and Y values, as defined in R4-1711569, for spectrum flatness requirement so as to not preclude any of the proposed filters
    X1 = 6dB, X2 = 20 dB, Y = -15 dB
    X3 such that X2 = X1 + X3
    Impact on network performance should be studied
PA Output Power for FR1: Qualcomm and IITH have shown that the PA can be driven with BPSK at a higher power level than with QPSK while meeting the requirements
  The waveform defined by BW = 100MHz, SCS=15KHz, DFT-S-OFDM QPSK is the reference waveform with 0dB MPR and is used for the power class definition
  MPR requirements for waveforms that operate at higher output power than the reference waveform can be defined with a negative value
  The Pcmax requirement includes an additional term to account for negative MPR in both Pcmax_L and Pcmax_H terms