## Slide 1: Motivation for SID proposal for RAN-centric BigData Collection and Utilization
CMCC
3GPP TSG RAN meeting #79
Chennai , India, March 19-22 2018
Agenda item: 9.1.4
RP-180312

## Slide 2
When BigData met LTE
Notes: over shot
OTT positioning
Standard BigData

## Slide 3: LTE BigData Utilization - Coverage Enhancement
MDT in Jiangxi Province
MDT in Shanxi Province
MDT-based RAN BigData is used to identify and analyze coverage issues, e.g. poor coverage and over shooting
Notes: over shot
OTT positioning
Standard BigData

## Slide 4: LTE BigData Utilization - Problem Detection
RLF report in Sichuan Province
By using traditional drive test, 288 problems were identified in 3 months
By using RLF Report, only 4 days spent and massive RFL reports (1473 per day) collected through MDT
The consistency of the two methods is more than 88%, and obviously MDT is more efficient
3 Months V.S. 4 Days

## Slide 5: LTE BigData Utilization - Positioning
Neural Network Algorithms | Algorithm 1 with 4Gbit training data | Algorithm 1 with 7Gbit training data | Algorithm 2 with 7Gbit training data | Algorithm 3 with 7Gbit training data
CDF of positioning accuracy <50m | 69.15% | 69.55% | 69.93% | 75.02%
CDF of positioning accuracy <100m | 86.12% | 88.15% | 88.04% | 89.58%
Shanghai, about 7 sq.km, with more than 160 base stations and 600 cells
Based on MR BigData, the CDF of positioning accuracy within 50m can achieve about 70%
The more BigData used, the higher accuracy achieved

## Slide 6: LTE BigData Utilization - Performance assessment for terminal models
•KPI can be associated with terminal models, since terminal models can be differentiated on network side by IMEI
•E.g., the sudden KPI drop of a newly launched smart phone is significantly lower than its predecessors
•Quick identification of the reason is important for the terminal vendor, network vendors and the operator

## Slide 7: BigData met LTE
Following advantages are observed and achieved from standard based BigData collection and utilization in LTE (i.e. MDT and SON):
  CAPEX & OPEX of operators significantly reduced, e.g. more accurate base station deployment, much less human resource for drive tests
  User experience enhanced, e.g. BigData based machine learning help proper RRM, Mobility Management and positioning
  Network planning and optimization becomes more effective and efficient, e.g. coverage enhancement and problem identification

## Slide 8: RAN-centric BigData collection and utilization should be thoroughly studied and investigated in NR
As in LTE, advantage of BigData collection and utilization still valid and attractive
Further enhancement and improvement will be achieved from lessons of LTE
New RAN architecture (CU/DU), powerful storage and computing capability of new RAN provide new opportunity for BigData collection and utilization

## Slide 9: Potential Specification Impact
Definition: what/where is BigData
  From consenting UEs: RRM measurement quantities, RLF, access failure,…
  From gNBs: L2 measurement quantities, signaling procedure log
Collection: how to obtain BigData
  Logical entity/function to configure and control collection
  Procedure of data collection (like LTE MDT)
Utilization: how to use BigData
  SON
  Open to third party,
  Edge computing

## Slide 10: SID objectives
Study the use cases and benefits of RAN centric BigData utilization, e.g. identify the NR scenarios that are the most prone to failures due to sub-optimal network configuration, scenarios of load balancing, and identify necessary standard effort on data collection and utilization. Scenarios where MCG is E-UTRA and SCG is NR (EN-DC) are included in the study.
Definition: Identify necessary measurement quantities for collection and utilization, including:
  RRM measurement quantities, RLF, access failure, etc from consenting UEs,
  L2 measurement quantities from gNB side, signalling procedure, from gNB side.
  Signalling procedure from eNB side, if needed, for EN-DC scenario.
Collection: Study the procedure for configuration and collection of UE measurements, L2 gNB measurements and signalling procedure for central analysis.
Utilization: Study necessary procedures and information exchange required for different use cases, e.g. SON, edge computing, as well as openness to the third party, etc.

## Slide 11
Thank You