## Slide 1
Motivation paper for SI on NR waveform beyond 52.6GHz
RP-180452
3GPP RAN #79
March 19-22, 2018
Chennai, India
Agenda Item 9.1.2
Qualcomm
Resubmission of RP-172635

## Slide 2: Outline
Background
Technical justification
Applicable scenarios
Waveform candidates
Preliminary comparisons
Proposal

## Slide 3: Background
Originally, NR SI considered operation at frequencies of up to 100GHz
  Channel model defined up to 100 GHz (ref. TR 38.900)
NR Rel-15 WI is defining operation up to 52.6GHz
  CP-OFDM for DL/UL and DFT-S-OFDM for UL
  Max channel BW: 100MHz (freq-range 1), 400MHz (freq-range 2)
    Subcarrier spacing: 15, 30, 60kHz for freq-range 1; 60, 120kHz for freq-range 2 (in addition to 240kHz for SSB)
    Max assumed FFT size: 4K points
Vast amount of spectrum available at 57-71GHz range
  Global spectrum for IEEE 802.11ad operation in 57-64GHz range [TR 38.805 for 60GHz band]
  ITS spectrum in Europe in 63-64GHz range
  FCC newly identified spectrum for wireless communications in the 64-71GHz range
NR-unlicensed SI calls out for operation at unlicensed bands above 52.6GHz to the extent that waveform design principles remain unchanged with respect to below 52.6GHz bands
Goal: want NR to be applicable for operation at these bands

## Slide 4: Technical justification
Operation at frequencies above 52.6GHz share some unique characteristics:
  Extremely harsh propagation loss
  Low PA efficiency
  High phase noise
  PSD limitations when applicable, e.g., 13dBm/MHz and 40dBm EIRP in 60GHz band
In addition, operation in 60GHz band (ref. 38.805) may require definition of channel bandwidths beyond 400MHz (e.g., around 2GHz) for, e.g., coex with IEEE 802.11ad systems
All of the above calls out for the need to study NR waveform for operation at frequencies above 52.6GHz

## Slide 5: Applicable scenarios
Operation at frequencies above 52.6GHz should be relevant for a variety of use cases:
  WAN operation, private networks, vehicular communications (C-V2X), and others
The waveform studies themselves should be agnostic to the type of spectrum, i.e., licensed, unlicensed or shared
Studies should consider the following aspects:
  From transmitter perspective: PAPR, power consumption
  From receiver perspective: implementation complexity, performance
  Generally: applicability to channel bandwidths beyond 400MHz

## Slide 6: Waveform candidates
CP-OFDM – regular NR DL waveform but with larger subcarrier spacing, e.g., 960KHz
  High PAPR, complexity relatively high complexity at both transmitter/receiver (due to FFT)
Single carrier waveform family: DFT-s-FDM and single-carrier (SC) QAM
  Better PAPR compared to OFDM
  DFT-s-FDM: NR UL waveform scaled to 960KHz subcarrier spacing
    Easy user multiplexing but with the cost of DFT spreading at transmitter
  SC-QAM
    Lowest PAPR, lower complexity at transmitter (no FFT) and receiver (if TDE used)
    Not as flexible in multiplexing users in frequency
    Bandwidth growth due to pulse shaping filter
Note that SID does not explicitly call out specific waveform candidates
  Shown here for background purposes only and to put in context some preliminary comparisons

## Slide 7: Preliminary comparisons
Single carrier waveform helpful for providing better coverage, critical in coverage limited mmW use case
  SC-QAM w/ QPSK has 4.4dB PAPR gain over OFDM
    SC-QAM w/ 16QAM still has 2.9dB PAPR gain
  SC-FDM w/ QPSK has 2.6dB PAPR gain over OFDM
    SC-FDM w/ 16QAM still has 1.9dB PAPR gain
Between SC-QAM and SC-FDM, SC-QAM has even better PAPR gain and worth considering
  1.8dB w/ QPSK
  2dB w/ 16QAM
EVM vs. clipped waveform

## Slide 8: Preliminary comparisons
Link level comparisons
For LOS channel , SC-QAM achieves similar performance as OFDM
For NLOS channel, the PAPR benefit of SC-QAM far outweighs the performance gain of OFDM

## Slide 9: Proposal
With the objective to further increase the footprint for applicability of 3GPP 5G NR systems, 3GPP needs to define a waveform suitable for operation at frequencies above 52.6GHz
Open SI in June ‘18 for the duration of 2 Quarters and with the following objectives:
  Waveform design for operation beyond 52.6GHz -- RAN1
    This design should take into consideration the following aspects:
      From transmitter perspective: PAPR, power consumption
      From receiver perspective: implementation complexity, performance
      Generally: applicability to channel bandwidths beyond 400MHz
    Note: the waveform design should be agnostic to the type of spectrum (i.e., licensed, unlicensed, or shared) or the applicable use case as the driving aspects for the waveform design are meant to apply fundamentally to any communication system operating at that frequency range.
  Channelization suitable for target bands, e.g., 57-64GHz (60GHz band), 64-71GHz (FCC) -- RAN4
Proposed TU allocation as shown in spreadsheet attached to the SID in RP-172633 (RAN1: 10TUs, RAN4: 3.5 TUs) over the duration of 2 Quarters: Q3 and Q4 ’18.