## Slide 1: Co-channel coexistence of NR-V2X with other technologies
3GPP TSG RAN #80 RP-180670
La Jolla, USA, 11th – 14th June 2018

## Slide 2: Background
NR V2X will need to coexist with other technologies in a co-channel fashion
  It is important to demonstrate to regulators that NR V2X can coexist with other technologies
  Otherwise it will be difficult to deploy NR V2X commercially and/or to secure spectrum
However, without proper guidance, coexistence can increase the scope of the study significantly and can slow down progress and cause loss of focus
We propose a ‘middle ground’ to address coexistence while limiting the related scope

## Slide 3: Proposal
The starting point should be that technologies can have different priorities in contending for the same spectrum
We know that co-channel coexistence between two technology at equal priority can be complex
  Example: LAA & WiFi
  This required TTI level of assessment for accessing the spectrum
However co-channel coexistence when technologies are at different priorities can be simpler
  Generic examples:
    The higher priority technology can transmit a beacon that can be detected by the lower priority technology
    The lower priority technology can then back off for by a certain amount of time/power
  Note that coexistence of LTE V2X with “tolling” technology already uses a similar approach
General concept

## Slide 4: Proposal
Only consider coexistence with technologies that occur at higher or lower priority wrt NR V2X
Only consider MAC layer & above solutions (RAN2)
Design can be agnostic to the technology with whom coexistence is being considered
Any physical layer beacon design, if needed, can be part of later releases or can be specified by regional ITS standards body tailored to their particular needs
Detailed proposal for NR V2X

## Slide 5: Examples of technologies covered
Technology | Technology’s priority against NR V2X (as specified by regional regulator or being proposed/studied/expected) | Co-Channel Coexistence to be covered in the NR V2X study?
Satellite | Higher [6] | Yes
Urban Rail | Higher or lower [6] [5] | Yes
Short range devices | Higher [6] | Yes
WiFi | Lower [8] | Yes
Co-channel coexistence between NR V2X and 802.11p or LTE V2X does not need to be studied

## Slide 6: Conclusions
The NR V2X study needs to consider co-channel coexistence with other technologies to ensure NR V2X can secure access to spectrum
Co-channel coexistence does not need to be a “complex affair” in the style of LAA
  Long term co-channel co-existence instead of slot level co-channel co-existence
  Upper layer (lead by RAN2) solutions should be considered instead
  Coexistence can be designed to be technology agnostic
RAN Plenary should agree on a charter for the NR V2X co-channel coexistence work

## Slide 8: References
[1] ECC Recommendation (08)01, “Use of the band 5855-5875 MHz for Intelligent Transport Systems (ITS),” 2015.
[2] EC Decision2008/671/EC, “Commission Decision 2008/671/EC of 5 August 2008 on the Harmonised Use of Radio Spectrum in the 5875 - 5905 MHz Frequency Band for Safety-related Applications of Intelligent Transport Systems (ITS),” 2008.
[3] Mandate to CEPT to study the extension of the Intelligent Transport Systems (ITS) safety-related band at 5.9GHz RSCOM17-26 rev.3
[4] ETSI TR 103 111 V1.1.1, “Electromagnetic compatibility and Radio spectrum Matters (ERM); System Reference Document; Spectrum requirements for Urban Rail Systems in the 5,9 GHz range,” 2014-10.
[5] ETSI TR 103 442 V1.2.1, “Railways Telecommunications (RT); Shared use of spectrum between Communication Based Train Control (CBTC) and ITS applications,” 2016-09.
[6] ECC Report 101, “COMPATIBILITY STUDIES IN THE BAND 5855 – 5925 MHz BETWEEN INTELLIGENT TRANSPORT SYSTEMS( ITS ) AND OTHER SYSTEMS,” Bern, 2007.
[7] ECC Report 228, “Compatibility studies between Intelligent Transport Systems (ITS) in the band 5855-5925 MHz and other systems in adjacent bands,” 2015.
[8] ETSI TR 103 309, “Broadband Radio Access Networks (BRAN); 5 GHz high performance RLAN; Mitigation techniques to enable sharing between RLANs and Road Tolling and Intelligent Transport Systems in the 5 725 MHz to 5 925 MHz band”, August, 2017
[9] RP-180426, “Summary of email discussion on NR V2X study item”, Vodafone
[10] ETSI EN 302 571, V2.1.1 “Intelligent Transport Systems (ITS); Radiocommunications equipment operating in the 5 855 MHz to 5 925 MHz frequency band; Harmonised Standard covering the essential requirements of article 3.2 of Directive 2014/53/EU”, 2017-02.

## Slide 9: Example: ITS spectrum in Europe [1][2][3][10]
Frequency Band | Frequency Range (MHz) | Usage
ITS-G5B | 5855 to 5875 | ITS non-safety applications
ITS-G5A | 5875 to 5905 | ITS road safety
ITS-G5D | 5905 to 5925 | Future ITS applications

## Slide 10: Example: Challenges to the ITS Spectrum in Europe
Several technologies such Urban Rail/CBTC[4] and RLAN[8] are vying for spectrum in the ITS spectrum
SRD (Short Range Devices) [6][7] already can coexist with higher priority in ITS-G5B
SRD specified at higher priority than ITS
RLAN (proposed at lower priority than ITS)
Urban Rail / CBTC (proposed at higher priority than ITS)
Urban Rail / CBTC (proposed at lower priority than ITS)

## Slide 11: Example: Possible new ITS Spectrum in Europe
There is discussion in Europe for new spectrum in 5.9 GHz to 7.2GHz
5GAA sent a LS to CEPT that some spectrum in this new band could be useful for advanced V2X use cases.
However, other constituencies are interested in this piece of spectrum, too
Other technologies are challenging ITS spectrum in US and some coexistence is likely needed in China as well.
Conclusion: ITS spectrum (present & possible future) is subject of interest from different technologies

## Slide 12: Potential sharing between ITS and Wi-Fi in US
Docket 13-49 asked for comments about sharing part or all of the ITS band with unlicensed devices such as Wi-Fi
Current proposals only suggest sharing of lower 40MHz
Upper 3 channels would not be shared
FCC has done some testing
Unknown status of possible future R&O