## Slide 1
Motivation for Study on Enhancement for Disaggregated gNB Architecture
3GPP TSG RAN Meeting #80 RP-180833
La Jolla, USA, June 11 - 14, 2018
Agenda Item: 9.2.3
Document for: Discussion
Source: China Telecom, CATT , China Unicom

## Slide 2: Background
2
In Rel-15,high layer CU/DU split and CP/UP separation were standardized for disaggregated gNB deployment scenario. Based on the current standardization progress and new requirements in future NSA/SA network deployment, the enhancement for disaggregated gNB architecture should be studied in Rel-16 as follows:
Handover Enhancement
01
to reduce the interruption time during Intra-gNB-CU handover procedure
to introduce HO assistant information (e.g., Load Status report) provided by gNB-DU
Resource Utilization Improvement
02
to avoid the unnecessary resource utilization for inter-gNB-DU duplicated transmission/ fast re-transmission
User Experience Improvement
03
to Support of multiple Connection for disaggregated gNB architecture

## Slide 3: Handover Enhancement
To reduce the interruption time during
Intra-gNB-CU handover procedure
To introduce HO assistant information provided by
gNB-DU
Since NR cell would be deployed in HF with continuous coverage, the handover within one gNB-CU may happen frequently. The interruption time during intra-gNB-CU handover procedure would impact the system performance seriously.
How to reduce the handover interruption time for intra-gNB-CU scenario should be studied
For intra-gNB-CU/inter-cell handover, gNB-CU decides the target SpCell. Since gNB-CU doesn’t have the load status of each cell, gNB-CU may select a cell that is overloaded and the selected SpCell may be rejected by the gNB-DU.
In this case, extra delay for handover preparation would be introduced which would impact the overall performance of the handover procedure. If the handover is urgent, handover failure may happen since the suitable target SpCell could not be found promptly.

## Slide 4: Resource Utilization Improvement
For duplicated transmission within two gNB-DUs, duplicated resources would be allocated to the UE which maybe unnecessary, especially for DRB with AM mode.
For intra-gNB/ inter-gNB-DU fast re-transmission scenario, if some RLC PDU segments are lost in one leg, currently, the whole PDCP PDU will be re-transmitted in another leg. Similarly, in case of duplication transmission, currently, the discard mechanism only focus on PDCP PDUs which are in order delivered .
However, it is possible that other part of the data which share the same PDCP has already been transmitted successfully in the first leg SN and/or some PDCP PDUs are delivered to UE out of order in one leg. In this case, it is not necessary to re-transmit these data to save radio resources.
Inter-gNB-DU Duplicated Transmission/Fast Re-transmission
Further optimization of radio resource utilization for duplicated transmission and fast re-transmission should be considered

## Slide 5: User Experience Improvement
Support of Multiple gNB-DUs Connectivity
Currently, one gNB may include multiple gNB-DUs, it is not supported for one UE to connect to two or more gNB-DUs at the same time in EN-DC/NGEN-DC scenario.
However, considering the requirement of 5G,i.e.the target for peak data rate should be 20Gbps for downlink and 10Gbps for uplink, it is beneficial that UE could utilize the resources in two gNB-DUs to enable the high rate data transmission.
Support of Multiple gNB-CU-UPs Connectivity
Currently, one PDU session is offloaded by one gNB-CU-UP in CP/UP seperation scenario.
However, considering the scenario that one PDU session will include multiple QoS flows which has different QoS profile, even for one PDU session, it shall be allowed to offload to different gNB-CU-UP in order to provide better user experience and flexibity.
Another left open issue for CP/UP seperation is that currently the gNB-CU-CP can not get the flow control related infor from gNB-CU-UP/gNB-DU. However, in some cases, e.g., for multiple gNB-CU-UPs connected case, if outage happens at one gNB-CU-UP leg, the gNB-CU-CP should be informed, therefore, CU-CP can perform data forwarding and retransmitting from one UP to another available UP entity.
Support of multiple gNB-DUs connectivity and Multiple gNB-CU-UPs Connectivity should be considered.

## Slide 6: Objective of this Study Item
The objectives of this SI are to:
Identifying detailed solutions to reduce the interruption time during Intra-gNB-CU handover procedure
Identifying detailed solutions to introduce HO assistant information (e.g., Load Status report) provided by gNB-DU
Identifying detailed solutions to minimize the utilization of radio resource for inter-gNB-DU duplicated transmission /fast re-transmission.
Identifying detailed solutions to support multiple gNB-DUs connectivity for EN-DC/NGEN-DC scenario.
Identifying detailed solutions to solve the left open issues on CP/UP seperation.
Study the necessary protocol functions and/or messages related to the possible identified solutions.
Time Budget: Jun,2018~Dec,2018

## Slide 7
Thanks For
Your Attention