## Slide 1: Supporting UDC in NR in Rel-16
CATT, CMCC, MediaTek Inc.
RP-180915
3GPP TSG RAN WG Meeting #80
La Jolla, USA, June 11-14, 2018
Document for: Discussion
Agenda Item: 9.2.2

## Slide 2: Background
The WI on UDC in LTE is completed 99%.
CRs to 36.300, 36.323 and 36.306 are agreed and CR to 36.331 is endorsed which would be approved in September to avoid the specification clashing with NSA.
During RAN#79 meeting, it was proposed to support UDC in NR in Rel-15, but considering it was not so urgent, it was suggested to brought UDC in Rel-16.
In this contribution, we further propose to support UDC in NR in Rel-16.

## Slide 3: Motivation to support UDC in NR
Considering UDC can save more UL resources and reduce transmission latency in LTE which make LTE transmission more efficient, 5G also should provide similar effective transmission;
  LTE UDC adopt public domain DELFATE method, which is a RAN-agnostic solution. Similar performance gain can be observed in NR network.
UDC can improve voice service coverage since it can improve the SIP signalling transmission successfully in the edge of cell. Considering the high frequency 5G used, uplink link budget issue would become a more severe problem.
The E-UTRAN connecting to EPC (using LTE PDCP) with UDC may have higher throughput than the E-UTRAN connecting to 5GC (using NR PDCP) without UDC. To let 5G not worse than LTE, supporting UDC in 5G is a natural way.
Saving uplink resource is very important for practical networks.

## Slide 4: Objectives to support UDC in NR
To specify the signaling and procedures enabling operator control of the DEFLATE-based solution.
To specify the UDC header (at least including checksum) and, PDCP control signaling as necessary, in PDCP protocol.
To specify pre-defined dictionary (including standard and operator defined) corresponding signaling and procedures.

## Slide 5: Proposals
UDC is not only used for VoNR but also can be used for other services without encryption. In real markets, most APPs haven’t used any encryption in order to increase the APP efficiency (encryption is an additional process of an APP).
To save more uplink resource and increase the transmission efficiency, it is proposed:
Proposal 1: supporting DEFLATE based UDC in NR in Rel-16.
Considering too many SIs/WIs to be involved in Rel-16 and the scope of the UDC (refer to NR UDC WID RP-180916) is clear with small workload, it proposed:
Proposal 2: supporting UDC in NR can be completed under an agreed WI, e.g. Voice enhancement or other WI.