## Slide 1: Motivation for new WID on Further Enhanced LTE Support for Aerial Vehicles
Ericsson
RAN #80, La Jolla, CA, US, June 11 - 14, 2018
AI 10.2.2
RP-181049

## Slide 2: Preceding SI (RP-170779)
In RAN#75, the SI ‘Study on enhanced Support for Aerial Vehicles’ was approved in RP-170779.
SI conclusions found that LTE networks are capable of serving aerial UEs, but there may be challenges related to interference as well as mobility:
  These issues were identified to be scenario dependent
  The challenges become more visible when the density of the aerial UEs is high
In the SI, both implementation based solutions and solutions requiring specification enhancements were identified.
The SI further concluded that to serve aerial UEs more efficiently and limit the impact on terrestrial UEs, solutions for interference detection and mobility based on specification enhancements are beneficial

## Slide 3: Preceding WI (RP-172826)
In RAN#78, a WI on “Enhanced LTE Support for Aerial Vehicles” was approved in RP-172826.
This WI specified features that can improve the efficiency and robustness of terrestrial LTE network for delivering connectivity solutions more efficiently for UAVs.
These specified features include the following:
  subscription based identification
  height and location reporting based on triggering on height threshold
  interference detection based on measurement report triggering on an event where multiple cells’ RSRPs are above a threshold,
  flight path plan information via RRC from UE to eNB
  open loop power control enhancements were specified to mitigate UL interference on PUSCH.

## Slide 4: New WID on Further Enhanced LTE Support for Aerial Vehicles
The new WID on ‘Further Enhanced LTE Support for Aerial Vehicles’ aims to further enhance the Aerial UE support specified in Rel-15.
The Rel-16 WI is aimed at further enhancing Aerial UE support for existing cellular deployments as that is the most viable approach in most scenarios.
The objective is to specify the following improvements for further enhanced LTE support for aerial vehicles:
  Specify Idle mode mobility enhancements, (e.g., broadcasting height thresholds) [RAN2]
  Specify conditional handover to improve mobility performance (shall not be limited to aerial UEs) [RAN2, RAN3]
  Specify RRM parameter scaling enhancements such as faster tuning of RRM configuration for Aerial UEs, (e.g., faster than RRC signalling and/or based on UE height or airborne status) [RAN2]
  Specify enhanced flight path plan signalling for connected mode UEs [RAN2]
  Specify closed loop power control with increased step size of TPC command [RAN1]
  Study and if needed specify enhancements for UL interference mitigation for random access, e.g. Msg1/Msg3, power control [RAN1, RAN2]

## Slide 5: Idle Mode Mobility Enhancements
As automated flights are possible for drones, an aerial UE may be flying, taking-off and landing while in RRC IDLE.
Thus, it may be beneficial to broadcast for example a height threshold and to define flying mode states similar to mobility states. When connection is established, network could be informed early of UE’s flying mode.
Hence, the WI will specify Idle mode mobility enhancements, (e.g., broadcasting height thresholds) [RAN2]

## Slide 6: Conditional handover
In some scenarios, when the UE moves towards another cell than the serving cell, the handover will not be performed quickly enough and hence can lead to handover failure.
To address such mobility issues, conditional handover has been discussed allowing the eNB to send the handover command to the UE in advance and the UE executes the handover command when conditions, configured for the command, are fulfilled. This could be useful also for non-aerial UEs.
Hence, the WI will specify conditional handover to improve mobility performance (shall not be limited to aerial UEs) [RAN2, RAN3]

## Slide 7: RRM parameter scaling enhancements
In Rel-15, UE can be reconfigured with new RRM parameters once network receives height and interference report from the UE. However, in certain scenarios, this may result in too slow update of the parameters.
To update the parameters faster, two distinct reporting configurations, for example, can be configured to airborne and non-airborne UE statuses with parameter values suitable for airborne and non-airborne UEs, respectively. In this way, multiple parameters may be scaled by the UE to fit airborne and non-airborne statuses of the UE, and also reporting amount related parameters may be scaled .
Hence, the WI will specify RRM parameter scaling enhancements such as faster tuning of RRM configuration for Aerial UEs, (e.g., faster than RRC signalling and/or based on UE height or airborne status) [RAN2]

## Slide 8: Enhanced Flight Path Plan Signaling
In Rel-15, the flight path plan reporting is per network polling only.
In Rel-15 discussions, it was acknowledged that as UE may receive updates of the flight path plan via application layer, it is beneficial to allow UE to report updates of the flight path plan. This should however be done in a way that UE does not congest the UL and thus cause excessive UL interference.
Hence, the WI will specify enhanced flight path plan signalling for connected mode UEs [RAN2]

## Slide 9: Closed Loop Power Control Enhancements
In Rel-15 SI, closed loop power control enhancements were studied for UL interference mitigation.
It was identified that closed loop power control for aerial UEs needs to cope with potential fast signal changes in the sky since aerial UEs may be served by the sidelobes of the eNodeB antennas and increased step size of TPC command is beneficial.
Hence, the WI will specify closed loop power control with increased step size of TPC command [RAN1]

## Slide 10: UL Interference Mitigation for Random Access
In Rel-15 SI, it was acknowledged that UL interference on PRACH could be a problem although this issue was not evaluated in RAN1.
Specifically, the TR 36.777 states that when there is strong interference on PRACH resources, successful detection of PRACH can be degraded and the UE may transmit with maximum transmission power as a result of power ramping which may further increase the uplink interference. This may also increase false alarm probabilities.
Hence, the WI will study and if needed specify enhancements for UL interference mitigation for random access, e.g. Msg1/Msg3, power control [RAN1, RAN2]