## Slide 1: Summary of discussion on supported number of MIMO layers
Qualcomm, Vodafone
RP-181405
3GPP TSG RAN #80
La Jolla, CA, U.S.A., June 11 - 14, 2018
Agenda item 9.8

## Slide 2: Background
The following was discussed for 2-3 (last column) in the NR UE Features list
2-3 | PDSCH MIMO layers | 1. Supported maximal number of MIMO layers | 2-1 | Yes | Only one layer is supported | Type 3 | N.A. | N.A. |  |  | RAN1 | Candidate values: {1,2,4,8} FFS on the minimal layers for different band or band combination. | Proposal: For non-CA and non EN-DC cases: A UE is mandated to support 2 layers and on the bands where 4Rx is mandatory, A UE is mandated to support 4 layers

## Slide 3: Company proposals
Company | Text proposal for last column
AT&T | For non CA case, UE is mandated to support at least 4 MIMO layers on the bands where 4Rx is identified as mandatory and 2 MIMO layers on FR2. For EN-DC where NR is on FR2, UE is mandated to support at least 2 MIMO layers on FR2 CC. FFS on EN-DC where NR is on FR1 case.
Vodafone, Telecom Italia, Orange, Telefonica, Deutsche Telekom (note: text proposal aligns with RP-172788 “Mandatory 4Rx antenna performance for NR UE”) | On the bands where 4Rx is mandatory, A UE is mandated to support 4 MIMO layers for all operating scenarios (EN-DC, CA, non-ENDC/non-CA). For certain UE types/categories, some exceptions to this requirement may be applicable in future. On all other bands, a UE is mandated to support 2 MIMO layers.
Nokia | On the bands where 4Rx is mandatory, A UE is mandated to support 4 MIMO layers for all operating scenarios (EN-DC, CA, non-ENDC/non-CA). On all other bands, a UE is mandated to support 2 MIMO layers.

## Slide 4: Company proposals (cont.)
Company | Text proposal for last column
Intel | For non-CA and non EN-DC cases (i.e. single CC in NR SA) in DL: A UE is mandated to support 4 MIMO layers on the bands where 4Rx is mandatory. A UE is mandated to support 2 MIMO layers where 4Rx is not mandatory. FFS: EN-DC case on how many CCs (0, 1, 2,…) for LTE CA with non-CA for NR can be configured for the number of MIMO layers
OPPO | For non-CA and non-EN-DC cases: A UE is mandated to support 4 MIMO layers on the bands where 4Rx is mandatory. In FR1, UE is mandated to support at least 2 MIMO layers In FR2, UE is mandated to support 1 MIMO layer. Optional to support 2 MIMO layers (As a compromise, mandatory with capability signaling is also acceptable) FFS: EN-DC and CA cases

## Slide 5: Company proposals (cont.)
Company | Text proposal for last column
Qualcomm | For CA/EN-DC with single CC in NR, UE has to support 4 MIMO layers in the bands in which 4Rx is mandatory. For EN-DC with NR CA, the UE is allowed to support 2Rx with intra-band NR CA in the bands in which 4Rx is mandatory. Also add the following: Note: Mandatory means mandatory with capability signaling. It is not expected that there is a signaling change as a result of this (i.e. signaling remains to be defined as {1, 2, 4, 8} in every band, including FR1 and FR2.
vivo | For non-CA and non EN-DC cases On the bands where 4Rx is mandatory, a UE is mandated to support 4 MIMO layers. On the bands of FR2, UE is mandated to support 1 MIMO layer. On all other bands, a UE is mandated to support 2 MIMO layers. FFS: EN-DC cases and CA cases based on whether the corresponding DC/CA band-combinations supports 4Rx or not.

## Slide 6: Discussion outcome / Proposal
Text proposal for ‘last column’
For non-CA and non-EN-DC cases, it is mandatory with capability signaling to support at least 4 MIMO layers on the bands where 4Rx is specified as mandatory and at least 2 MIMO layers on FR2. For certain UE types/categories, some exceptions to this requirement may be applicable in the future. For CA and EN-DC: in FR2, it is mandatory with capability signaling to support at least 2 MIMO layers in the FR2 CC(s) In FR1, it is mandatory with capability signalling to support at least 2 MIMO layers in NR bands where 4Rx is not specified as mandatory. in band combinations with single NR CC in FR1, it is mandatory with capability signaling to support at least 4 MIMO layers for operation in the NR bands in which 4Rx is mandatory in band combinations with single NR CC in FR1, or with multiple NR CCs in FR1 where the sum of aggregated bandwidth for NR CCs ≤ the maximum specified channel bandwidth for 1 NR CC, it is mandatory with capability signaling to support at least 4 MIMO layers for operation in all NR CCs operated in bands in which 4Rx is mandatory and in which intra-band CA applies in band combinations with multiple NR CCs in FR1 where the sum of aggregated bandwidth from NR CCs > the maximum specified channel bandwidth for 1 NR CC, it is mandatory with capability signaling to support at least 2 MIMO layers for operation in all NR CCs operated in bands in which 4Rx is mandatory and in which intra-band CA applies Mandatory in all cases above means mandatory with capability signaling. It is not expected that there is a signaling change resulting from this (i.e. signaling remains to be defined as {1, 2, 4, 8} in every band, including FR1 and FR2.