## Slide 1
LG Electronics
Consideration on next approach
for 2Rx vehicular UE
3GPP TSG-RAN #82
Sorrento, Italy, 10th – 13th Dec., 2018
Agenda Item: 9.3.16
Document for : Discussion
RP-182307

## Slide 2: Background (1/2)
Study on 2Rx exception for vehicle mounted UE in Rel-15 is completed with following conclusion in RAN4[1]
  For Coverage
    Based on the results of the cell-edge performance evaluation, there was no indication for a degradation of the cell-edge coverage performance by using 2Rx vehicular UEs in bands where 4Rx is mandated.
  For UE distinction
    2 RX Vehicular UE can be distinguished based on conclusion 1+2+3+4
      Conclusion 1: “Declare and differentiate 2 RX Vehicular UE through 3GPP compliance testing via GCF/other certification organizations [9].
      Conclusion 2: RAN 4 agree on existing UE capability signaling for # of MIMO layers to differentiate 2 RX UE from 4 RX UE.
      Conclusion 3: Definition of Vehicular UE in TS 38.101-1 is needed.
      Conclusion 4: For Vehicular UE, network based identification is required for authorization purposes. The actual implementation of network based identification method does not impact 3GPP decision on 2 RX exception.

## Slide 3: Background (2/2)
LS has been sent to RAN with 5GAA CC’ed [2]
  To inform that all the objectives are resolved with conclusions as captured
Status Report is submitted to RAN#82 [3]
  The completion level is 100%
RAN4 CR[4] is provided to reflect SI conclusion [4],[5] into TS38.101-1
  The definition of vehicular UE in Section 3
    Vehicular UE: A UE which is integrated in a vehicle with externally radiating antenna for NR operating bands.
    NOTE: Integrated UE does not refer to other UE form factors placed inside the vehicle
  Add NOTE1 in Section 7
    NOTE 1:Four Rx antenna ports shall be the baseline for this operating band. The exception is allowed for vehicular UE in this operating band, for which the requirements with two Rx antenna ports can be applied. 2Rx vehicular UE typically has better antenna system gain than other UE [9].

## Slide 4: The follow-up actions
Based on the results in RAN4#89 and input in RAN#82 [1]~[5], the following should be considered as next steps
  RAN1 feature list on MIMO layer signaling
    Currently, # of MIMO layers in 4Rx mandated bands are 4. But vehicular UE with 2Rx exception can only have 2 MIMO layers at most even in 4Rx mandated bands. So this issue needs to be addressed when finalizing RAN1 feature list on # of MIMO layer.
  LS to 5GAA
    All the related discussions and conclusions on 2Rx exception for vehicular UE in RAN#82 need to be summarized and delivered to 5GAA as LS
  RAN2 CR
    RAN4 agreed the actual implementation of network based identification method does not impact 3GPP decision on 2 RX exception. So implementing RAN2 CR [6] needs to be concluded.
The follow-up actions are based on the assumption that RAN4 CR[4] has been approved in RAN#82

## Slide 5
[1] RP-182305 TR 38.826 v1.0.0; SI on 2Rx exception for NR vehicular UE , LG Electronics
[2] R4-1816775 LS on conclusion of “Study on evaluation for 2 RX exception in Rel-15 vehicle mounted UE for NR” , Samsung
[3] RP-182316 Status Report for SI: Study on evaluation for 2 RX exception in Rel-15 vehicle mounted UE for NR , Samsung
[4] RP-182306 Company CR on 2Rx exception for NR vehicular UE at FR1, LG Electronics, Volkswagen AG and Samsung
[5] R4-186771 WF on 2Rx exception for NR vehicle UE, Samsung, LG Electronics, Volkswagen AG
[6] RP-182622 draft CR for the addition of an SPID value for vehicle UE subscriber, Vodafone
References