## Slide 1
Motivation for WID proposal on
SRVCC from 5G to 3G
China Unicom, Telefonica, Huawei, Hisilicon
3GPP TSG RAN meeting #82
Sorrento, Italy, December 10-13, 2018
Agenda item: 9.1.2
RP-182419

## Slide 2: Background
The interworking between NR and UTRAN is not supported in 3GPP Rel-15 specification, leading to the lack of Voice Call Continuity from NR to UTRAN. This may cause problem to voice service, have impact on the user experience, when NR coverage is limited, Thus the voice service continuity from 5G to UTRAN shall be supported, in order to enable an MNO to offer a good service to its subscribers.

## Slide 3: Background
Support for voice service continuity between NG-RAN and 2/3G have been discussed in SA1, and the following requirements have been captured in after SA#79:
In principle, the 5G system shall support all EPS capabilities (e.g., from TSs 22.011, 22.101, 22.278, 22.185, 22.071, 22.115, 22.153, 22.173), however:
Voice service continuity from NG-RAN to GERAN shall not be supported,
Voice service continuity from NG-RAN to UTRAN CS should be supported,
Voice service continuity from GERAN to NG-RAN shall not be supported,
Voice service continuity from UTRAN to NG-RAN shall not be supported,
CS fallback from NG-RAN to GERAN shall not be supported,
CS fallback from NG-RAN to UTRAN shall not be supported,
seamless handover between NG-RAN and GERAN shall not be supported,
seamless handover between NG-RAN and UTRAN shall not be supported,
access to a 5G core network via GERAN or UTRAN shall not be supported,
Video service continuity between 5GS and UMTS shall not be supported,
IP address preservation for PS service when UE moves between 5GS and GSM/UMTS shall not be supported,
Service continuity between 5GS and CDMA2000 shall not be supported.

## Slide 4: Background
Based on the SA1 conclusions, an related SA2 Study Item was also approved in SA#79. The Study Item has been completed and solutions were recommended in TR23.756. It is clear that the following solutions will be supported:
Solution#1: Enable 5G SRVCC with existing mechanism, including 5GS Registration for SRVCC, Service Request procedure for SRVCC, Intra-5GS PS Handover procedure for SRVCC, and eSRVCC from 5G to 3G using ATCF enhancements. Normative work is expected to be reflected in TS 23.501, TS 23.502 and TS 23.216.
Solution#2: Indirect SRVCC Procedure to support SRVCC HO procedure from NG-RAN to UTRAN. Normative work is expected to be reflected in TS 23.216.
Solution#5: PDU Session Release after 5G-SRVCC procedure is adopted as conclusion. IMS service control is assumed to be transferred to the CS domain when UE moves to UTRAN cell due to 5G-SRVCC.
solution #9: Return 5GS after 5G SRVCC depend on UE implementation and no normative work is needed.
The Work Item for SRVCC from 5GS to 3G was approved at SA#81. The conclusions captured in TR 23.756 will be delivered into the Stage 2 specifications.

## Slide 5: Proposals in RAN#82
Proposal: It is proposed that RAN2 start a new work item for SRVCC from 5G to 3G.