## Slide 1: Consideration on IAB WI scope

## Slide 2: IAB WI focus: DL flow control
On uplink, there was no clear need for flow control because an IAB node can control all uplink resource.
However, on downlink, it was identified that an IAB node can be congested, which may lead to packet discard.
  Unnecessary packet discard should be avoided to provide stable service to upper layer.
UE-bearer granularity should be considered to support 1:1 bearer mapping in unified design.
IAB WI should focus on DL Flow control with UE-bearer granularity.

## Slide 3: IAB WI focus: Hop-by-hop ARQ
Hop-by-hop ARQ is selected in IAB SI.
However, as identified in SI phase, hop-by-hop ARQ cannot support lossless delivery without a new mechanism.
  A new mechanism should be studied to support lossless delivery using hop-by-hop ARQ.
IAB WI should focus on hop-by-hop ARQ with lossless delivery support.

## Slide 4: IAB WI focus: Backhaul RLF handling
If backhaul RLF occurs in the middle of the path from IAB donor to UE and this RLF cannot be recovered shortly, descendant IAB nodes and UEs cannot support QoS properly.
IAB nodes and UEs should recognize this RLF problem and have a chance to move to other IAB node to provide QoS appropriately.
IAB WI should focus on backhaul RLF handling.

## Slide 5: IAB WI focus: Bearer mapping
Bearer mapping at every hop is a basic function to support UE bearers in multi-hop IAB network.
N:1 bearer mapping allows an IAB node maintain a reasonable number of BH RLC channel.
Proper QoS handling at each hop is one of most important factors in an IAB WI.
QoS based bearer mapping should be considered to support proper QoS handling at every hop.
IAB WI should focus on QoS based N:1 bearer mapping in IAB node.

## Slide 6: IAB WI focus: LCID and LCG extension
The current LCID and LCG space is not enough to support 1:1 bearer mapping with finer granular QoS.
Especially, an IAB node which is close to the IAB donor should maintain lots of logical channels to support 1:1 mapping to all descendent UE bearers.
IAB WI should focus on LCID and LCG extension in IAB node.

## Slide 7: IAB WI focus: IAB UL scheduling
Increased latency due to multiple hops in an IAB network can adversely impact the performance of both control plane and user plane data transmission.
Current UL data scheduling is designed to support one-hop networks. It is not sufficient to satisfy end-to-end delay and provide QoS in an multi-hop IAB network.
Considering that the data received from the descendant node is relayed to the parent node, an efficient mechanism to support fast UL scheduling in IAB node is required.
IAB WI should focus on UL scheduling enhancement in IAB node.

## Slide 8: Proposals for IAB WI scope in RAN2
Following objectives should be included in RAN2 work scope
  DL Flow control with UE-bearer granularity
  Hop-by-hop ARQ with lossless delivery support
  Backhaul RLF handling
  QoS based N:1 Bearer mapping
  LCID and LCG extension
  UL scheduling enhancement for IAB node