## Slide 1: On Beam Correspondence Optionality
Intel
Agenda item: 9.6
Document for: Approval
TSG-RAN Plenary meeting #82 RP-182495
Sorrento, IT, 10 – 13 December 2018

## Slide 2: Observations
In RAN4#89, as one of outcomes of joint AH between RAN1 and RAN4, 5 alternatives for BC optionality [1] are summarized as
Alt.1:
  Mandatory with capability signalling
  No relaxation on spherical coverage and minimal EIRP
Alt.2:
  Optional with capability signalling
  No relaxation spherical coverage and minimal EIRP
Alt.3:
  Mandatory with capability signalling
  Introduce a new UE capability to indicate whether UE request the relaxation based on existing spherical coverage and minimal EIRP.
Alt.4:
  Mandatory/optional per power class
  PC3 UE is mandated to support beam correspondence with certain relaxation
Alt.5:
  Beam correspondence and uplink beam management can not be both optional.
  UE needs to report to support either beam correspondence (FG 2-20) or uplink beam management (2-30) or both.

## Slide 3: Observations
When deriving the minimum peak EIRP and spherical coverage requirements[2]
  The best Tx beam is assumed
  No beam correspondence under consideration
  Tx beam selection is not based on DL measurement
In RAN4#89, it has been agreed that UE with beam correspondence should comply with existing minimum peak EIRP and spherical coverage requirements
  It is UNREALISTICLY assumed that the best Tx/Rx beam can always be identified based on beam correspondence .
  No implementation margin and imperfection is allowed!

## Slide 4: Implementation Imperfection of Beam Correspondence (1)
Imperfect UL/DL beam reciprocity:
  In real implementation, Tx beam pattern not always identical with the selected Rx beam pattern
    Antenna impedance can be different for Tx and Rx
    Tx and Rx may use different physical phase shifter implementations, causing Tx and Rx beam phase/pattern mismatch
  Perfect reciprocity between UL and DL beam pairs cannot be taken for granted

## Slide 5: Implementation Imperfection of Beam Correspondence (2)
Rx beam selection error:
  Rx beam selection - typically based on RSRP measurement of DL signals
    Relative SS-RSRP accuracy requirements: -6dB for normal condition / -9dB for extreme conditions
    Large estimation error makes it hard to guarantee the best Rx beam always be idenfied
  The best Tx beam - can not be guaranteed accordingly if no best Rx beam selected
  No relative RSRP accuracy specified based on CSI-RS, the corresponding performance is unclear

## Slide 6: Implementation Imperfection of Beam Correspondence (3)
Codebook mismatch between DL measurement and Tx transmission:
  SSB – can simultaneously serve at least two purposes
    beam refinement for beam correspondence purpose
    RSRP/RSRQ/SINR measurements for mobility purpose
  To fulfill existing RRM requirements, SSB based Rx sweeping is expected to
    covers the full sphere for both serving and neighboring cell measurement
    have limited RX codebook size to satisfy measurement delay constraints
      For example, it is defined that up to 24 SMTC occasions are allowed for cell measurement. Simulations suggest ~5 SMTC occasions are needed per Rx beam.
      This implies up to 5 Rx beams can be chosen for Rx beam sweeping.
  It is not straigthfoward to ensure the same codebook used for Tx beam refinement and SSB-based DL measurement all the time

## Slide 7: Proposals for Beam correspondence requirements
Proposal: One of two following options should be selected for beam correspondence requirements.
Option 1: Beam correspondence shall be an optional feature if there is no margin in spherical coverage and minimum peak EIRP requirements
Option 2: If beam correspondence feature is mandated, UE capability signaling should be introduced to allow EIRP tolerance if needed. It is FFS on the exact signaling definition.
  Depending on UE capability, a margin should be specified to accommodate EIRP tolerance (e.g. within [2] dB tolerance) in spherical coverage and minimum peak EIRP requirements

## Slide 8: Reference
R1-1814275, LS on beam correspondence related features, AT&T. RAN1#85, Spokane, US. Nov. 2018
R4-1812197, “On Beam Correspondence requirements”, Intel. RAN4#88bis, Chengdu, China. October, 2018