## Slide 1: On the NOMA Study outcome
Ericsson
RP-182577
Agenda Item: 9.3.4

## Slide 2: NOMA study objectives & results
NOMA study objectives (RP-181403) include the following mechanisms impacted by NOMA operation:
  Transmission schemes
    Including DMRS enhancements
  Receivers
  Procedures needed to support NOMA
    Including synchronous and asynchronous operation
Not all mechanisms were studied in detail, and most were link level studies
  Many hundreds of link level simulations of transmission schemes and corresponding receivers were carried out and captured in the TR
    35 cases were studied, some with as many as 125 different BLER curves
    14 companies provided link level results for the TR
    Link level parameters were generally well aligned among companies, allowing easy comparison
  Tens of system level simulations of transmission schemes and corresponding receivers were carried out and captured in the TR
    37 different sets of NOMA vs. baseline results were provided
    8 companies provided results
    Widely different parameter sets were used, and with different baselines, making comparisons intractable
      Baselines used linear or advanced receivers, while NOMA used advanced receivers
      Different numbers of slots or numbers of PRBs were used for baseline and NOMA and between companies
      Different amounts of HARQ retransmissions were used in different scenarios and between companies
      Etc.
  Example DMRS enhancements were simulated, but not really studied
    A single configuration was generally studied by a company at 3 kmph,
    Alternative designs, higher speeds, sensitivity to impairments, etc., were not considered
  Asynchronous operation (with 0..1.5 CP timing offset) had link sims from 3 companies, while all 13 companies simulated synchronous operation
    Preamble+data operation for use with asynchronous operation was simulated by one company (at link level)

## Slide 3: System level performance
MU-MIMO can outperform or underperform NOMA according to how it is configured
  NOMA with e.g. 4x spreading requires 4x more PRBs per UE –or- 4x higher code rate
  MU-MIMO therefore can have 4x fewer UEs / PRB, allowing more spatial interference suppression for a given number of Rx antennas
    Breaking PRBs into groups improves MU-MIMO performance substantially
Packet drop rate statistics are highly sensitive and not indicative of user experience over a cell
  Curves are very flat, so small changes in drop rate result in large changes in packet arrival rate
    Some results* show going from 1% to 2% packet loss results in 200% change in packet arrival rate
  Cell throughput differences can be small at a given arrival rate
    In example shown, arrival rate for 4 group MU-MIMO vs. NOMA is 56% better at 1% drop rate, while its cell throughput is 6% better than NOMA at 1700 packets/sec/cell.
*NOMA curve in figure 2a of R1-1812175
NOMA & MU-MIMO Cell Throughput @ 1700 packets/sec/cell Offered Load |  | 
4 Group MU-MIMO | NOMA | 1 Group MU-MIMO
1.39 Mbps/cell | 1.32 Mpbs/cell | 1.28 Mbps/cell
6% Gain | 0% (reference) | -3% Gain
Assumptions:
Embedded link level simulator with real channel estimation used (L2S mapping not needed)
4 Rx, 12 PRBs occupied, 1 slot transmission, 75 byte TBS
Details:
2%
56%

## Slide 4: Link Level Performance
1.3 dB NOMA Loss
3.0 dB NOMA Loss
0.5 dB NOMA Gain
1.3 dB NOMA Gain
1.0 dB NOMA Loss
3.7 dB NOMA Loss
Assumptions:
WSMA: spreading length 4, TDL-C, MMSE-SLIC
‘ICE’ == Ideal channel estimation
‘RCE’ == Realistic channel estimation
Additional results & details in R1-1813258
NOMA vs. MU-MIMO performance is a function of BLER and overloading
  In ideal conditions, NOMA can be better or worse than MU-MIMO, depending on the number of UEs
With realistic channel estimation in multipath and with 2Rx, NOMA can perform worse than MU-MIMO

## Slide 5: Conclusions
No clear gain from NOMA over Rel-15 mechanisms in studied scenarios
  Link level results from many companies in a large number of conditions show no gain over Rel-15 techniques
    All NOMA schemes, including those supported by Rel-15, perform similarly at link level in key conditions
  System simulations do not show conclusive gain
    Baselines not aligned and/or not the best of Rel-15
      Inefficient resource utilization of baseline was used in in some cases: NOMA was 3-5x higher
    Commonly used packet drop rate metric is highly sensitive & not indicative of user experience over a cell
    Not all companies show gains from NOMA
Need for DMRS enhancements not yet shown
  DMRS design enhancements were not a focus of NOMA study;
  Need for more ports vs. Rel-15 (including with different scrambling IDs) not clear
  DMRS limitations driven by NOMA spreading: spreading by N means N x fewer DMRS resources
  If NOMA does not benefit capacity, then DMRS enhancements are not motivated by NOMA
Benefits of preamble+data structures not established for NOMA
  Few results available
  Higher layer packets generally segmented into multiple slots in NOMA simulations; leads to high overhead if preamble is always used
  Use case of asynchronous operation driving interest in preamble+data in scenarios studied is unclear
    Round trip time is less than CP length except for very large cell
    Unclear why Rel-15 procedures to maintain and recover timing alignment are insufficient