## Slide 1: Motivation for SI on 6 -24 GHz frequency range
3GPP RAN#82 RP-182618
Sorrento, Italy

## Slide 2: Motivation 1/2
NR system should support frequencies up to 100GHz according to the WI description
So far NR work has been done for two frequency ranges, <6GHz and 24-52.6GHz
  LTE/NR-U SI has been done for up to 7.125GHz, hence this SI does not need to include those frequencies
  Also, a RAN SI is working on frequencies >52.6GHz
7.125-24GHz is a large spectrum range, which applicable RF characteristics (conducted and OTA) and regulatory aspects have not been studied yet
Based on RAN e-mail discussions, at least the following frequency ranges have operator interest
Frequencies of interest between 7.125 – 24 GHz |  | 
Company | Frequency range [GHz] | Region/Country
Dish Network | 12.2 - 12.7 | Region 2/USA
Orange | 7.125 - 8.5 | Region 1/Europe
Orange | 21.4 - 22 | Region 1/Europe
Etisalat | 10.7 - 11.7 | Region 1/MENA

## Slide 3: Motivation 2/2
A completely new & large frequency range requires significant effort
  mmWave was also studied in a release before the WI in Rel-15
Study on Applicable RF characteristics
  Identifies the impact to existing frequencies (FR1, FR2)
  Allows equipment vendors time for an analysis on the development
  Allows test equipment vendors to consider this in their FR1 and FR2 design
RAN5 can take the outcome into account in the existing TS 38.5xx conformance specifications by Rel-17 Band WIs

## Slide 4: Proposal
Study the basic characteristics for the 7.125-24GHz frequency range in Rel16
  Regulatory landscape survey
  Boundary frequency for conductive/OTA requirements, and related boundary conditions
  Basic RF characteristics evaluations for chosen frequency ranges
  Co-existence analysis, preferably around the boundary frequency
RAN4 study as no impacts for other WG’s are foreseen

## Slide 5
THANK YOU!