## Slide 1: WF on Beam Correspondence
Samsung
RP-182780
3GPP TSG RAN meeting #82
Sorrento, Italia, December 10 – 13, 2018

## Slide 2: Proposal
Beam correspondence is UE mandatory with capability signaling
RAN4 to define details of the beam correspondence requirements given in the next slide which needs to be decided in RAN#82
Remove the contents of section 6.6.4 of the big CR to 38.101-2 in RP-182359
No change on the existing RAN4 agreement on minimum peak EIRP and spherical coverage requirements in section 6.2.1.3
RAN4 to revise the test procedure for minimum peak EIRP and spherical coverage requirements so that the UE may rely on uplink beam sweeping during the test based on OEM declaration among the followings:
  Using the downlink reference signals only
  Using the downlink reference signals and uplink beam sweeping
Beam correspondence requirement is considered to be fulfilled if
  the UE meets the minimum peak EIRP and spherical coverage requirements without the uplink beam sweeping and beam correspondence tolerance requirements
  the UE meets the minimum peak EIRP and spherical coverage requirements with the uplink beam sweeping and beam correspondence tolerance requirements
The UE that passes minimum peak EIRP and spherical coverage requirements without beam sweeping does not need to be tested against the BC tolerance requirement in the next slide

## Slide 3: Beam correspondence tolerance requirements
RAN4 should specify the procedure and tolerance requirement for beam correspondence as follows
  For each of the test points in the grid, two EIRP should be calculated.
    EIRP1 is calculated based on the beam the UE chooses autonomously (corresponding beam) to transmit in the direction of the incoming DL signal. Procedure is based on what is described in section 5.2.1.3.7 of TR38.810 (R4-1816258)
    EIRP2 is the best EIRP (beam yielding highest EIRP in a given direction) which is based on UL beam sweeping or TE scan
      RAN4 should specify the procedure how the best EIRP is defined and derived
    Delta EIRP = EIRP2-EIRP1
    The test grid points where beam correspondence is verified are the grid points where the UE meets the spherical coverage requirements as specified in 6.2.1.3 of TS38.101-2
  The Delta EIRP CDF is obtained from the Cumulative Distribution Function (CDF) computed using Delta EIRP from all test points.
    For power class 3 UEs which support beam correspondence in single FR2 band, the requirement is fulfilled if the UE’s corresponding UL beams satisfy the following conditions
      [X]-percentile of delta EIRP CDF is no more than [Y] dB
    RAN4 to choose X between 80 and 100 by RAN#83
    RAN4 to choose Y by RAN#84
  The presence of both SSB and CSI-RS signals is assumed and Type D QCL is maintained between SSB and CSI-RS.
    The presence of both SSB and CSI-RS signals is defined in either RAN4 or RAN5 specs.

## Slide 4: Decision points for beam correspondence
Decide whether to task RAN4 to decide whether there will be one or multiple tolerance level(s) by RAN#84
Decide one of the following two alternatives for the UEs who supports the beam correspondence
  Alt1: introduce an additional capability signaling support for a UE that meets the beam correspondence requirement with the uplink beam sweeping to indicate it needs the uplink beam sweeping support
  Alt2: redefine the meaning of the existing UE feature 2-20 capability signaling
    UE that meets the requirement without the uplink beam sweeping should set the bit to 1
    UE that meets the requirement with the uplink beam sweeping should set the bit to 0