## Slide 1: WF on Beam Correspondence
Samsung, Apple, Nokia, Intel, ZTE, Sanechips, Qualcomm, MediaTek, Panasonic, Verizon, CATT, AT&T, OPPO, CMCC, Huawei, HiSilicon, CAICT, vivo, LG Electronics, KT Corp.
RP-182879
3GPP TSG RAN meeting #82
Sorrento, Italia, December 10 – 13, 2018

## Slide 2: Proposal
Clarify in TS 38.306 that beam correspondence (UE feature 2-20) is applicable only for FR2
Beam correspondence is mandatory with the capability signaling definition as below (UE feature 2-20)
  UE that fulfills the beam correspondence requirement without the uplink beam sweeping shall set the bit to 1
  UE that fulfills the beam correspondence requirement with the uplink beam sweeping shall set the bit to 0
Uplink beam management (UE feature 2-30) is UE optional with capability signaling
  UE feature 2-30 shall be set to 1 if UE feature 2-20 is set to 0
  For the UE meeting the minimum peak EIRP and spherical coverage requirements without the uplink beam sweeping, the uplink beam management (UE feature 2-30) is optional
RAN4 to define details of the beam correspondence tolerance requirements given in the next slide
Remove the contents of section 6.6.4 of the big CR to 38.101-2 in RP-182359
No change on the existing RAN4 agreement on minimum peak EIRP and spherical coverage requirements in TS 38.101-2 section 6.2.1.3
RAN4 to revise the test procedure for minimum peak EIRP and spherical coverage requirements so that the UE may rely on uplink beam sweeping during the test based on OEM declaration among the followings:
  Using the downlink reference signals only
  Using the downlink reference signals and uplink beam sweeping
Beam correspondence requirement for all UEs consists of three requirements as follows:
  Req1: Minimum peak EIRP requirement
  Req2: Spherical coverage requirement
  Req3: Beam correspondence tolerance requirement
The UE meeting Req1 and Req2 without the uplink beam sweeping is considered to have met Req3
The UE meeting Req1 and Req2 with the uplink beam sweeping shall be tested against the beam correspondence tolerance requirement (i.e., Req3) in the next slide

## Slide 3: Beam correspondence tolerance requirements
RAN4 should specify the procedure and a single tolerance level for beam correspondence by RAN#84 as follows
  For each of the test points in the grid, two EIRP should be calculated.
    EIRP1 is calculated based on the beam the UE chooses autonomously (corresponding beam) to transmit in the direction of the incoming DL signal. Procedure is based on what is described in section 5.2.1.3.7 of TR38.810 (R4-1816258)
      No uplink beam sweeping is assumed
    EIRP2 is the best EIRP (beam yielding highest EIRP in a given direction) which is based on UL beam sweeping or TE scan
      RAN4 should specify the procedure how the best EIRP is defined and derived
    Delta EIRP = EIRP2-EIRP1
    The test grid points where beam correspondence is verified are the grid points where the UE meets the spherical coverage requirements as specified in 6.2.1.3 of TS38.101-2
  The Delta EIRP CDF is obtained from the Cumulative Distribution Function (CDF) computed using Delta EIRP from all test points.
    For power class 3 UEs which support beam correspondence in single FR2 band, the requirement is fulfilled if the UE’s corresponding UL beams satisfy the following conditions
      [X]-percentile of delta EIRP CDF is no more than [Y] dB
    RAN4 to choose X between 80 and 100 by RAN#83
    RAN4 to choose Y by RAN#84
  The presence of both SSB and CSI-RS signals is assumed and Type D QCL is maintained between SSB and CSI-RS.
    The presence of both SSB and CSI-RS signals is defined in either RAN4 or RAN5 specs.