## Slide 1: Motivation for study on device to device proximity services in NR
CATT
RP-190306
3GPP TSG RAN WG Meeting #83
Shenzhen, P. R. China, Mar. 18th -21st, 2019
Document for: Discussion
Agenda Item: 9.1.2

## Slide 2: LTE D2D background
D2D is specified in LTE to meet the proximity service requirements listed in TS22.278, mainly includes:
  R12 D2D
    ProSe device to device discovery within network coverage;
    ProSe device to device broadcast communication;
  R13 eD2D
    Support D2D discovery for partial and out of network coverage;
    Support D2D discovery in the presence of multiple carriers and PLMNs;
    Enhancements on D2D communication to support L3-based UE-to-network relay;
    Enhancements on D2D communication to support priority of different groups.
Observation 1: LTE D2D has been specified to meet the proximity service requirements listed in TS22.278.

## Slide 3: Proximity service requirements in NR
      Observation 2: 5G D2D should not only consider the proximity service requirements listed in TS22.278, but also the requirements listed in TS22.261 and TS22.125.
Spec | Requirements
TS22.278 | D2D discovery for both commercial and PS services should be supported; D2D communication should be supported at least for PS services.
TS22.261 | UE-to-network relay should be supported: Connection between remote UE and relay UE can be 3GPP RAT or non-3GPP RAT； UE using simultaneous indirect and direct network connection should be supported; Connection between remote UE and relay UE can be licensed or unlicensed band; 5G system with satellite access should be considered.
TS22.125 | D2D broadcast communication should be supported for UAV: Compared with Rel-16 V2X, higher relative speed, e.g., up to 320 km/h, should be considered.

## Slide 4: Proximity service supporting status in SA2
A new SID on system enhancement for proximity based services in 5GS is already agreed on SA2 meeting#131:
  Suppport of one-to-many direct communication including out-of-coverage;
  Support of one-to-one direct communication including out-of-coverage;
  Support of UE-to-Network Relay (including QoS aspects);
  Support of direct discovery including out-of-coverage;
  System enhancement to support NCIS related service requirements.
Observation 3: SA2 already agreed to study the proximity services enhancements.

## Slide 5: Proximity service supporting status in RAN
In Rel-15, NR D2D is not specified.
In Rel-16, V2X SID is studied and its main objectives include:
  Sidelink design
    Study the support of sidelink unicast, sidelink groupcast and sidelink broadcast
    Study NR sidelink physical layer structures and procedure(s)
    Study sidelink synchronization mechanism
    Study sidelink resource allocation mechanism
    Study sidelink L2/L3 protocols
  Uu enhancements
  Uu based sidelink resource allocation
  RAT/Interface selection
  QoS management
  Coexistence

## Slide 6: Proximity service supporting status in RAN
      Observation 4: Rel-16 V2X is an incomplete D2D system, which only supports sidelink communication.
NR proximity service requirements | Rel-16 V2X status | Should be included in R17 D2D SI?
D2D discovery | Not supported | Yes
UE-network relay | Not supported | Yes Remote UE/relay UE uses licensed or unlicensed band; UE can be with indirect and direct network connection mode simultaneously ; Satellite access, e.g., relay UE Uu interface with satellite access .
D2D communication Max communication range: 600m(UAV)； Max message frequency: 10 message/s; Max end-to-end latency: 100ms; Maximum relative speed 320km/h(UAV). | Supported Max communication range: 1000m; Max message frequency: 50 message/s; Max end-to-end latency: 3ms; Max relative speed: 250km/h. | Yes The possible enhancements should be considered, e.g., support the maximum relative speed up to 320kmph for UAV.

## Slide 7
Sidelink discovery
  Study NR sidelink physical layer structures and procedure(s) ;
  Study sidelink synchronization mechanism;
  Study sidelink resource allocation mechanism;
  Study sidelink L2/L3 protocols.
Sidelink communication
  Identify the different requirements compared with R16 V2X and if any, study the potential enhancements.
UE-to-network relay
  Identify the scenarios for UE-to-Network relay;
  Identify the architecture, protocol stack and procedure(s) for UE-to-network relay.
Proposal: NR D2D SI should be involved in Rel-17 scope in order to meet the requirements of proximity services.
Objectives of R17 D2D SI