## Slide 1: Motivation for Supporting Local Location Management Component (LMC) in RAN in NR Rel-16
CATT, CMCC, CAICT
RP-190308
3GPP TSG RAN WG Meeting #83
Shenzhen, P.R.China, Mar. 18th -21st, 2019
Document for: Discussion
Agenda Item: 9.3.13

## Slide 2: Back ground
SA2 conclusion on local LCS management function in NG-RAN which attempt to resolve “Key Issue 3: Support of low latency and high performance LCS”:
  23.731-2.0.0: “NG-RAN node enhanced with the support of location management functionality may be selected to perform UE positioning locally in the RAN under the condition that RAN WG(s) concludes that NG-RAN supports location management functionality.”
  23.731-2.0.0 section 7.8: “allowing location management functionality supported in NG-RAN, as supported by Solution 15, 23, 26 and 28.”

## Slide 3: RAN2/RAN3 conclusion on architecture
RAN2 discussed this issue for two meetings and its conclusion is captured in R2-1902478:
  Regarding location management functionality in RAN, RAN2 conclude that this option is recommended for normative work, provided the concerns (as described in subclause 9.3.1) raised in the study phase are addressed.
RAN3 discussed this issue for a few minutes and its conclusion is captured in R3-191089:
  Regarding location management functionality in RAN, RAN3 could not reach a common understanding on any recommendation.
Observation1: RAN2 has already studied and analyzed the architecture with LMC in RAN and recommended to support LMC in RAN in NR positioning in Rel-16.
Observation2: RAN3 has no enough time to discuss the architecture with location management functionality in RAN.

## Slide 4: Operators requirements and Proposals
Requirements of operators:
  Low latency and high performance are required
  To improve the utilization rate of radio resources through the dynamic coordination of position resources
  Deployment consideration: some operators prefer distributed location management functionality in RAN
Proposals:
RAN3 to further analysis and study the architecture with local location management component in RAN in NR positioning WI.