## Slide 1: NR enhancements for Advanced Sleep Modes
Orange
3GPP RAN #83
March 2019
Shenzhen, China
Agenda Item 9.1.2
RP-190326

## Slide 2: Context: What are Advanced Sleep Modes (ASM)?
  We can define Advanced Sleep Modes as “long sleep durations” for base stations to switch-off transmission elements and save power consumption
  ASM is the key mechanism to fulfill the “Zero Load - Zero Watt” target
  4 levels of sleep modes have been defined by IEEE with increasing sleep time and depth
  3GPP Rel15 enables these long sleep durations (until SM3) by specifying different possible SS Burst set periodicities, from 5ms to 160ms (default periodicity is 20ms)

## Slide 3: SSB periodicities: current Rel15 specifications
  In NR, periodicities higher than LTE have been agreed (LTE = 5ms default periodicity), with a default periodicity of 20 ms.
  Two mechanisms have been specified:
    1) For Cell Selection
      SS Block default periodicity (expected by UE for initial access): [20 ms]
      Signaling periodicity remains configurable and be set to any value among [5, 10, 20, 40, 80, 160 ms]
    2) For Cell Re-selection
    Intra-frequency cell reselection: a single SSB periodicity value is broadcasted within NR SIB2, referred to as “smtc” of type SSB-MTC (as described in TS 38.331)
    Inter-frequency cell reselection: a single SSB periodicity value is broadcasted within NR SIB4 per frequency, referred to as “smtc” of type SSB-MTC (as described in TS 38.331)
    Inter-RAT cell reselection (4G to 5G): a single SSB periodicity value is broadcasted within the LTE SIB24 to assist inter-RAT cell reselection. The single value is referred to as “measTimingConfig” in SIB24 per frequency (as described in TS36.331)

## Slide 4: SSB periodicities: limitations with Rel15 specifications
  First limitation: long cell selection & reselection time to camp on the expected 5G cell
    5G cells set with higher periodicities than default (i.e. > 20 ms) may be missed by the UE in cell selection, in which case UEs may need to select another 5G or 4G cell before re-selecting to the best 5G cell.
    The cell reselection process takes time. The UE will need to decode the SIBs related to cell reselection (SIB3 and SIB4 in 5G, SIB24 in 4G).
    A typical case would be for co-located 4G / 5G deployment:
      UE misses the 5G cell
      UE selects the co-located 4G cell (or a co-located 5G cell on another band)
      UE reads SIB24 of the 4G cell (or SIB4 in case of 5G in inter-frequency) and reselect the co-located 5G cell

## Slide 5: SSB periodicities: limitations with Rel15 specifications
  Second limitation: lack of granularity at cell level
    Only a single value of SSB periodicity is a given in the SIB, within the list of common parameters.
    There are no neighbor specific parameters to differentiate cells with different SSB periodicities.
    This incurs an overall increase of the SSB scanning complexity at the UE. Indeed, the UE should look for the SSB of all neighbor cells assuming the highest SSB periodicity, i.e. if only one cell is set to 160ms and the other at 20ms, the UE will have to scan all cells with the assumption of 160 ms periodicity.

## Slide 6: SSB periodicities: proposed enhancements (1)
  Proposed enhancement for cell selection to target a specific cell
  The cell selection of the target 5G cell could be more efficient if the UE was instructed immediately during the cell selection process, while reading SIB1, that it should look for a specific 5G cell.
  This enhancement is particularly useful for co-located deployments, with only the target 5G cell co-located with a 4G or 5G cell on another band. Given the scarce resources of SIB1, it is not expected in practice to declare more than 1 or 2 target cells.
    More precisely, it is proposed to add the following fields:
      For inter-RAT more efficient cell selection from 4G, within LTE SIB1, and for more efficient inter-frequency cell selection from 5G, within NR SIB1:
        The DL carrier frequency of the target cell(s) identified by its GSCN
        The Physical Cell Id of the target cell(s)
        The SSB periodicity of the target cell(s)
        In case of synchronous deployment between the source cell and the target cell, the following field will be added:
          The time location(s) of the SSB of the target cell(s)

## Slide 7: SSB periodicities: proposed enhancements (2)
  Proposed enhancement for cell reselection with granularity at neighbor cell level
  The cell reselection process could be accelerated if the UE was instructed that only specific cells are set with SSB periodicities higher than the default value of 20 ms.
  Indeed, if only 1 neighbor cell is set with for instance 160 ms, and others set to 20 ms, the scanning process could stop as soon as the cell with 160 ms periodicity is decoded (as long as this time is greater than 20 ms)
    More precisely, it is proposed to add the following fields:
      For inter-RAT cell re-selection from 4G, within LTE SIB24, for intra-frequency cell re-selection from 5G, within SIB3, and for inter-frequency cell re-selection from 5G, within SIB4, for each neighbor cell identified by its Physical Cell Id:
        The SSB periodicity of the target cell(s)
        In case of synchronous deployment between the source cell and the target cell, the following field will be added:
          The time location(s) of the SSB of the target cell(s)