## Slide 1: Motivation for new WI on Direct data transfer in Inactive
3GPP TSG RAN #83
Shenzhen, China, 18 - 21 Mar 2019
Agenda Item: 9.1.2
RP-190490

## Slide 2: Background: Inactive state
Rel-15 INACTIVE State
  Provides much faster transition to connected
  Fewer signalling compared to Idle to Connected
  Possible to achieve about [30ms] transition
2 step RACH (Rel-16) can be applicable for Resume
  Reduce delay of 4 step RACH
  Msg A is expected to be the same as msg 3
    Resume request and Release expected to be used
    No reduction in number of messages or signalling sequence expected
    Overall concepts of INACTIVE re-used
    UE transitions to CONNECTED, even if it is just for transmission of data and back to Idle

## Slide 3: Direct data transfer in INACtive
Key aspects
  Resume Request/RRCRelease (to suspend) signalling to be avoided
    Two step could be used to further improve performance
      UE sends data in msg A of 2 step RACH
    UE may not fully transition to CONNECTED if there is no further data to send
  Data to be sent in same cell or within an RNA
  Data to be sent with security (both integrity and ciphering)
  Other optimisations can be considered
    Avoid Paging in the downlink

## Slide 4: Key benefits
Reduced latency, signalling and power consumption
  UE can send data directly and immediately go back to Suspend or stay connected
  Avoid multistep process of Resume procedure before data transmission
  Avoid RRC connection release with Suspend configuration related signalling
  Security to be supported for data, including Integrity protection and ciphering
  Downlink Paging optimisation to allow similar enhancements for DL traffic