## Slide 1: WF for NR RF requirement work continuation in Rel-16
Nokia, Nokia Shanghai Bell
3GPP TSG RAN #83 RP-190741
Shenzhen, CN, 18 – 21 March, 2019

## Slide 2: References
[1] R4-1902216, WF on UE RF spec scope in Rel-15, Qualcomm
[2] RP‑190455, NR requirement work continuation in Rel-16 Nokia, Nokia Shanghai Bell
[3] RP‑190253, New WID: Add support of NR DL 256QAM for FR2 China Telecomunication Corp
[4] RP-190255, New WID: Generic requirements for NR FR1 UL intra-band contiguous CA in Rel-16 China Telecomunication Corp.
[5] RP‑190386, New WI proposal: Intra-band non-contiguous CA requirements for FR1 Huawei, HiSilicon
[6] RP‑190356, New WID on Supplemental uplink usage of FR2 spectrum (SA and NSA) , Apple Inc.

## Slide 3: Objectives for Rel-16 RF requirement continuation work for FR1
Complete UE requirements for almost contiguous allocations for CP-OFDM UL for FR1, which is optional feature UE requirements for Intra-band contiguous DL CA for FR1
UE requirements for Intra-band non-contiguous DL CA for FR1
  Including generic and band specific requirements for intra-band non-contiguous CA in n77 and n78
    Corresponding CA configuration will be removed from basket WID
UE requirements Intra-band contiguous UL CA for FR1
UE requirements Intra-band non-contiguous UL CA for FR1
Study if UE intra-band EN-DC MPR/A-MPR requirements can be improved
  Define detailed objectives in RAN#84
  This study will not started until detailed objectives are defined in RAN#84

## Slide 4: Objectives for Rel-16 RF requirement continuation work for FR2
NR DL 256QAM for FR2
  Phase 1: Continue and complete the feasibility and performance benefit study to identify applicable scenarios.
  Phase 2 : Specify BS and UE requirements for NR DL 256QAM for FR2 if applicable scenarios and feasible requirements are identified
Enhancements methods for avoiding radio link failures and connection releases due to significant and unpredictable UE P-MPRs due to the FR2 UE RF exposure compliance reasons
  This work is started after RAN#84 when the Rel-15 requirements are completed
FR2 UE Beam Correspondence requirements for PC1, PC2 and PC4: RAN#84 in June will discuss and decide how to handle this
FR2 UE Beam Correspondence requirements to ensure that UE performs beam correspondence based on DL reference signal (SSB or CSI-RS) configured by the network
  This work is started after RAN#84 when the Rel-15 Beam Correspondence requirements are completed
  UE capability for supporting SSB based on BC and/or CSI-RS based on BC will be further discussed in WI phase.
  These requirements are only valid from Rel-16 onwards
FR2 UE requirements for contiguous intra-band DL CA for aggregated bandwidth larger than 1400 MHz
FR2 UE requirements for non-contiguous intra-DL CA for aggregated bandwidth larger than 1400 MHz FR2 UE requirements for contiguous UL CA
FR2 UE requirements for non-contiguous intra-band UL CA
  Phase 1: Study if both simultaneous UE transmission on aggregated UL carriers and non-simultaneous transmission on aggregated UL carriers with UE switching between two non-contiguous carriers could and should be specified. Study potential impacts of non-simultaneous transmission on RAN1 and/or RAN2 specifications
  Phase 2: Define FR2 UE requirements for non-contiguous intra-band UL CA based on the outcome of the Phase 1 study
FR2 UE requirements for inter-band DL CA
FR2 UE requirements for inter-band UL CA
  Phase 1: Study if both simultaneous UE transmission on aggregated UL carriers and non-simultaneous transmission on aggregated UL carriers with UE switching between two carriers could and should be specified. Study potential impacts of non-simultaneous transmission on RAN1 and/or RAN2 specifications
  Phase 2: Define FR2 UE requirements for inter-band UL CA based on the outcome of the Phase 1 study
Enhance FR2 UE MPR requirements by balancing with in-band emission requirements
Finalize FR2 UE power classes 3 and related UE requirements
Study if FR2 UE spherical coverage requirements for PC3 for >20%-tile can be defined