## Slide 1: Lawful Interception for Non-IP Data Delivery (NIDD) using SCEF

## Slide 2: What is SCEF
SCEF is a platform introduced in 3GPP Release 13 that exposes a set of network services through a secure REST based interface to external Application Servers.
SCEF can provide a set of business and security policies to ensure that external Application Servers get access only to an agreed set of services exposed by the platform with an agreed SLA.
While SCEF is targeted to IoT Applications it is not restricted to IoT use cases.
The stage 2 definition of SCEF is defined in TS 23.682.
Release 15 has introduced a stage 3 definition of the SCEF REST API over the T8 interface in TS 29.122.

## Slide 3: 3GPP Architecture for Machine-Type Communication (non-roaming) and the scope of CR0306
Scope of CR0306 to TS33.107

## Slide 4: 3GPP Architecture for Machine-Type Communication (roaming) and the scope of CR0306
Scope of CR0306 to TS33.107

## Slide 5: 3GPP Architecture for SCEF

## Slide 6: SCEF Addressing
An SCS/AS can address a device or group of devices over T8 with the following identifiers:
MSISDN
External Identifier
External Group Identifier
An MTC subscription in HSS has one IMSI and may have several External Identifiers stored in the HSS (note that if several External Identifiers are mapped to a single IMSI some functions of SCEF may not work)
The External Identifier shall have the form username@realm. The username (local identifier) is unique within the specific domain and the realm (domain identifier) is a registered Internet domain name e.g. 123456789@domain.com. The local identifier is used to derive the IMSI in HSS.
An MTC subscription in HSS may have one or several IMSI-Group Identifiers and one or several External Group Identifiers stored in the HSS.
The External Group Identifier will have the same format as the External Identifier. The local identifier is used to derive IMSI-Group Identifier in HSS.
The T8 interface does not expose the IMSI or IMSI-Group Identifier.

## Slide 7: SCEF Services
The services and capabilities offered by SCEF to SCS/AS include:
Non-IP Data Delivery*
Group Message Delivery
Monitoring events
High latency communication
Informing about potential network issues
Resource management of background data transfer
E-UTRAN network resource optimizations based on communication patterns provided to the MME
Support of setting up an AS session with required QoS
Change the chargeable party at session set-up or during the session
Packet Flow Description management
Enhanced Coverage restriction control
Network Parameter Configuration
Accessing MTC-IWF Functionality via T8
* Only Non-IP Data Delivery is in scope of CR0306

## Slide 8: NIDD: Non-IP Data Delivery
Non-IP Data Delivery provides a means of delivering payloads from the UE to the AS or vice versa without the need for an IP stack on the device. The transported data is considered unstructured from the EPS standpoint and is transported over the control channel rather than using dedicated radio data bearers.
Other benefits include improving security and reducing some of the threat vectors with IoT devices and applications as traditional IP based attacks cannot be used on the devices.
NIDD can be achieved using two mechanisms:
  Delivery via SCEF
  Delivery using a Point-to-Point SGi tunnel between the PGW and the AS
The UE is not made aware that a particular Non-IP PDN connection is provided via SCEF or via PGW. This selection will be based on the default Non-IP PDN APN configured for the subscriber in the HSS if no APN is specified by the device or by the selected APN if specified by the UE.
SCS/AS

## Slide 9: NIDD Connection Establishment
T6a/T6a Connection Establishment
NIDD Configuration

## Slide 10: Mobile Originating & Terminating Procedure
Mobile Originating NIDD procedure
Mobile Terminating NIDD procedure

## Slide 11: Reliable Data Service
The Reliable Data Service (RDS) was introduced in Release 14 as an optional lightweight transport control layer for NIDD. The RDS provides a mechanism for the SCEF or P-GW to determine if the data was successfully delivered to the UE and for the UE to determine if the data was successfully delivered to the SCEF or P-GW. When a requested acknowledgement is not received, the RDS retransmits the packet.
RDS also adds support for Port Numbers in the header that can be used to identify the application on the originator and the application on the receiver of a NIDD communication allowing for multiple applications to communicate over a single NIDD connection.
The stage 3 definition of the Reliable Data Service (RDS) is defined in TS 24.250.
Protocol Layer for RDS between UE and SCEF via E-UTRAN
RDS Header Format

## Slide 12: Lawful Interception of NIDD using SCEF
Regulatory authorities in Australia have indicated that IoT communications are not exempt from Lawful Interception obligations and it is assumed that this is also the case in other markets.
Telstra is currently evaluating the introduction of SCEF and Non-IP Data Delivery (NIDD) via SCEF. Based on previous feedback from regulatory authorities in relation to IoT communications, Telstra anticipates it will be obliged to support Lawful Interception of NIDD communications via SCEF.
TS 33.107 currently states that “Data over NAS for Internet of Things is for further study” and does not describe a solution for the Lawful Interception of NIDD communications via SCEF.
CR0306 on TS 33.107 introduces a solution that supports the Lawful Interception of NIDD communications via SCEF.

## Slide 13: CR0306 Solution Architecture
CR0306 replicates the LI solution for EPS by supporting IRI for the MME and HSS on the X2 interface but replaces the reporting of the IRI and CC from the S-GW/P-GW with IRI and CC reporting from the SCEF and IWK-SCEF. IRI and CC reporting from the IWK-SCEF allow for LI in the VPLMN. IRI reporting is also provided on the SGSN as NIDD can also be supported on GPRS.
CR0306 also re-uses a modified version of the existing Packet Data Header event to allow for the reporting of the Service Capability Server (SCS) or Application Server (AS) identity associated with a NIDD packet flow or RDS packet flow when the Reliable Data Service is being used for an NIDD connection.
Interception of NIDD using PtP SGi tunnel and interception of monitoring events requested via SCEF if for further study and not addressed in CR0306.

## Slide 14: Appendix

## Slide 15: Monitoring Events/MONTE Feature
Allows SCEF to monitor specific events in the 3GPP network and make that information available to Application Servers.
The following monitoring events may be supported:
Association of the UE and UICC and/or new IMSI-IMEI-SV association
UE reachability
Location of the UE, and change in location of the UE
Loss of connectivity
Communication failure
Roaming status (i.e. whether the UE is in HPLMN or VPLMN)
Number of UEs present in a geographical area
Availability of Downlink Data Notification (DDN) failure
Two types of Monitoring Events can be requested:
One-time Monitoring Events
  The request will generate a single report
Continuous Monitoring Events
  May generate more than one Monitoring Indication
Monitoring requests can be made against a single service or group of services.

## Slide 16: Monitoring Event Configuration
Monitoring Event Configuration via HSS
Monitoring Event Configuration directly at MME/SGSN

## Slide 17: Reporting of Monitoring Events

## Slide 18: Group Message Delivery
Group message delivery via MBMS (LTE-B)
  Intended to efficiently distribute the same content to a group located in a particular geographical area when MBMS (LTE-B) is used
  Limited applicability (does not support all scenarios)
    E.g. UEs not supporting MBMS/LTE-B
    UEs located where MBMS/LTE-B is not deployed
  Note: Release 14 added ability for device to receive MBMS user service in idle mode if connected mode not required for the user service, reducing signalling needed between UE and the network
This service allows an AS to deliver a payload to a group of UEs. There are two methods to achieve this:
Group message via unicast MT NIDD
  For UEs which are part of the same External Group Identifier
  Uses the SCS/AS Identifier and External Group Identifier to determine which APN will be used to send the non-IP data to the UEs
  SCEF queries the HSS to resolve the members of the group and then sends the message in a unicast manner to all of the UEs

## Slide 19: Group Message Delivery using MBMS

## Slide 20: Group Message Delivery via unicast MT NIDD

## Slide 21: Security on T8 Interface
Mutual Authentication
  Mutual Authentication based on client and server certificates shall be performed between the SCEF and SCS/AS using TLS.
Security Profiles
  TLS shall provide integrity protection, replay protection and confidentiality protection for T8 interface. Security profiles for TLS implementation and usage shall follow provisions given in TS 33.310.
Authorisation of SCS/AS’s requests
  After authentication, SCEF determines whether SCS/AS us authorised to send requests using Oauth authorisation mechanism as per RFC6749.

## Slide 22: Benefits of SCEF
Removal of IP overhead allows simplification of device and lower power consumption resulting in lower device costs, improved battery life and lower data usage costs for the customer
Removal of IP interface on device, reduces device exposure to traditional IP based security threats
Use of data transfer over the radio signalling channel and removal of IP bearers lowers the network unit costs and better enables the ability of the network to scale for millions of IoT devices
Application servers can integrate with all their IoT devices through a single REST based interface easing complexity of IoT application development
Support for real-time device monitoring, allowing customers to be notified of connectivity issues or retrieve location information for their devices and offers a possible monetisation opportunity for operators
Enables the use of LTE-B broadcast capabilities for customers to quickly and efficiently deliver updates (such as FOTA) to their devices without consuming the limited radio bandwidth available to narrowband devices.
Facilitates new charging models better aligned to the consumption model of the device including the option of transaction based charging
Builds a foundation for the service based 5G core architecture and a pathway to the 5G Network Exposure function
Optionally provides an access point for a customer’s data, allowing operators (with the permission of the customer) to enrich this data with other operator data sources or external data sources and provide further data analytics for the customer or share the data with 3rd parties as part of an expanded IoT use case