## Slide 1
TSG CT WG4 Chairman
Lionel Morand (Orange)
CT WG4 Status Report to TSG CT #81
3GPP TSG CT Meeting #81 CP-182009
Gold Coast, Australia; 10th – 11th September 2018

## Slide 2: TSG CT WG4 Organisation
Meetings since the last CT plenary
  CT4#85-bis (Sophia-Antipolis, FR)
  CT4#86 (West Palm Beach, US)
  Meeting Report after last plenary in CP-182010
Upcoming Meetings before the next CT plenary
  CT4#86-bis (Vilnius, LT)
  CT4#87 (West Palm Beach, US)
    Full agenda
TSG CT WG4 officials are:
  Chairman:
    Lionel Morand (Orange / ETSI)
  Vice chairs:
    Yvette Koza (DT / ETSI)
    Peter Schmitt (Huawei / CCSA)
  MCC support:
    Kimmo Kymäläinen
Legend Blue – elected since previous plenary
Blue – re-elected since previous plenary Red – for election in coming plenary period
Notes: 2

## Slide 3
TSG CT WG4 Statistics
TSG CT WG4 statistics:
  379 (364 BCF + 15 A) Change Requests agreed, mainly 5GS_Ph1-CT
  36 pCRs agreed on 5GS Restoration, N32 and FS on QUIC, UPPS
  Work Items / Study Items agreed
    0 new Study Item and
  Work Items / Study Items endorsed
    0 new Work Item, 1 revised Work Item (5GS_Ph1-CT) and 1 revised SID (FS_UPPS)
  TS/TRs sent for information and approval
    2 TS sent for information and approval
  Participation:
    CT4 #85-bis:
      78 Registered Participants: CT4#85bis attendees List
      ~35 Attended Participants
    CT4 #86:
      83 Registered Participants: CT4#86 attendees List
      ~35 Attended Participants

## Slide 4: CT4 Progress
  The above table shows the progress for the approved Rel-16 and Rel-15 WIs.

## Slide 5: Rel-15 Exception Sheets
CT4 aspects of 5G System Phase 1 (CP-181112)
  Expected completion date: CT#81
  Output:
    100% Completed except:
      Restoration Mechanism: 95%
      PLMN Interconnect (N32): 85%
CT4 aspects of 5G Trace management (CP-181114)
  Expected completion date: CT#81
  Output:
    100% Completed

## Slide 6
Agreed Revised SI
Tdoc | Revised WIDS | Source | Notes
CP-182052 | Revised SID on User Plane Protocol Study in 5GC | SoftBank | Addition of supporting companies
Endorsed Revised WI
Tdoc | Endorsed WIDS | Source | Notes
CP-182204 | Revised WID on CT aspects on 5G System - Phase 1 | Huawei | Adding the new spec on N32

## Slide 7: Technical Specifications sent for Approval
Tdoc | TS Agreed to go for Information and Approval | Source | Rapporteurs
CP-182082 | 3GPP TS 23.527 v0.3.0: Restoration Procedures; Stage 2 | CT4 | Peter Wild
CP-182083 | 3GPP TS 29.cde v0.2.0: Public Land Mobile Network (PLMN) Interconnection | CT4 | Sridhar Bhaskaran

## Slide 8: LS OUT (1/2)
TDoc # | Title | Source | Notes
C4-185319 | LS on Nausf_SoRProtection-service (to: SA2; cc: SA3) | CT4 | Julien Bournelle Julien.bournelle@orange.com
C4-185320 | Reply LS to S3-181468 = C4-185028 on avoiding race condition in 5G AKA (to: SA3; cc: -) | CT4 | Julien Bournelle Julien.bournelle@orange.com
C4-185491 | LS on User Plane Analysis (to IETF DMM; cc: -) | CT4 | Sridhar Bhaskaran sridhar.bhaskaran@huawei.com
C4-185492 | LS on event reporting from AMF (to: SA2; cc: -) | CT4 | Yunjie Lu jones.lu@ericsson.com
C4-185493 | Reply LS to S3-182088 = C4-185031 on TLS and Inter PLMN Routing (to: SA3; cc: SA2) | CT4 | Sridhar Bhaskaran sridhar.bhaskaran@huawei.com
C4-185495 | LS on Usage of Instance Id in the Authentication Information (to: SA3; cc: CT) | CT4 | Ulrich Wiehe ulrich.wiehe@nokia.com
C4-185505 | Reply to S3-182033 = C4-185030 on OAuth 2.0 (to: SA3; cc: -) | CT4 | Sridhar Bhaskaran sridhar.bhaskaran@huawei.com

## Slide 9: LS OUT (2/2)
TDoc # | Title | Source | Notes
C4-186360 | Reply LS on template availability in TS 29.501 (To: SA5, cc: CT3) | CT4 | Ulrich Wiehe ulrich.wiehe@nokia.com
C4-186547 | Reply LS on maximum size of UE Radio Capabilities and maximum Information Element size on network interfaces (To: SA2) | CT4 | Peter Wild peter.wild@vodafone.com
C4-186573 | IMSI-based NAI format for SUPI (To: CT6, CT1; cc: SA3, SA2 | CT4 | Bruno Landais bruno.landais@nokia.com
C4-186602 | LS on API specification and API version number maintenance (To: CT, SA; cc: CT3, SA5) | CT4 | Lionel Morand lionel.morand@orange.com
C4-186606 | Response to “Reply LS on AUSF/UDM instance selection and SUCI parameters” (To: SA2; cc: RAN2, RAN3, CT1, CT3) | CT4 | Bruno Landais bruno.landais@nokia.com

## Slide 10: CT4: Update on 5GS_Ph1 (1/2)
Title:
  CT aspects on 5G System - Phase 1 (CT1)
Objectives:
  After completion of the Study, specify the service-based interfaces (API)
  CT4 responsible for the specification of core-network SBIs (except PCC) and impacts on existing protocols (e.g. GTP, Sx)
WID: 99% completed
Study Phase: 100% completed.
  TR 29.891 sent for approval at CT#78
Normative Phase: 99% completed
  2 new TSs sent for information and approval at CT#81
  About 350 CRs and pCRs agreed on TSs
~90% of the meeting dedicated to 5GS

## Slide 11: CT4: Update on 5GS_Ph1 (2/2)
(Source: C4-186636)
New TS
New TR
Impacted Spec
Study Phase | 100%
Normative Phase | 99,16%
Completion of 5GS_Ph1 CT4 aspects | 99%
Spec No | Title | After CT4#86
23.527 | 5G System; Restoration Procedures; Stage 2 | 95%
29.500 | 5G System; Technical Realization of Service Based Architecture; Stage 3 | 100%
29.501 | 5G System; Principles and Guidelines for Services Definition; Stage 3 | 100%
29.502 | 5G System; Session Management Services; Stage 3 | 100%
29.503 | 5G System; Unified Data Management Services; Stage 3 | 100%
29.504 | 5G System; Unified Data Repository Services; Stage 3 | 100%
29.505 | 5G System; Usage of the Unified Data Repository services for Subscription Data; Stage 3 | 100%
29.509 | 5G System; Authentication Server Services; Stage 3 | 100%
29.510 | 5G System; Network function repository services; Stage 3 | 100%
29.511 | 5G System; Equipment Identity Register Services; Stage 3 | 100%
29.518 | 5G System; Access and Mobility Management Services; Stage 3 | 100%
29.531 | 5G System; Network Slice Selection Services; Stage 3 | 100%
29.540 | 5G System; SMS Services; Stage 3 | 100%
29.571 | 5G System; Common Data Types for Service Based Interfaces; Stage 3 | 100%
29.572 | 5G System; Location Management Services; Stage 3 | 100%
29.cde | 5G System; Public Land Mobile Network (PLMN) Interconnection; Stage 3 | 85%
29.891 | 5G System - Phase 1 CT WG4 Aspects | 100%
23.003 | Numbering, addressing and identification | 100%
23.008 | Organization of subscriber data | 100%
23.380 | IMS Restoration Procedures | 100%
29.168 | Cell Broadcast Centre interfaces with the Evolved Packet Core; Stage 3 | 100%
29.244 | Interface between the Control Plane and the User Plane nodes | 100%
29.274 | 3GPP Evolved Packet System (EPS); Evolved General Packet Radio Service (GPRS) Tunnelling Protocol for Control plane (GTPv2-C); Stage 3 | 100%
29.281 | General Packet Radio System (GPRS) Tunnelling Protocol User Plane (GTPv1-U) | 100%

## Slide 12: CT4: 5GS_Ph1 Highlights (1/2)
5GC API specification
  All the specs are completed (except 2, see below)
  some Editor’s Notes are still to be removed
Restoration procedures
  TS 23.527 sent for information and Approval
  includes:
    Restauration procedures for Rel-15, focus on N4 and user plane interfaces, reusing existing mechanisms for CUPS and GTP
    Basic procedure for NF failure and restart detection using NRF
  The rest of the functions will be covered in Rel-16.
Security on N32
  TS 29.cde sent for Information and Approval but completed at 85% only
  CT4 still asks for clarification on the SEPP functionality and inter-PLMN routing
  Warning: Late SA3 feedback will delay the completion of API specs.

## Slide 13: CT4: 5GS_Ph1 Highlights (2/2)
5G Trace
  Work completed in CT4 and CT3
API design guideline
  Decision to define a specific freezing date for API (+3 months after Rel freeze)
  Decision not to generate a separate YAML file to include the OpenAPI description.
Close coordination with CT3
  Joint sessions with CT3 for discussions and common conclusions on API specification, API design guidelines and common data types
Next main steps:
  Finalize the TS 23.527 on restauration procedures for Rel-15
  Cover the security aspects based on SA3 feedback
  Alignment with Stage 2 modifications/corrections
  Stabilize the API until the freezing date (CT#82)

## Slide 14: Some "Company" CRs sent to CT#81
About 40 CRs sent to plenary as revisions of agreed CT4 CRs
Triggered by early implementation of the CRs in draft versions of API specifications and detection of errors
Mainly correction of the OpenAPI description in Annex and related alignment in the main body of the specifications
Following "Recommendation 5" of LS on "API specification and API version number maintenance" (CP-182210)

## Slide 15: 5G Timeline and impacts on CT4
Rel-14
Rel-15 (5G Phase 1)
2017
2018
Stage 3 Study Phase on CT aspects for 5G
Stage 3 Normative Phase
Extension
Stage 2 Normative Phase (SA2, SA3, SA6…)
Extension
- CT/SA
- CTx WG
Extension
Extension
Rel-16 (5G Phase 2)
5G Timeline and impacts on CT4
  TR 100% completed and the normative phase is on the right track
  About 99% for the normative phase, with 15 specifications sent for approval
Release Timeline (Stage 3 focus)

## Slide 16: CT4: Shared Data Handling
Title:
  Shared Data Handling on Nudm and Nudr [Shared_Data] (CT4)
Objectives:
  Enhance Nudr and Nudm-SDM services, allowing signalling optimizations for cases where shared subscription data are modified.
Status:
  A CR has been agreed (CP-182056/C4-186497)
  This CR introduces a specific identifier identifying additional parts of subscription data shared by several UEs
  Initially submitted for Rel-16, the solution has been finally agreed for Rel-15 as the impact on the existing Nudm API is minimal. No need to wait for Rel-16 to introduce it.
WID completion: 90% completed

## Slide 17: CT4: User-plane Protocol for Rel-16
Title:
  Study on User-plane Protocol [FS_UPPS] (CT4)
Objectives:
  1st phase: Liaise with IETF on the current GTP-U definition
  2nd phase: Set of criteria for protocol selection based on Rel-16 requirements and candidate protocol evaluation
Spec:
  TR 29.892 v0.2.0.
Status:
  Start of the second phase
  Exchange of LS between CT4 and DMM WG for clarification on GTP-U
  LS received from DMM WG to list the solutions under discussion in DMM WG
  First contributions to describe candidate for the User plane in rel-16 (GTP-U, SRv6)
Next Steps:
  Complete the description of the candidate protocols and identify impacts on the architecture
SID completion: 10%

## Slide 18: CT4: QUIC Transport for SBI
Title:
  Study on IETF QUIC Transport for 5GC Service Based Interfaces [FS_QUIC] (CT4)
Objectives:
  Study the differences between HTTP/2 over TCP vs HTTP/2 over QUIC and appraise the possible advantages of using QUIC as transport for the Service Based Interfaces
Spec:
  TR 29.893 v0.2.0
Status:
  Description of QUIC features as defined by IETF
  Description of HTTP/2 layering over QUIC and use
  Description of some key issues and proposed solution (Discovery of QUIC support)
Next steps:
  describe the applicability of HTTP/QUIC and the impacts on SBA
SID completion: 40%

## Slide 19: CT4: Load/Overload Control on SBI
Title:
  Study on Load and Overload Control of 5GC Service Based Interfaces [FS_LOLC] (CT4)
Objectives:
  Identify the requirements and solution for Load Control and Overload Control, including Overload Prevention and Detection, and Overload Mitigation.
Spec:
  TR 29.843 v0.1.0
Status:
  Only the skeleton has been provided so far
Next steps:
  Complete the TR
SID completion: 5%

## Slide 20: CT Plenary Decisions for CT4
None.

## Slide 21: Incoming liaisons to CT plenary
CP-182196: API specification and API version number maintenance
  To CT and SA
  Some questions were raised on the handling of the API version number and the consequence for the API specification management.
  After discussion, a set of recommendations has been reached between CT3 and CT4 regarding the handling of 5GC API specifications and the API version numbers. These recommendations are provided in this LS
CP-182195: Usage of Instance Id in the Authentication Information
  CT in Cc
  It could not be clarified which purpose the Requester ID used as input parameter serves and what the AUSF is expected to do with this input. CT4 therefore kindly ask SA3 to either clarify the use of this parameter or remove it from TS 33.501. In the latter case, CT4 will withdraw the attached 29.509 CR

## Slide 22: For CT Plenary action
API specification and API version number maintenance
  Discuss proposed recommendations
  provide CT view
  Provide input to SA

## Slide 23: CRs to CT Plenary
CRs agreed at CT4#84 and CT4#85
  Rel-8 = 0
  Rel-9 = 0
  Rel-10 = 0
  Rel-11 = 0
  Rel-12 = 0
  Rel-13 = 0
  Rel-14 = 17
  Rel-15 = 345
  No mirror CRs are included in these figures
  Rel-8 to Rel-14 CRs are under FASMO acceptance, i.e. CRs that solve Frequent and Serious Mis-operation Only are accepted.
    Careful check of the “Consequences if not approved” even for Rel-14 CRs

## Slide 24: CRs for Conditional Approval (CT4)
Tdoc | TS | CR | Rev | Title | TD# | Other Affected Specs | Affected WG
CP-182079 | 29.244 | 0153 | 2 | Application detection report when the PFDs are removed | C4-186609 | 23.214-0067 | SA2
CP-182079 | 29.244 | 0154 | 2 | Application detection report when the PFDs are removed | C4-186610 | 23.214-0068 23.501-0485 | SA2
CP-182072 | 29.272 | 0769 | 1 | Subscribed PTW length | C4-186489 | 23.401-3445 | SA2
CP-182084 | 29.272 | 0773 | - | Access Restrictions | C4-186103 | 23.502-0525 | SA2
CP-182055 | 29.502 | 0032 | 1 | User Location Timestamp | C4-186381 | 23.502-0532 29.571-0032 | SA2
CP-182056 | 29.503 | 0046 | 2 | BackUp AMF Info | C4-186555 | 23.502-0594 | SA2
CP-182056 | 29.503 | 0047 | 2 | Interworking with EPS indication | C4-186556 | 23.502-0585 | SA2
CP-182058 | 29.509 | 0004 | 4 | SoRProtection Service Description | C4-186407 | 23.501-0536 | SA2
CP-182068 | 29.509 | 0014 | 2 | 5G Trace for AUSF | C4-186334 | 23.501-0474 | SA2
CP-182062 | 29.518 | 0032 | 3 | N1N2MessageTransfer and Notify for PCF | C4-186591 | 23.502-0612 | SA2
CP-182064 | 29.540 | 0007 | 2 | BackUp AMF Info | C4-186570 | 23.502-0594 | SA2
SA
RAN
CT

## Slide 25: CRs Overview
Rel-15 CRs (Category B, C, F)
  345 agreed CRs
    Correction of the new 5GC specs
    Specifications impacted by 5GS (TS 23.003, Sx, GTP)
    Stage 2 alignment in EDCE5, NAPS, CIoT, GENCEF
    Some TEI15 clarifications/corrections
Rel-14 CRs (Category F)
  17 agreed CRs
    14 CRs on CUPS
    2 CRs on eDRX/S6A
    1 CR on MCVideo

## Slide 26: Acknowledgements
The Chairman wants to:
  Thank CT4 delegates for the completion of the work on the 5GS related specs
  Thank Susana for the coordination and the joint sessions on 5GS work between CT3 and CT4
  Thank WI and spec rapporteurs for their priceless coordination work and the pre-editing work of the 5GC specs
  Thank Peter Schmitt and Yvette Koza for their help in CT4 management
  Thank Kimmo for just being Kimmo (which means a lot)
  Thank the ETSI and NAF of our meeting locations (Sophia-Antipolis and West Palm Beach) and ETSI support for IT facilities.

## Slide 27: Thank You
Lionel Morand
3GPP TSG CT WG4 chairman
lionel.morand@orange.com