## Slide 1: Motivation for “Low cost & enhanced coverage MTC UE for LTE” Work Item
Vodafone Group
3GPP TSG RAN#60,
Oranjestad, Aruba, 11th – 14th June 2013
RP-130729

## Slide 2: High level view
Many MTC applications target low data rate, that can be handled sufficiently by GSM/GPRS networks with low modem development cost.
There is a need to make LTE the natural home for these applications, as otherwise:
  GSM/GPRS spectrum and network functions will need to be maintained longer
  Re-farming of spectrum to LTE will take longer
  Running more radio technologies leads to additional operational costs for the operator.
Due to the nature of MTC applications being autonomous (not necessarily located close to humans), ubiquitous geographical coverage is an important driver for wireless networks supporting MTC.
  New technologies are emerging that aim to offer a better service to MTC than GSM today.
Vodafone believes that it is important for LTE to maximise its ability to serve MTC applications, so that LTE operators can generate new revenue.
  Low cost LTE devices and enhanced LTE coverage will drive more MTC applications to use LTE.

## Slide 3: 3GPP status and proposed way forward
The study item on “Provision of low-cost MTC UEs based on LTE” showed that:
  Low cost device with Bill of Material Cost comparable to E-GPRS would be possible.
  Coverage improvement* of 20dB possible, but 15dB offers a good trade-off with other factors such as spectrum efficiency, UE power consumption (see proposed WID for more details).
PROPOSAL: Agree new work item to specify some or all of the techniques identified in outcome of the study item.
This will allow LTE to offer:
  A low cost LTE device type for MTC.
  15dB coverage improvement for low cost MTC and other MTC UEs for delay tolerant MTC applications.
    We believe that 15dB of improvement will significantly enhance the likelihood of LTE being selected instead of GSM and other technologies to provide MTC services.
We believe that the proposed Rel-12 work item will significantly enhance the ability of LTE as a technology to provide MTC services.
*Unlike for normal LTE MTC devices, for low cost MTC devices, the coverage is reduced by adding low cost techniques, so the improvement would be relative to that for those devices.

## Slide 4: Summary of work needed in working groups
Impacts to RAN1:
  Potential Link level solutions studied for coverage improvement for delay tolerant MTC UE include PSD boosting, relaxed requirement, design of new channels/signals, repetitions/TTI bundling, low rate coding, retransmission, code spreading and new decoding techniques.
  For higher RS power boosting or PSD boosting
  New channel design or support of increased DMRS density, code spreading, and shorter length CRC in existing channels will have specification impact.
  Define new UE category and associated additional UE capabilities for cost reduction techniques.
Impacts to RAN2:
  Possible design of new SIBs to allow UE operation with reduced bandwidth.
  Specification of signalling to configure the UE to use the new physical layer techniques.
  Increased delay from techniques such as repetition may impact some higher layer procedures.
  Involvement in specification of a mechanism to identify delay tolerant MTC UE’s in poor coverage and configure tuneability to trade-off coverage with spectrum efficiency impacts.
Impacts to RAN4:
  Impact from PSD boosting on PDCCH/EPDCCH or the demodulation RS could arise from the larger variation in transmit power across subcarriers and its effects on EVM requirements.
  RF and core requirements will need to be defined for Single Rx, Time domain repetition using TTI bundling for PUSCH/PDSCH and, if introduced, higher RS power boosting, PSD boosting, New channel design, increased DMRS density, code spreading, or shorter length CRC.

## Slide 5: Time budget requested
August 2013
RAN1#74 [ 2 Time Units]
  Liaise to RAN2 UE category and UE capabilities for Low cost MTC UE, liaise to RAN4 techniques requiring additional core requirements.
  Specify coverage improvement techniques for common channels (PBCH/SIB, PRACH and SCH)
RAN2#83 [ 1.5 Time Units]
  Specify coverage improvement techniques for PDSCH/PUSCH
RAN4#68 [ 1 Time Units]
  Specify core requirements for single Rx
October 2013
RAN1#74b [ 2 Time Units]
  Specify coverage improvement techniques for control channel (E)PDCCH
RAN2#83b [ 2 Time Units]
  Specify UE category and associated UE capability for low cost MTC UE
  Specify mechanism for identifying UE's in poor coverage and amount of coverage required.
  Specify RAN2 aspects of coverage improvement for common channels (PBCH/SIB, PRACH and SCH)
RAN4#68b [ 1 Time Units]
  Specify core requirements for aspects identified by RAN1 for (PSD boosting, RS power boosting etc)
November 2013
RAN1#75 [ 2 Time Units]
  Specify stage 3 aspects
RAN2#84 [ 2 Time Units]
  Specify stage 3 aspects
RAN4#69 [1Time Units]