## Slide 1: Way Forward on supplemental downlink for TD-LTE in Rel.12
NTT DOCOMO, INC.
RP-140483
3GPP TSG-RAN#63
Fukuoka, Japan, 3-6 March 2014
Agenda: 14.1.1

## Slide 2: Introduction
The followings are proposed in this document
  Way forward on new WI on supplemental downlink for TD-LTE
  A technical analysis in terms of the co-existence with the existing UL-DL configurations

## Slide 3: Way Forward
New WI on supplemental downlink for TD-LTE is approved in RAN#63 where:
  The new configuration for supplemental downlink for TD-LTE is introduced.
    Specification work will start from the following WG meetings and completed within Rel.12
  At the same time, the technical aspect in terms of the co-existence with the existing UL-DL configurations could be clarified if necessary in RAN1

## Slide 4: Technical analysis on co-existence
Co-existence b/w UL/DL configs #2 and #5
  One of two UL SFs in config #2 is blocked by a DL SF in config #5
  Lost of one UL SF in config #2 results in 50% DL + 50% UL losses
    Since the UL SF is responsible for both UL data and DL HARQ-ACK
  50% DL/UL transmission resources are lost
Co-existence b/w UL/DL configs #5 and DL-only
  A UL SF is blocked by a DL SF in DL-only config
  Lost of one UL SF in config #5 results in 100% DL and UL losses
    Since the UL SF is responsible for both UL data and DL HARQ-ACK
  100% DL/UL transmission resources are lost
#2
#5
#5
#”7”
Both cases are not acceptable from operator’s point of view

## Slide 5: Technical analysis on co-existence
Co-existence b/w UL/DL configs #2 and #5
  One of two UL SFs in config #2 is blocked by a DL SF in config #5
  Lost of one UL SF in config #2 results in 50% DL + 50% UL losses
    Since the UL SF is responsible for both UL data and DL HARQ-ACK
  50% DL/UL transmission resources are lost
Co-existence b/w UL/DL configs #5 and DL-only
  A UL SF is blocked by a DL SF in DL-only config
  Lost of one UL SF in config #5 results in 100% DL and UL losses
    Since the UL SF is responsible for both UL data and DL HARQ-ACK
  100% DL/UL transmission resources are lost
#2
#5
#5
#”7”
In principle, it is not allowed to decrease someone’s assets coming from co-existence using different UL/DL configs, regardless of whether or not new DL-only configuration is introduced
Consensus b/w operators is essential for TDD co-existence cases

## Slide 6: Technical analysis on co-existence
If an operator has multiple carriers, a TDD band can be utilized as DL-only carrier even without DL-only configuration
If the operator wants to damage intentionally or accidentally to the neighboring operator, the operator can use UL/DL config #5 without UL transmission on the carrier
#5
#2
#”7”
#2
There is no fundamental difference b/w existing case and DL-only config

## Slide 7: Summary on co-existence aspect
A consensus on the configuration among associated operators is essential to make maximum use of TD-LTE system.
If the consensus was not reached, co-existence issues happen regardless of the configurations.
Otherwise, some guard band(s) is required, however, the advantage of TD-LTE system is lost.