## Slide 1: Way forward on advanced receiver enhancements in Rel-13
ASUSTek, AT&T, ATR, CATR, CEWiT, CMCC, CHTTL, China Telecom, China Unicom, Coolpad, Deutsche Telekom, Dish Network, Fraunhofer IIS, IAESI, III, Intel Corporation, ITL Inc., ITRI, KDDI, KT Corp., Lightsquared, Shanghai Tejet Com Technology, SoftBank Mobile, SK Telecom, Telecom Italia, Telefonica, T-Mobile USA, Verizon Wireless, ZTE
3GPP TSG RAN meeting #66
Maui, USA, Decmber 8 - 11, 2014
RP-142271

## Slide 2: Background (Overview of PDSCH receiver enhancements)
In LTE-A systems several receiver enhancements were introduced to cope with interference issues in the physical downlink data channel (PDSCH) in different scenarios.
However, the interference suppression and cancellation for the downlink control channels (e.g. PCFICH / PDCCH, PHICH, etc.), which carries the DL / UL scheduling assignments and ACK / NACK are still based on Rel-8 MMSE receiver without interference mitigation capability.
Rel-11 MMSE-IRC
Rel-11
CRS-IC
Rel-12 CRS-IM
Rel-12 NAICS
Rel-8
MMSE
PDSCH performance
Study / Work Item
Large gap in the performance comparing to Rel-8 MMSE receiver!

## Slide 3: Issues for Rel-12 NAICS (Rel-12 NAICS performance with and without PDCCH/PCFICH demodulation)
Realistic Rel-12 NAICS performance with consideration of control channel demodulation
Rel-12 NAICS performance w/o consideration of control channel demodulation
The advantages of Rel-12 NAICS receivers for PDSCH can’t be achieved without enhancements to control channel receivers!
Note: A similar performance trends for Rel-12 NACIS have been observed in other companies contributions (refer to e.g. R4-145750, R4-146268, R4-146514). The issue is currently under discussion in RAN4.
MCS#5, 2 interfering cell modelling with INR1 = 13.9dB, INR2 = 3.3dB

## Slide 4: Proposals
Approve to study control channel interference cancellation/mitigation on LTE advanced receiver enhancement as a study item in RAN#66