## Slide 1: Signalling Reduction for Idle-Active Transitions in LTE
RP-150312 - Motivation for New proposed WI

## Slide 2: Background
Networks face continuous traffic growth from increasing number of devices.
  So far addressed by physical layer enhancements, e.g. improving spectral efficiency.
Continuous traffic growths result in continuous increase of control signaling load mainly due to Idle/Active mode transitions.
  Acknowledged by number of earlier studies and work items, e.g. MTC, EDDA, small cell enhancements
Continues increase of control signaling requires
  Radio resources to conduct the actual message transfer
  Processing resources in the affected network nodes

## Slide 3: Proposed RAN Work Item
Reduction of signaling and processing load by
  Re-use of information from the previous RRC connection for the subsequent RRC connection setup.
    Store and re-use previous RRC connection related information (Uu related), e.g. AS Security Context, DRB-id etc.
    Store and re-use previous S1-MME UE association (S1AP)
    Store and re-use previous S1-U bearer context related information (S1-U)
Planned approval of WID in RAN #67

## Slide 4: Store and re-use previous connection information
SGW
MME
eNodeB
S1-U
RRC
RRC
S1AP
S1AP,
S1-U
Relevant nodes store and re-use appropriate
information for a sub-sequent RRC connection

## Slide 5: Details
First UE performs RRC Connection Establishment as today.
At the transition from CONNECTED to IDLE, the eNB and UE store previous RRC connection related information
  AS configuration or part of it and security related info maybe stored
At the next RRC Connection Establishment (IDLE to CONNECTED), the previously stored information in the UE and the eNB is reused to establish RRC connection. This procedure is controlled by the network.
  Parameter that are outdated (like PUCCH configuration) can be reconfigured meanwhile
If the UE is not known by the cell, the legacy RRC Connection Establishment is triggered.
The UE can be paged when it is in suspended state.
No impacts are foreseen to the existing mobility procedures.

## Slide 6: benefits
Possible signaling and processing load reduction:
  Reduction of number of RRC messages on Uu interface, e.g. by re-using the AS Security Context (no need for Security Command/Security Command Complete).
    Number of RRC messages can be reduced up to 50%
    Number of S1 messages can be reduced up to 30%
  Less processing required by the eNodeB when re-using stored information.
  Potential to reduce signaling on the S1AP by keeping the S1 MME-UE association and introducing a simplified re-activation procedure instead of a 3-way-hand-shake at setup/release.
  Less processing in the eNode by re-using S1-U information.