## Slide 1: Way forward on new UE categories in Rel-12
3GPP TSG-RAN#67
Shanghai, China, 9 - 12 March 2015
Agenda: 14
RP-150489
KDDI, Sprint, CMCC, Huawei, HiSilicon, Qualcomm, Ericsson, Nokia Corporation, Nokia Networks, Samsung

## Slide 2: Way forward
Introduce three new DL UE categories for
800 Mbps and 1Gbps, 1.2Gbps from Rel-12
  256QAM should not be mandatory for any of these new categories
  RAN WGs work in 2015/2Q
  The corresponding CR is prepared for RAN#68

## Slide 3: Annex
DL Peak | Examples of combinations
750Mbps(covered by 800Mbps) | 2CC 4*4MIMO + 1CC 2*2MIMO 1CC 4*4MIMO + 3CC 2*2MIMO 5CC 2*2 MIMO
800Mbps | 2CC 4*4MIMO 256QAM 1CC 4*4MIMO 256QAM + 2CC 2*2MIMO 256QAM 4CC 2*2MIMO 256QAM
900Mbps(covered by 1.0Gbps) | 3CC 4*4MIMO 2CC 4*4MIMO 2CC 2*2MIMO 1CC 4*4MIMO 4CC 2*2MIMO

## Slide 4: Annex(Con’t)
DL Peak | Examples of combinations
1.0Gbps | 2CC 4*4MIMO 256QAM + 1CC 2*2MIMO 256QAM 1CC 4*4MIMO 256QAM + 3CC 2*2MIMO 256QAM 5CC 2*2MIMO 256QAM 2CC 4*4MIMO 64QAM + 3CC 2*2 MIMO 64QAM(1050Mbps) 3CC 4*4MIMO 64QAM + 1CC 2*2 MIMO 64QAM(1050Mbps)
1.2Gbps | 4CC 4*4MIMO 1CC 4*4 MIMO 256QAM + 4CC 2*2MIMO 256QAM 3CC 4*4MIMO 256QAM 2CC 4*4MIMO 256QAM + 2CC 2*2MIMO 256QAM 1CC 4*4 MIMO 256QAM + 4CC 2*2MIMO 256QAM