## Slide 1: Motivation on smooth mobility across small cells in LTE
Sept. 14~16 2015

## Slide 2: Outline
Key scenario
Key challenges
Solution example

## Slide 3: What have been discussed before on small cell (1/3)
Ideal backhaul + inter-frequency=carrier aggregation
Ideal backhaul + co-channel= intra-Site CoMP
Non-ideal backhaul+ inter-frequency= dual connectivity
Non-ideal backhaul + inter/intra-frequency=small cell in RAN1
Observation: ideal backhaul vs non-ideal backhaul really makes difference

## Slide 4: What have been discussed before on small cell (2/3)
Observation: inter-frequency between macro and small cell have much better mobility performance
#scenario2 #1
#scenario2 #2
#scenario1
#scenario2 #3

## Slide 5
6.1.5 Synchronization [36.932 c10]
Both synchronized and un-synchronized scenarios should be considered between small cells as well as between small cells and macro cell(s). For specific operations e.g. interference coordination, carrier aggregation and inter-eNB COMP, small cell enhancement can benefit from synchronized deployments with respect to small cell search/measurements and interference/resource management. Therefore time synchronized deployments of small cell clusters are prioritized in the study and new means to achieve such synchronization shall be considered.
6.3 Feasibility and benefits of radio-interface based synchronization mechanisms [36.872 c10]
It is well known that TDD system needs inter-cell synchronization on the same frequency or different frequencies within the same band; in addition, for both TDD and FDD, it would be essential to consider the synchronization mechanisms between cells to bring benefit to the existing features (e.g. (f)eICIC, CoMP as well as carrier aggregation) and some potential techniques for small cell enhancements (e.g. efficient small cell discovery). For some other techniques such as advanced receiver at UE, a synchronized network is beneficial for the receiver performance. It is thus observed that
Synchronization for both TDD and FDD systems needs to be considered.
Observation: synchronization requirement is critical for small cell deployment

## Slide 6: The key scenario
So the most interested scenario is as following:
1, Outdoor with macro cell coverage
2, Non-ideal backhaul between macro and small cell as well as between small cell
3, Small cell is in another frequency from macro. Maybe there are more than one frequency layers .
4, Small cells are synchronized between each other
5, small cells are densely deployed
f1
f2
f2

## Slide 7: Simulation assumption comparison:
Items | Dual connectivity (36.842) | UDN in RP-150612
Network layout | 7 macro sites (21 macro cells), wrap-around. | 3-sectorized Hexagonal grid with 19 cells wrap-around
Inter-site distance / cell radius | Macro cell: 500 m (ISD); Small cell: 40 m (Cell radius) | Macro cell ISD: 500 m small cell ISD: 20 m Cluster distance: 100 m Cluster to macro distance: 75 m
Transmit power | Macro eNB: 46 dBm Small cell: 30 dBm | Macro eNB: 46 dBm Small cell: 24dbm/ 30 dBm
Number of small cells | 4 small cells randomly placed per macro cell | 4/8/16/32/40/60

## Slide 8: Outstanding difference
1, Much more small cells per cluster and more clusters
2, Smaller cell radius and smaller cell ISD
Compared to the typical density assumed in 3GPP, e.g., ~8 LPNs per macro cell, 60 LPNs per cell would lead to 7~8 dB degradation in median SINR in non-co-channel case

## Slide 9: key challenges
pico
MACRO
pico
MACRO
Dual Connectivity: (R12/R13):
Signaling overhead;
Per-user throughput
Small cell in RAN1: (R12/R13)
Interference avoidance and coordination among small cells
Small cell discovery
HO performance e.g. interruption time
1, interference cancellation and coordination
2, user throughput at small cell edge
3,mobility performance enhancement on user plane
CA:(R10): user throughput
CoMP: (R11): user throughput
Hetnet mobility: (R11)
intra-f: HO mobility performance
Inter-f: cell detection and power consumption

## Slide 10: Potential mobility issue- split bearer
TCP Thp
Uu Thp

## Slide 11: Further analysis (1/3)
Figure 10.1.2.8.4-1: Change of SeNB (36.300 c50)

## Slide 12: Further analysis (2/3)
Temporary congestion due to following extra delay:
1, data forwarding over X2 from source SeNB to target eNB
2, extra queue delay due to shrink of throughput
3, massive forwarded PDCP PDU need go through MeNB pipe which is quite small compared to SeNB pipe due to sharing among all the UEs in the macro cell
Msg4/5
Msg7
Msg9
X2 delay=e.g. 60ms [1]
MeNB Throughput
SeNB throughput
[1] R2-144103 NSN,Nokia

## Slide 13: Further analysis (3/3)
Compared to split bearer, the situation for SCG bearer or normal MCG bearer (w/o DC) is worse due to following reason:
1, even no MeNB pipe during interruption time i.e. UP will be stopped
2, much more flushed buffer including PDCP PDU and RLC buffer
Msg4/5
Msg7
Msg9
X2 delay=e.g. 60ms [1]
MeNB Throughput
SeNB throughput
[1] R2-144103 NSN,Nokia

## Slide 14: Simulation scenario

## Slide 15: Simulation outcome with X2 delay=5ms

## Slide 16: Simulation result of smooth mobility

## Slide 17: Potential solution – make before break
MeNB
SeNB1
SeNB2
MeNB
SeNB1
SeNB2
MeNB
SeNB1
SeNB2
Note: it is just one example!

## Slide 18: ANNEX: simulation assumption
Environment Parameter | Value
Cellular Layout | Hexagonal grid, 7 cell sites
Inter-site distance | 500m，18m
CF for Pico | 2.6GHz
CF for Macro | 1.8GHz
System bandwidth | 20MHz
Traffic Model | FullBuffer
Macro Antenna Height | 35m
Pico Antenna Height | 10m
BS Antenna Num | 2
UE Antenna Num | 2
Pico Transmit Power | 23 dBm
Macro Transmit Power | 46 dBm
Macro antenna gain + Cable Loss | 14 dBi
BS noise figure | 5dB
UE noise figure | 9dB
Macro PathLoss model | ITU Uma
Pico PathLoss model | ITU Umi
UE Speed | 3km/h
Macro Antenna pattern (horizontal) | = 70 degrees, Am = 25 dB
Macro Antenna pattern (vertical) | = 10, SLAv = 20 dB
Macor BS antenna downtilt | 12 degree
Pico Antenna pattern | 5dBi Omni
User Plane Parameter | Value
Pico UE average RB/subframe | 20
Macro UE average RB/subframe | 5
TCP MTU(bit) | 1500*8
PDCP buffer size for UE | MTU * 200
Initial Congestion Window Size | MTU * 1
Initial Slow Start Threshold | MTU * 32
PDN Static Delay | 10ms
PDCP discard Timer | 500ms

## Slide 19: Thank you