## Slide 1: Narrowband Cellular-IoT (NB-CIoT): The clean-slate technology for the Internet of Things
3GPP TSG RAN Meeting #69
Phoenix, USA, 14 -16 September 2015
Document for: Discussion
Agenda Item: 14.1.1
RP-151358

## Slide 2: CONTENTS
CIoT Standard status
Comparison between NB-CIoT and NB-LTE
View on way forward in RAN#69

## Slide 3: PCG decision
The PCG#34 April 2015 approved document PCG34_39r2 on the way forward on handling the GERAN Cellular IoT activities for both the Clean Slate track and the GSM Evolution track. The PCG decided that
  For the Clean Slate Track
    At TSG RAN#68, GERAN will present the latest status of the Clean Slate track of activities. (DONE)
    TSG GERAN#67 aims to conclude the FS_IoT_LC SI as planned in August, 2015, with conclusions/recommendations for the Clean Slate candidate proposals. (DONE)
    At TSG RAN#69
      TSG GERAN is invited to present the conclusion of the Clean Slate track of activities. (SEE NEXT SLIDE)
      One Clean Slate WI can be proposed for approval (this overrides the previous guidance from RAN that no new items will be approved in RAN#69 except for existing SIs moved to WIs and spectrum related items).
      Such a WI proposal will not be subject to the regular RAN prioritization, it will be done in parallel to the existing RAN WG work/capacity (no TU’s discussion; no schedule constraints due to the existing work).
      TSG RAN should strive to complete the work (if necessary adding AH meetings to keep the work schedule) within R13 as per prior understanding.
      GERAN ToR needs no modification.
  For the GSM Evolution Track
    GERAN may approve a GERAN Evolution candidate proposal for normative work. GERAN will have ownership of this work (DONE; GERAN#67 approved a work item on EC-GSM evolution)

## Slide 4: 3GPP Standard Progress
NB-M2M
NB-OFDM
NB-CIoT
EC-GSM
eMTC
MTC
May.2014
Aug.2015
Sep.2015
Mar.2016
WI Completed
WI Approved
Dec.2015
WI Completion
SI Start
(Clean-slate track)
Proposals
Convergence
SI Start
(GSM track)
WI Approved
WI Completion
WI Completion
R12
R13
WI Approval
(Move to RAN)
R13
R13
NB-LTE
?
We are here
First outline concept
SI Closed
Notes: NB CIoT: Narrow Band Cellular IoT
EC GSM: Extended Coverage GSM
eMTC: Enhancements for Machine Type Communication
2015年5月在GERAN#62 NB CIoT立项（SI Kickoff）
2015年7月在3GPP TSG GERAN#67 Conclusion
EC-GSM concluded and shown compliance to all objectives.
NB-CIoT concluded and shown compliance to all objectives.
NB-LTE, NB-M2M, NB-OFDMA, N-GSM, C-UNB are partially described.
Release 12定义了MTC(Machine type communication),但是在覆盖能力、终端成本等方面不能很好的满足LPWA市场的诉求，所以在3GPP R13各家厂商提出了一些候选的技术.
eMTC是其中之一，预计eMTC标准将在今年年底冻结，然后eMTC仍然面临着成本较高，覆盖能力不够、终端功耗较大等问题，不能帮助运营商建立一张无处不在的蜂窝物联网网络。
华为在2014年提出了NB M2M的技术，高通提出了NB OFDM技术，E///提出了EC GSM技术，前两者为clean slate技术，可以与当前网络共存，利用当前网络设备。EC GSM为GSM技术的增强，需要对存量GSM网络升级。这三个技术都是在GERAN的标准中定义。今年5月，华为和高通的方案进行了融合，新的标准名称叫做NB CIoT，将在今年9月在RAN进行work item立项，计划在2016年3月冻结标准。

## Slide 5: Conclusion of GERAN study
Objective | Completed techniques |  | Partially described techniques |  |  |  | 
 | EC-GSM | NB-CIoT | NB-LTE | NB-M2M | NB-OFDMA | N-GSM | C-UNB
Improved indoor coverage (20dB) | Compliant | Compliant | Expected to be fulfilled | Compliant | Compliant | Expected to be fulfilled | Not compliant
Support of massive number of low throughput devices (52547 devices per cell by mixed traffic models) | Compliant | Compliant | Inconclusive/FFS | Compliant | Expected to be fulfilled | Inconclusive/FFS | Not compliant
Reduced device complexity (much lower cost than GPRS chipset) | Compliant | Compliant | Inconclusive/FFS | Expected to be fulfilled | Expected to be fulfilled | Expected to be fulfilled | Not compliant
Improved power efficiency (10 years battery life) | Compliant | Compliant | Inconclusive/FFS | Compliant | Compliant | Inconclusive/FFS | Not compliant
Latency (exceptional report within 10 seconds) | Compliant | Compliant | Expected to be fulfilled | Compliant | Compliant | Compliant | Not compliant
Co-existence with GSM/UMTS/LTE | Compliant | Compliant | Inconclusive/FFS | Expected to be fulfilled | Expected to be fulfilled | Expected to be fulfilled | Not compliant
Impact on GSM/EDGE BTS hardware | Compliant | Compliant | Inconclusive/FFS | Expected to be fulfilled | Expected to be fulfilled | Compliant | Not compliant
Key conclusions (in GP-151022) are:
  NB-CIoT is the only completed clean-slate technique, and was shown to be compliant with all performance and compatibility objectives
  EC-GSM is also a completed technique, and was shown to be compliant with all performance and compatibility objectives
    But assumes 2.4 MHz system bandwidth, has much less capacity in reports/hour/200kHz, requires 10 dB more UE transmit power for the same coverage, and does not offer a good solution after GSM re-farming
  NB-LTE, NB-M2M, NB-OFDMA, N-GSM, C-UNB are partially described techniques
Notes: NB-LTE works at a very high sampling rate of 128*15kHz = 1.92MHz!

## Slide 6: CONTENTS
CIoT Standard status
Comparison between NB-CIoT and NB-LTE
View on way forward in RAN#69

## Slide 7: Key messages on NB-LTE
NB-LTE was a last-minute proposal submitted to GERAN, based on LTE
  The underlying concept for NB-LTE is to re-use LTE as much as possible. Therefore, the concept description is adopted into TR 45.820 as a separate chapter 7A, which is a different section than Sec 7 clean slate solution.
  However, due to some key differences between Cellular IoT and eMTC/LTE, it is actually very difficult to re-use many aspects of the eMTC and LTE design – so a large amount of standardization effort is still required.
NB-LTE proposal is incomplete and only evaluated to a very limited degree in GERAN.
  Proper evaluation to same level of maturity as other proposals in GERAN would need ~9 additional months of study, and even more for an in-band deployment option.
  TR 45.820 captured many areas for FFS. It has not been proven that NB-LTE can meet any of the Study Item objectives (see the Conclusions of the SI). No coexistence analysis for any scenarios was provided.
Operation using in-band LTE spectrum is very challenging, unproven, and unlikely to meet the performance objectives defined in Cellular IoT study
  NB-LTE in-band deployment was claimed in GERAN but the proponents did not provide the detailed design and there were no in-band performance evaluations or any coexistence analysis.
  Huawei submitted a paper in GP-150871 containing detail analysis explaining the challenges of in-band deployment for NB-LTE design (such as limited PSD boosting, non-orthogonality of uplink, etc.) and the drawbacks in terms of performance. No answers to these key questions were provided.

## Slide 8: Overview of NB-CIoT and NB-LTE
 | Downlink |  | Uplink | 
 | NB-LTE | NB-CIoT | NB-LTE | NB-CIoT
Multiple access | OFDMA | OFDMA | SC-FDMA | FDMA
Frame structure | M-frame 60ms M-subframe 6ms | Frame 1.28s Subframe 160ms |  | 
Sub-carrier spacing | 15 kHz | 3.75 kHz | 2.5 kHz | 5 kHz
Number of sub-channels | 12 | 48 | 72 | 36
Maximum transmit power | 43 dBm | 43 dBm (1/1 reuse) 38 dBm (1/3 reuse) | 23 dBm | 23 dBm
Modulation mandatory | BPSK, QPSK | BPSK, QPSK | BPSK, QPSK | GMSK
Modulation optional | 16QAM | 16QAM | 16QAM | BPSK, QPSK, 8PSK
FFT size | 128 | 64 | 128 | -
Sampling rate | 1.92MHz | 240kHz | 320kHz | 240kHz
Cyclic prefix | 9/10 samples (4.7/5.2us) | 6 samples (25us) | 9/10 samples (28.125/31.25us) | None
FEC | CC | CC | Turbo | Turbo
PAPR (dB) | 7.8 | 7.9 | 5.7 dB | 0 dB
DC overhead | 8.3% | 2% | - | -
NB-LTE has higher sampling rate, more overhead, and cannot support large cell sizes
Notes: NB-LTE works at a very high sampling rate of 128*15kHz = 1.92MHz!

## Slide 9: Performance comparison between NB-LTE vs NB-CIoT
 | NB-CIoT | NB-LTE
Coverage enhancement | 20dB | 20dB (for stand-alone deployment)
Battery life | >10 years | Not shown, probably ~10 years
Re-farm GSM | Yes | Not shown, but problem with Tx mask
LTE in-band (in PRBs) | Not shown | Not shown
LTE guard-band deployment | Yes, shown in trial | Likely
Capacity | >50k devices/sector | Not shown
Data rate | DL: 0.45 to 360 kbps UL: 0.3 to 48 kbps | DL: 0.3 to 128 kbps UL: 0.22 to 64 kbps
Frequency re-use | Flexible: Re-use factor 1/3 or 1 within 200 kHz | Relies on re-use factor 1 within 200 kHz but inter-cell interference not modelled
Scalability | Yes | Yes
Maturity of solution | Good, concept description and evaluation completed in study item | Last-minute proposal: much of the detailed design and most of the evaluation is missing
Standardization effort | Medium | Immature solution
Base station baseband complexity | Low | Medium
Re-use of RRU | LTE only RRU, MSR RRU, GSM MCBTS RRU | LTE only RRU, MSR RRU, cannot re-use GSM MCBTS RRU
Future proof | Yes | Yes
Notes: NB-LTE works at a very high sampling rate of 128*15kHz = 1.92MHz!

## Slide 10: Device Complexity – Why is NB-CIoT cheaper?
 | NB-CIoT | NB-LTE
Complexity Analysis of synchronisation (key driver of complexity for chipset baseband) |  | 
PSS+SSS operations | 45 Mops/sec | > 585 Mops/sec
Buffer memory | 28 kbytes | > 63 kbytes
Implementation Cost Analysis |  | 
Single-die SoC | Yes, using ~512 kbyte embedded flash | No, due to need of external memory (many Mbytes LP-DDR due to large LTE L1/L2/L3 stack)
Software-defined Modem | Yes, low cost DSP is enough | No, the sampling rate is high, so higher processing power is needed especially for PSS/SSS synchronization.
Low-cost CPU | Yes, ARM M0 is enough | TBD, the protocol is more complex and has tighter turn-around times which define peak CPU loading.
Battery | Low instantaneous current draw allows wide range of battery technologies | Higher cost, due to higher PAPR of SC-OFDMA which requires higher instantaneous current draw
On-chip PA | Yes, due to high efficiency PA since modulation is zero or low PAPR | No, SC-OFDMA may have 5dB PAPR; PA efficiency is 35% lower than GMSK.
Low cost radio architecture | Yes, direct conversion receiver and low bandwidth polar modulator transmitter | No, direct conversion receiver is not possible if all DL subcarriers are used; modulation is discontinuous phase and higher PAPR, so requires Cartesian transmit
Overall Cost of Solution | Lower than GSM (about 50% complexity reduction for SoC) | Marginally lower than eMTC, but higher than GSM and much higher than NB-CIoT
Notes: NB-LTE works at a very high sampling rate of 128*15kHz = 1.92MHz!

## Slide 11: Integrated in LTE network –NB-CIoT is feasible
  NB-CIoT can be integrated in LTE network because:
  Common core network based on S1 interface
      Common S1-based protocol structure and
      Common OAM and OSS with NB-CIoT as a specific carrier in LTE system
  Common BBU
      Reuse LTE L2/L3 functions and procedures
      The required computational complexity for NB-CIoT is tiny compared to that for LTE, software upgrade is feasible
  Can be integrated in LTE band with common RRU
      NB-CIOT can be deployed in the LTE guard band
      The worst case equivalent downlink PAPR of NB-CIoT is only 7.33 dB which is remarkably lower than the PAPR tolerance of a typical LTE BS

## Slide 12: NB-LTE design cannot support in-band deployment with 20dB coverage enhancement and massive number of devices per cell
  Limitation in downlink transmit power
    Maximum PSD boosting of about 4 dB is realistic when deployed in-band.
    The resulting MCL is 13 dB and 16 dB lower than that for stand-alone deployment with LTE bandwidth of 10 MHz and 20 MHz, respectively.
    Even if more repetitions are used, the resulting data rates will be too low to be useful (<<100 bps).
    PSCH may fail to work at the extremely low SNR of -17.6 dB and -20.6 dB (NB-LTE stand-alone is designed to operate at SNR = -4.6dB).
  Collision with LTE channels/signals (~30% loss to avoid collision)
    NB-LTE PSS/SSS collides with LTE PDCCH/CRS/CSI-RS
    NB-LTE PDCCH/EPDCCH collides with LTE PDCCH/CSI-RS
    NB-LTE PBCH collides with LTE CSI-RS
    eMBMS is difficult to support by LTE when NB-LTE is
    deployed in-band (since PMCH is a wideband transmission at L1)
  Uplink interference from LTE subcarriers
    Orthogonality is not maintained between uplink LTE subcarriers and NB-LTE subcarriers. The 10 kHz guard band introduced by NB-LTE is insufficient to counter the side-lobe leakage of the LTE sub-carriers.

## Slide 13: References to GERAN key documents
  GP-150869: Comparison of Downlink PAPR between NB-CIoT and NB-LTE
  GP-150870: Comparison of Base Station Complexity between NB-CIoT and NB-LTE
  GP-150871: On In-band Deployment of NB-LTE
  GP-150872: On M-PDCCH/M-EPDCCH Design in NB-LTE
  GP-150875: Analysis on the re-use of L2/L3 of LTE for NB-CIoT

## Slide 14: CONTENTS
CIoT Standard status
Comparison between NB-CIoT and NB-LTE
View on way forward in RAN#69

## Slide 15: Overall Summary
The PCG in April 2015 have decided that upon the completion of the Ultra Low Complexity and Low Throughput Internet of Things (CIoT) GERAN study item:
  To continue the GSM Evolution track normative work under GERAN
  To move the Clean Slate (NB-CIoT) track normative work under TSG RAN
GERAN#67 August 2015 completed the CIoT study item
  GERAN has already approved the GSM Evolution Track work item
  NB-CIoT Clean Slate solution is fully evaluated and compliant with SI objectives. NB-CIoT work is proposed for approval, as per the PCG directive.
Last minute proposal on NB-LTE was submitted to GERAN#67 in the closing meeting of a 15 month study item
  NB-LTE proposal was not properly evaluated and is incomplete. It should not be considered now.
CIoT is very important feature for operators. Time to market in Rel13 is key for market success and to ensure early entry into some of the vertical markets.

## Slide 16: Way forward
WID discussion
  NB-CIoT WID should be approved as the only Rel-13 clean slate, compliant, and complete solution.
  NB-LTE proposal is an incomplete 3rd track study and not clean slate. It should not be considered now.
Meeting scheduling for NB-CIoT
  Parallel session required for RAN1/RAN2/RAN4
  For each session in regular meetings: at least 2 days (better 3 days) are allocated to NB-CIoT
  2 ad-hoc meetings are considered for RAN1/RAN2/RAN4 for 5 days
    14 – 18 December 2015
    11 – 15 January 2016
  1 ad-hoc meeting is considered for RAN3
    11 – 15 January 2016
Notes: NB-LTE works at a very high sampling rate of 128*15kHz = 1.92MHz!

## Slide 17: Thank you