## Slide 1: Way forward on CIoT WID
Vodafone, Telecom Italia, Telus, China Mobile, China Unicom, Huawei,
RP-151604

## Slide 2: Motivations for this compromise way forward
Follow PCG decision for a single Clean Slate solution based on the outcome of the GERAN SI.
Address some operators’ interests to have CIoT solution deployable in-band LTE.
Follow strong request from some operators for a unified solution.
Maintain design principles of the outcome of the compliant solution from the GERAN study item
Address time urgent LPWA market requirement

## Slide 3: High level principle
The new CIoT design will allow the following scenarios:
  “Stand-alone operation’ utilizing for example the bands currently being used by GERAN systems as a replacement of one or more GSM carriers
  ‘Guard band operation’ within a normal LTE carrier’s guard band
  ‘In-band operation’ utilizing resource blocks within a normal LTE carrier’s transmission bandwidth
At least for the stand-alone operation and guard band operation, the new radio access technology should guarantee the performance requirements defined in TR45.820

## Slide 4: Design principle
Common synchronization design for all the three scenarios, with support for up to 20 kHz frequency offset.
DL design based on OFDMA :
    a) 3.75 kHz sub-carrier spacing optimised for stand-alone and guard band operation.
    b) 15 kHz sub-carrier spacing for in-band operation
  Evaluate the performance of b) for the purpose of down selection until November to use one numerology if feasible for all scenarios
Common uplink design for all the scenarios
  Usage of FDMA in the uplink with 3.75 kHz symbol rate.
  Support of GMSK modulation on the uplink for high-efficiency of power amplifier.

## Slide 5: Timeline
The work item is for Rel13
  Independent of regular Rel13 completion
A new set of specifications for CIoT