## Slide 1: Commonality design between eMTC and NB-IOT
Panasonic
3GPP RAN workshop on 5G
Phoenix, AZ, USA, 17-18 September, 2015
RP-151614

## Slide 2: Possible commonality between eMTC and NB-IOT
 | Synch channels | System information except PBCH* | DL control channels (M-PDCCH) | DL traffic (PDSCH) | UL traffic (PUSCH) | PRACH
eMTC up to Rel8 coverage (No/small repetition) | Rel.8 PSS/SSS |  | Simple enhancement from Rel.12 | Simple enhancement from Rel.12 | Simple enhancement from Rel.12 | Simple extension of Rel.8 design
eMTC 15 dB coverage (large repetition) | Rel.8 PSS/SSS but to use NB-IOT design may be good design. |  |  |  |  | Rel.8 PSS/SSS but to use NB-IOT design may be better.
1 PRB in-band design NB-IOT |  |  |  |  |  | 
1 PRB standalone design NB-IOT |  |  |  |  |  | 
Common design including numerologies
Common design
except
1 PRB or 6 PRB
15 kHz subcarrier
- * FFS: PBCH
- 3.75 kHz subcarrier for the standalone is mainly determined by the strict spectrum mask requirement.
Common design
except
3.75 kHz subcarrier
Common design
except
1 PRB or 6 PRB
15 kHz subcarrier
Common design
except
3.75 kHz subcarrier
Common design
except
1 PRB or 6 PRB
15 kHz subcarrier
Common design
except
3.75 kHz subcarrier
Common design except
maximum
bandwidth
and
modulation
GMSK &
FDMA
or
SC-FDMA
SC-FDMA
Common design including numerologies

## Slide 3: Proposal
On the areas not concluded in eMTC, to have the commonality between eMTC (especially in large repetition case) and CIOT should not be precluded.