## Slide 1: Motivation for Further Enhanced Machine-Type Communications in Rel-14
Ericsson
RP-151974
3GPP TSG RAN Meeting #70
Sitges, Spain, 7th – 10th December, 2015
Agenda item 14.1.1

## Slide 2: Justification
Rel-13 introduces two classes of low-cost MTC devices with enhanced coverage and low power consumption:
  eMTC devices with a UE bandwidth of 6 PRBs (1.08 MHz)
  NB-IOT devices with a UE bandwidth of 1 PRB (180 kHz)
It is important to ensure that large amounts of MTC devices and MTC traffic can be handled efficiently in the networks.
It is desired to ensure that useful higher-layer improvements introduced for NB-IOT devices can be exploited also for eMTC devices, and vice versa.
It is in many cases more efficient to use multicast transmission instead of unicast transmission, e.g. for rollout of firmware or software upgrades.
As positioning is important in many MTC applications, some improvements of the positioning accuracy may also be motivated.

## Slide 3: Objective
Physical layer improvements for eMTC devices, e.g.
  Sync signal repetition for quicker sync acquisition and reduced power consumption
  Uplink lower order modulation for improved PA efficiency and enhanced coverage
  Starting OFDM symbol 0 for improved downlink capacity and throughput
  Smaller uplink resource allocation than 1 PRB for improved uplink capacity
  Improved uplink user throughput, e.g. using a longer TTI for PUSCH
  Reduced soft buffer size for reduced device cost
Higher layer improvements for eMTC devices [and NB-IOT devices?]
  Congestion and overload control in connected mode
Low complexity multicast functionality for eMTC devices [and NB-IOT devices?]
  E.g. MBMS transmission based on MBSFN or SC-PtM
Improved positioning accuracy for [eMTC devices and/or NB-IOT devices?]
  May or may not be needed depending on what accuracy can be achieved in Rel-13