## Slide 1: Generic filtered uph measurements for umts
RP-152000 - Motivation for New proposed WI

## Slide 2: Background
In Rel-12, a filtered UE power headroom (UPH) measurement has been specified as part of the "Further EUL enhancements". It was designed specifically for use with the Enhanced E-DCH TTI switch feature. The measurement has been found to have a much wider application and is especially suitable for triggering compressed mode measurements.
Compressed mode start is currently triggered using Event 6d (UE TX power reached maximum). The triggering of 6d is dependent on UL data activity and is rather difficult to tune:
  With E-DCH on the UL, the maximum power can be reached quite easily when there are enough data to send. As a result, if not tuned properly, the event may be triggered without any coverage problem, and can lead to frequent false compressed mode triggering. The time-to-trigger parameter may be used to limit the amount of false triggering, but it delays the process and is dependent on the details of the E-TFC selection scheme in the UE.
  On the other hand when there is a temporary inactivity on the UL, event 6d is not triggered while the UE is going out of coverage since the physical control channels (DPCCH and HS-DPCCH) are not using very much power. By the time a 6d event is triggered, the DPCCH and HS-DPCCH by themselves have used up all the power and it is obvious that there will not be sufficient power to send the event itself.

## Slide 3: Proposed RAN Work Item
The UPH is a measure of the maximum UE power relative to the power used by the DPCCH.
It is not affected by the presence of data, and it can be triggered correctly even without any ongoing data transmission.
Thus, it is a good coverage indication and ideal for triggering compressed mode start.
Therefore, this work item aims at standardizing a generic version of the filtered UPH measurements.

## Slide 4: Proposed RAN Work Item
The objectives of this WI are the following ones:
  Include a measurement ID in the configuration of the measurement to simplify the handling on the network side.
  Define two general triggers, one for crossing the configured threshold from above and one for crossing from below.
Considerations should be given to whether it is more suitable to define two new RRC events or to modify the current mechanism as it is specified in the MAC specification. The considerations should be based on conceptual simplicity, extensibility, and implementation impacts on the network and UE.

## Slide 5: benefits
The usage of the filtered UPH measurements can be made generic aiming at using it for other purposes such as triggering compressed mode.
They provide a robust coverage indication even in absence of data activity which make it ideal for triggering compressed mode start.
The extended usage of the filtered UPH measurements will allow performing both a faster and more accurate triggering mechanism.