## Slide 1: Scope of 5G Study Item on RAN architecture
Telecom Italia, Orange, Telefonica, China Mobile Communications Corporation, Deutsche Telekom
3GPP TSG RAN Meeting #70
Sitges, Spain, December 7 - 10, 2015
RP-152211

## Slide 2: Background
The evolution of the RAN architecture is one of the key aspects to cope with evolution towards 5G
The availability of new technology enablers such as NFV gives 3GPP the opportunity to design a flexible RAN architecture, addressing
  Performance requirements for radio interfaces
  Different service and deployment scenarios
  Efficient support for network and service management with CAPEX/OPEX reduction and agile service delivery
5G family of radio interfaces is constituted by LTE evolutions and new RAT
Tight interworking between the new radio interface and LTE evolution was expressed by major operators, during the 5G RAN workshop, as a top priority requirement, including possibility for Carrier aggregation and/or dual connectivity between LTE and new RATs
In order to increase the benefits of New Rats and LTE evolutions tight radio interworking, it is important that both systems architectures evolve in a homogeneous way

## Slide 3: Proposed scope for 5G Study Item
A Study on RAN architecture evolution should be started in parallel to the feasibility study of a new radio interface
Proposals for RAN SID are being elaborated. The objectives of the study shall include:
  Assessment of RAN architectural options applicable to LTE and new radio interfaces
  Identification of technical requirements for Virtual RAN architectural options
Overall architecture design to be considered in a holistic manner
Core Network

## Slide 4: Annex
RRC
PDCP
RLC
MAC
PHY
Traditional BS
RLC
MAC
PHY
MAC
PHY
PHY
RF
RF
RF
RF
RF
Cloud RAN Protocol layer options
Remote Radio Head Protocol layer options
Examples of functional split options applicable for 5G RATs (LTE and new radio interfaces)
RRC
PDCP
RRC
PDCP
RLC
RRC
PDCP
RLC
MAC
RRC
PDCP
RLC
MAC
PHY
Fronthaul
Interface