## Slide 1
3GPP TSG RAN Meeting #71
Gothenburg, Sweden, 7 - 10 March 2016
Agenda Item: 10.1.1
Document for: Discussion
RP-160262
Motivation on New WI Proposal for MUST
MediaTek Inc.

## Slide 2: Overview of MUST Study
The 3GPP study item on MUST was approved at RAN#66 in December 2014
The results and findings of the study are documented in the Technical Report 36.859 v.1.0.1 submitted to RAN#70
It has been identified that MUST can increase system capacity as well as improve user experience in certain scenarios at least for 2Tx case

## Slide 3: Candidate Multiuser Superposition Transmission Schemes (1/2)
Categories | Power ratio | Gray mapping | Label-bit assignment
MUST Category 1 | adaptive, on component constellations | N | on component constellations
MUST Category 2 | adaptive, on component constellations | Y | on the composite constellation
MUST Category 3 | N/A | Y | on the composite constellation

## Slide 4: Candidate Multiuser Superposition Transmission Schemes (2/2)
MUST Category | Block Diagram
MUST Category 1 | 
MUST Category 2 | 
MUST Category 3 | 

## Slide 5: Potential Receiver Schemes
MUST-far UEs
  MMSE-IRC receiver can achieve similar link-level performance as R-ML/ML receiver in most of MUST pairing cases, assuming Release 12 EVM requirements for 64QAM
  MUST-far UEs can be legacy UEs when QPSK is applied to MUST-far UEs
MUST-near UEs
  R-ML/ML receiver can achieve similar link-level performance as CWIC receiver in most of MUST pairing cases, assuming Release 12 EVM requirements for 64QAM

## Slide 6: Potential MUST Assistance Information
Assistance information required for UE receivers to cancel inter-superposition-layer interference
  Details depending on MUST categories and receiver types
  Full information can be found in TR 36.859
Methods for obtaining assistance information
  Blind detection
  Dynamic or higher layer signalling
  Tied to UE’s scheduling information
  Tied to specific UE assumptions

## Slide 7: SLS Results for PDSCH
  The UPT gain captured in TR 36.859 can be summarized as follows:
Chart: FTP1 traffic, wideband scheduling CWIC
| 7.23
source1-cat1-RU60 | 14.88
source6-cat1-RU60 | 5.6
source8-cat1-RU60 | 3 | -5 | -7 | -13 | 5.94
source10-cat1-RU60 | 5.94
source11-cat1-RU60 | 16.5 | 17.85
source4-cat2-RU60 | 14.69 | 14.24
source6-cat2-RU60 | 6.3 | 12.7
source11-cat2-RU60 | 16.5 | 17.85
source8-cat3-RU60 | -3 | -2
source1-cat1-RU80/90 | 30.65
source4-cat1-RU80/90 | 23.68 | 25.37
source6-cat1-RU80/90 | 8.5
Chart: FTP1 traffic, subband scheduling CWIC
| 8.2399999999999984 | 11.09
source3-cat3-RU80/90 | 2.96 | 3.77
source1-cat1-RU60 | -0.29
source7-cat1-RU60 | 5.2 | 9.5
source12-cat1-RU60 | 1.5
source11-cat1-RU60 | 8.77 | 8.95
source3-cat2-RU60 | 4.94
source4-cat2-RU60 | 3.89 | 3.16
source3-cat3-RU60 | 2.16
source1-cat1-RU80/90 | 16.38 | 16.24
source4-cat1-RU80/90 | 14.41 | 16.85
source7-cat1-RU80/90 | 11 | 11 | 11.1
source10-cat1-RU80/90 | 0.97 | 30.39

## Slide 8: SLS Results for PDSCH (cont.)
Chart: FTP1 traffic, wideband scheduling, R-ML/SLIC
| -3 | -9
source8-cat1-RU60 | -5 | -13
source11-cat1-RU60 | 16.5
source4-cat2-RU60 | 14.24
source6-cat2-RU60 | 6.3 | 12.7
source11-cat2-RU60 | 16.5
source8-cat3-RU60 | -2
source6-cat1-RU80/90 | 8.5
source11-cat1-RU80/90 | 22.7 | 23.96
source4-cat2-RU80/90 | 23.49 | 24.63
source6-cat2-RU80/90 | 4.4 | 7.3
Chart: FTP1 traffic, subband scheduling, R-ML/SLIC
| 0.2
source7-cat1-RU60 | 5.2
source11-cat1-RU60 | 8.77
source3-cat2-RU60 | 4.94
source4-cat2-RU60 | 3.16
source3-cat3-RU60 | 2.16
source7-cat1-RU80/90 | 11 | 11.1
source11-cat1-RU80/90 | 14.15
source3-cat2-RU80/90 | 10.59 | 13.61
source4-cat2-RU80/90 | 13.77 | 16.65
source3-cat3-RU80/90 | 2.96 | 3.77
  The UPT gain captured in TR36.859 can be summarized as follows:

## Slide 9: SLS Results for PDSCH (cont.)
Serving/Offered traffic ratio versus resource utilization rate for wideband scheduling
  Macrocell-only deployment is assumed
Chart: 
| 60 | 80.599999999999994 | 83 | 59 | 80 | 82
HW-6430 | 99 | 99 | 98.5 | 99 | 99 | 98.7
Ericsson-7212 | 100 | 100 | 98 | 98 | 100 | 100
MTK-7191 | 99.7 | 99.24
Nokia Net-7541 | 99.3 | 99.4 | 99.32 | 97.9 | 98.23 | 98.27
LGE-7456 | 95.8 | 95.2 | 90.3
ZTE-6630 | 98.7 | 93.82
CATT-6599 | 98.37 | 97.94
ALU-6719 | 98.76 | 98.75 | 98.54 | 98.53
RU
Serving/Offered Ratio

## Slide 10: SLS Results for PDSCH (cont.)
Chart: 
| 61 | 78 | 87 | 60 | 77 | 86.2
HW-6430 | 99 | 99 | 99 | 99 | 99 | 99
MTK-7191 | 99.8 | 99.3 | 99.2
DCM-7352 | 99.8 | 99.78 | 99.2 | 98.55 | 99.05 | 98.17
Intel-6531 | 92.4 | 91.9 | 90.9
LGE-7454 | 96.9 | 94.4
ZTE-6630 | 99.04 | 93.97
CATT-6599 | 98.06 | 97.69
ALU-6719 | 98.72 | 98.72 | 98.55 | 98.56 | 98.62 | 98.6
Serving/Offered traffic ratio versus resource utilization rate for subband scheduling
  Macrocell-only deployment is assumed
RU
Serving/Offered Ratio

## Slide 11: SLS Results for PMCH
No conclusion in TR 36.859
Initial evaluation results of MUST for PMCH can be found in R1-156432, R1-157457, R1-155699 and R1-157610

## Slide 12: Conclusions of the Study
MUST can increase system capacity as well as improve user experience in certain scenarios at least for 2Tx case
  MUST is generally more beneficial when the network experiences higher traffic load
  MUST is generally more beneficial in user perceived throughput for wideband scheduling case, compared to subband scheduling case
  MUST is generally more beneficial in user perceived throughput for cell-edge UEs, compared to other UEs
MUST-far UEs can be legacy UEs when QPSK is applied to MUST-far UEs or the most two significant bits in the modulation symbol are assigned to far UE

## Slide 13: Objective of WI
Specify necessary mechanisms to enable LTE up to 8 Tx downlink intra-cell multiuser superposition transmission for PDSCH
Network assistance information for up to two interfering data layers
The following cases are supported
  Case 1: The interfering PDSCH is transmitted using the same transmission scheme and the same spatial precoding vector(s) as the serving PDSCH
  Case 2: The interfering PDSCH is transmitted using the same transmit diversity scheme as the serving PDSCH
  Case 3: The interfering PDSCH is transmitted using the same transmission scheme and a different spatial precoding vector as the serving PDSCH
eNB
Near-user
Far-user
eNB
Far-user
Near-user
Beam 1
Beam 2

## Slide 14: References
Source of system performance in TR36.859 :
  Source 1 (MTK-R1-157191)
  Source 2 (DCM-R1-155931)
  Source 3 (DCM-R1-157352)
  Source 4 (Huawei-R1-157558)
  Source 5 (ZTE-R1-156630)
  Source 6 (Nokia-R1-157541)
  Source 7 (Intel-R1-156531)
  Source 8 (Ericsson-R1-157748)
  Source 9 (China Telecom-R1-154402)
  Source10 (LGE R1-157456)
  Source11 (ALU R1-156719)
  Source12 (CATT-R1-156599)