## Slide 1: Motivation for new WI: Enhancement of NB-IoT
Huawei, HiSilicon, Neul
RP-160297
3GPP TSG RAN Meeting #71
Göteborg, Sweden, 7th – 10th March, 2016
Agenda item 10.1.1

## Slide 2: Justification
Rel-13 introduces NB-IoT with 180kHz UE RF bandwidth which can be deployed in 3 scenarios
  In-band
  Guard-band
  Standalone
It is important to further enhance NB-IoT in R14
  Support positioning without increasing the device cost and power consumption
  Support of device software and firmware with multi-cast over the air
  Further enhance the flexibility and system efficiency when NB-IoT operates in multiple carriers
  Further reduce the power consumption for very small packet report such as smoke alarm sensor/emergency sensor use cases

## Slide 3: Objective
    NB-IoT positioning support
      Narrow band positioning based on dedicated scheduled UL reference signals for UTDOA [RAN1, RAN2]
    Support for multi-cast downlink transmission (e.g. firmware or software updates, group message delivery)
      Including necessary enhancements to Rel-13 SC-PTM [RAN2]
    Enhancements to multi-carrier NB-IoT operation
      Cross carrier dynamic scheduling for unicast transmissions [RAN1]
      SI transmissions on non-anchor carrier(s) [RAN1, RAN2]
      Multiple configured NB-IoT carriers for NB-PRACH transmission [RAN1]
    Mobility enhancements, e.g. use of measurements for handover [RAN2]
    Uplink enhancements to further reduce device power consumption
      Contention-based data transmission for small packets, using e,g. RACH-less access, grant-free access connectionless operation. [RAN1, RAN2]
    Support for extended cyclic prefix (in-band) [RAN1]
    RAN4 to specify related core requirements.

## Slide 4: NB-IoT+ narrow band positioning principle
IoT positioning is different from the MBB positioning
  Most of devices are stationary or nomadic, i.e. not continuously moving
  Narrower UE transmission and receive bandwidth
  Accuracy of 30 – 100m at 67%.
Design principle
  UTDOA is preferred
    It has small impact on device cost. OTDOA may increase the device complexity
    Some tracking applications are less sensitive to power consumption because 10 year’s battery life is not required for tracking applications such as animal tracking, people tracking
    No impact to the power consumption if the device is stationary and equipped with battery because positioning only occurs once or few times.
  Can be based on single tone hopping or dedicated reference signal
  UE can transmit longer time (around 1 second, similar as the uplink traffic transmission time in extreme coverage) to achieve better accuracy
  UE can transmit every OFDM symbol and every subcarrier for multi-tone devices if necessary
  Should support both singe-tone devices and multi-tone devices

## Slide 5: Multi-cast downlink transmission
Benefits
  Software/firmware update is an essential service for IoT in future, to allow deployed devices to receive patches and software upgrades without in-field device replacement.
  To improve the spectrum efficiency for software/firmware upgrade
Design principle
  Based on Rel-13 SC-PTM
  Could include uplink feedback
  The solution should balance the device cost and power consumption

## Slide 6: Contention based uplink design principle (1)
Benefits of contention based uplink design
  The targeted use cases include e.g. smoke/fire alarm, emergency alarm, typical message size of 10 bytes, and there are almost no uplink traffic reports (only in emergencies or occasional testing). The only report is status report which tells the sensor is operating well.
  Signaling is a more significant part of over-the-air transmissions for such rare transmission case, and therefore a larger proportion of the device power consumption
  But these emergency reports are very high priority when they do need to be sent
    Lower power consumption due to less signaling
    Shorter latency due to less signaling
Benefits: save Msg1, Msg2, Msg3, Msg4, leading to 15%~100% longer battery life

## Slide 7: Contention based uplink design principle (2)
Allocate some dedicated resources for contention based access
  Can be broadcast by system information
Uplink MCS can be based on downlink measurements
  Very coarse levels of uplink MCS are needed
Single-tone is preferred due to benefits in extreme coverage become more desirable
  Support both ST and MT will add additional blind decoding complexity of eNB
3.75kHz subcarrier spacing is preferred because less CP overhead due to its longer symbol time