## Slide 1: Motivation for WI proposal for L1/L2 eMTC and NB-IoT enhancements
Ericsson
RP-160877
3GPP TSG RAN Meeting #72
Busan, Korea, 13th – 16th June, 2016
Agenda item 10.1.1

## Slide 2: Positioning
Justification
  Rel-13 eMTC in principle supports LTE positioning methods but without guaranteed performance
  Rel-13 NB-IoT only supports positioning based on measurements made by the network
  As positioning is important in many MTC/IoT applications, some improvements of the supported positioning functionality and positioning accuracy are motivated.
Objective
  Specify missing RAN4 requirements are for existing positioning methods for eMTC
    OTDOA: RSTD measurement
    E-CID: RSRQ and UE Rx – Tx time difference measurements
  Specify positioning accuracy improvements for eMTC and NB-IOT
    DL signal based positioning: Define new PRS configurations to improve accuracy
    UL signal based positioning: Define new UL signal configuration to improve accuracy
    RAN1/4 requirements for the new DL and UL measurements
    RAN2/3 to specify corresponding RRC/LPP/LPPa signalling

## Slide 3: Multicast
  Justification
  When many devices need to receive the same information simultaneously, for example in case of rollout of firmware or software upgrades, it is in many cases more efficient to use multicast transmission instead of unicast transmission.
  Low complexity multicast functionality for eMTC devices and NB-IoT devices can be introduced either in the form of a narrowband format of the regular MBSFN transmission functionality or as a small extension of the recently introduced single-cell point-to-multipoint transmission (SC-PtM) functionality.
  The transmission format of SC-PtM is expected to be significantly more straightforward than MBSFN to adapt to eMTC and NB-IoT devices.
Objective
  Specify low complexity multicast functionality for eMTC and NB-IoT devices
  Base the multicast functionality on MBMS transmission over SC-PtM (not MBSFN)

## Slide 4: Congestion and overload control
  Justification
  Currently it is only possible to control RACH load of idle mode UEs. It would be beneficial to be able to control RACH load of connected mode UEs in case of congestion by extending access class barring mechanisms for connected mode as per SA1 requirements.
  TS 22.011 section 4.6: “The network shall be able to control the behavior of UEs in E-UTRAN in connected mode to prevent mobile originating signalling and/or data traffic, while the access barring mechanisms specified under Clause 4.3 are being applied to UEs in idle mode.”
  Barring/control of CP access for NB-IoT and eMTC. SA2 has a requirement to be able to control the load of control plane (CP) access in the eNB and MME but that corresponding mechanisms have not yet been introduced by RAN2. This is slightly related to SA2 plans to study QoS enhancements for CP access.
Objective
  Congestion and overload control in connected mode for eMTC and NB-IoT
  Barring/control of CP access for NB-IoT and eMTC

## Slide 5: Mobility and link adaptation
  Justification
  For eMTC, RAN4 requirements are missing for inter-frequency measurements in Rel-13.
  For NB-IoT, reporting and RAN4 requirements are missing for RSRP/RSRQ in Rel-13.
  These measurements would be useful for mobility support and/or link adaptation.
Objective
  Specify RAN4 requirements for inter-frequency measurements for eMTC.
  Specify reporting and RAN4 requirements for RSRP/RSRQ for NB-IoT.

## Slide 6: Higher data rates
  Justification
  In Rel-13 the requirements of complexity reduction, extended battery life, and coverage enhancements aimed at devices such as sensors, meters, smart readers, and similar.
  Other types of devices/use cases, such as wearable devices and health monitoring devices share similar requirements.
  However, these devices are not fully covered by the Rel-13 improvements because they require higher data rates, mobility and may support services that are more delay sensitive.
  It is important to address such use cases with higher data rate requirements and with mobility compared to those addressed by Rel-13 while maximally harvesting the power consumption and complexity reduction and link budget enhancements features enabled by using the existing Rel-13 solutions.
Objective
  Larger TBS, HARQ-ACK bundling, up to 10 DL HARQ processes and CE mode B with up to 6 UL PRBs for eMTC
    VoLTE enhancements for eMTC (work to be started after the on-going SI is concluded)
  16QAM and redundancy version support with larger TBS for NB-IoT

## Slide 7: Sub-PRB uplink resource allocation
  Justification
  The eMTC UEs in poor coverage currently must occupy at least 1 PRB thus it would be beneficial to support a sub-PRB transmission mechanism to improve capacity and secondarily increased PA efficiency.
Objective
  Specify smaller UL resource allocation than 1 PRB with reduced PAPR for eMTC.
  Reuse the sub-PRB mechanisms developed in Rel-13 NB-IoT as much as possible.